## Slide 1: Support of 1x/2x/4x OFDM Symbol in HE SU PPDU
Date: 2015-09-14
Authors:

## Slide 2: Background
In [1], an efficient padding method was proposed. In this submission, we explain the more details of the proposed method.
  By adjusting the duration of the last OFDM symbol, e.g., 1x, 2x, and 4x OFDM symbol, the padding inefficiency caused by increasing OFDM symbol duration can be reduced.
Furthermore, we analysis relationship between our proposed method and PHY padding and packet extension method that was proposed in [2].

## Slide 3: Proposed PSDU_LENGTH Calculation
Time
…
NCBPS
NCBPS
Data Payload
EOF Padding
PHY Padding
PSDU_LENGTH
APEP_LENGTH
Last OFDM Symbol
TOO MUCH!
Time
…
NCBPS
NCBPS,last
Data Payload
EOF
PSDU_LENGTH
APEP_LENGTH
Last OFDM Symbol
2x OFDM Symbol
4x OFDM Symbol
PSDU_LENGTH is approximately calculated to the nearest 1/4, 1/2, or 1 times NCBPS
Proposed Method
11ac PSDU_LENGTH calculation rules

## Slide 4: Proposed Frame Structure for HE SU PPDU
1x OFDM symbol duration
2x OFDM symbol duration
4x OFDM symbol duration
CP
CP
4x OFDM symbol (12.8us)
1x OFDM symbol
3.2us
TX
waveform
CP
CP
4x OFDM symbol (12.8us)
2x OFDM symbol
6.4us
TX
waveform
CP
CP
4x OFDM symbol (12.8us)
4x OFDM symbol
12.8us
TX
waveform
1x/2x OFDM symbol only applied to the last OFDM symbol.
…
…
…

## Slide 5: PSDU_LENGTH Calculation Process
Calculate the numbers of OFDM symbols and bits in the last symbol (NSYM,init, NDbit,last).
Determine the number of data subcarrier in the last symbol (NSD,1x, NSD,2x, NSD,4x) and NDPBS,last,init, NCBPS,last,init.
For LDPC cases, update NSYM, Navbits depending on the conditions of OFDM symbol extension.
Calculate the number of padding bits Npad.
Details and examples shown in Appendix

## Slide 6: Relationship with PHY Padding Proposal in [2]
PHY Padding proposal in [2] addressed a different aspect of the decoding process. Padding is used to give extra processing time at the receiver for high data rate transmissions. The padding is used for OFDM and OFDMA transmissions.
Our proposal, support of 1x/2x/4x OFDM symbol, targets small payload transmissions in OFDM transmissions. We reduce amount of EOF padding performed and transmit air-time.
However, both proposals change how PSDU_LENGTH is computed and differ in how data tones are mapped to the last OFDM symbol. Therefore, it has potential conflict even though they target very different scenarios and operation modes.
Note that the use of packet extension in [2] can still be applied to 1x/2x/4x OFDM symbol proposal.

## Slide 7: Use Cases for 1x/2x/4x OFDM Symbol and PHY Padding in [2]
The two proposal actually have distinct use cases.
  The PHY padding in [2] is useful when data rate is high and data bandwidth is large (in both OFDM and OFDMA transmissions).
  1x/2x/4x OFDM symbol support is useful when payload sizes is small in OFDM transmissions.
Small payload with high data-rate and large bandwidth case (overlap case)
  This seems to be a unlikely operating scenario, as allocating larger bandwidth to send small payload would be very wasteful. Furthermore, small payload will result in a single LDPC codeword which may not require any PHY padding.
Each solution can be applied to different TX/RXVECTOR configurations
Use Case | Small Payload | Large Payload
Low Rate or Small BW | 1x/2x/4x OFDM symbol | N/A
High Rate & Large BW | 1x/2x/4x OFDM symbol / PHY Padding in [2] | PHY Padding in [2]

## Slide 8: Conclusion
The details of a padding method are explained with 1x, 2x, 4x last OFDM symbol duration.
By exploiting the repeated waveform in 1x, 2x symbol duration cases, we can achieve throughput gain shown in [1].
Because the computation of PSDU_LENGTH and data tone mapping of the last OFDM symbol have potential conflict with the proposal in [2], careful merger is needed if both proposals are to be supported in 802.11ax.

## Slide 9: Appendix: encoding process

## Slide 10: PSDU_LENGTH Calculation Process
Definition of variables
Calculate NSYM,init.

## Slide 11: PSDU_LENGTH Calculation Process (cont.)
Calculate the number of data bits in the last OFDM symbol.
Define NSD,1x , NSD,2x , and NSD,4x (=NSD) depending on channel BW
  NSD is defined in 11ax . Use of above parameters result in re-use of agreed BCC interleaver parameters.
 | NSD,1x | NSD,2x | NSD,4x
20MHz | 48 | 102 | 234
40MHz | 102 | 234 | 458
80MHz | 240 | 480 | 980
160MHz | 480 | 980 | 980*2

## Slide 12: PSDU_LENGTH Calculation Process (cont.)
If 0 <NDbit,last mSTBC  NDBPS,1x, (1x OFDM symbol duration)
  NDBPS,last,init = NDBPS,1x (NCBPS,last,init = NCBPS,1x)
  BCC case: interleaver size = NSD,1x
  Data subcarrier with 4k (k=1,2…) indices excluding DC and pilot tones are used.
If mSTBC  NDBPS,1x <NDbit,last mSTBC  NDBPS,2x, (2x OFDM symbol duration)
  NDBPS,last,init = NDBPS,2x (NCBPS,last,init = NCBPS,2x)
  BCC case: interleaver size = NSD,2x
  Data subcarrier with 2k (k=1,2…) indices excluding DC and pilot tones are used.
If mSTBC  NDBPS,2x <NDbit,last mSTBC  NDBPS,4x , (4x OFDM symbol duration)
  NDBPS,last,init = NDBPS,4x(=NDBPS) (NCBPS,last,init = NCBPS,4x(=NCBPS))
  BCC case: interleaver size = NSD,4x(=NSD)
  Data subcarrier with k (k=1,2…) indices excluding DC and pilot tones are used.

## Slide 13: PSDU_LENGTH Calculation Process (cont.)
PSDU_LENGTH
  BCC
  LDPC

## Slide 14: Special Cases for LDPC encoding
Calculate NDBPS,last,init and NCBPS,last,init
Calculate Npld and Navbits.

## Slide 15: Special Cases for LDPC encoding (cont.)
  With above parameters, determine {LLDPC, NCW, Nshrt, Nrep, Npunc} as in 11n/11ac.
    In the puncturing step, if one of conditions for LDPC OFDM symbol extension is met,
    Re-compute Npunc, Nrep based on updated parameters.

## Slide 16: PHY Padding Bits
Calculation of the number of PHY padding bits (0~7 bits)
  BCC
  LDPC

## Slide 17: Example) LDPC Case
APEP_LENGTH = 1000, MCS7 (64-QAM, 5/6-code), Nss = 1, No STBC. 40MHz Channel
NDBPS,4x = 2290, NDBPS,2x = 1170, NDBPS,1x = 510
NCBPS,4x = 2748, NCBPS,2x = 1404, NCBPS,1x = 612
NSYM,init = ceil((8*1000+16)/2290) = 4
NDbit,last = (8*1000+16)-2290*3 = 1146
  The last symbol is 2x OFDM symbol.
  NDBPS,last,init = NDBPS,2x=1170, NCBPS,last,init = NCBPS,2x =1404.

## Slide 18: Example) LDPC Case (cont.)
Npld = 3*2290 + 1*1170 = 8040
Navbits = 3*2748 + 1*1404 = 9648
From Table 20-16,
  NCW = ceil(8040/(1944*5/6)) = 5
  LLDPC = 1944
Nshrt = 5*1944*5/6-8040 = 60
Npunc = 5*1944-9648-60 = 12, No symbol extension.
  NSYM = NSYM,init
  NDBPS,last,init = NDBPS,2x=1170, NCBPS,last,init = NCBPS,2x =1404.