## Slide 1: OBSS NAV and PD Threshold Rule for Spatial Reuse
Date: 2015-09-13
Authors:
Name | Affiliation | Address | Phone | Email
Rossi Jun Luo | Huawei | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18916768513 | jun.l@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liule@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | zhangjiayin@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Yunsong Yang | Huawei | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jun Zhu |  |  |  | zhujun75@huawei.com
Name | Affiliation | Address | Phone | Email
Matthew Fischer | Broadcom |  |  | mfischer@broadcom.com
Ron Porat |  |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 6
Name | Affiliation | Address | Phone | Email
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Authors (continued)
Name | Affiliation | Address | Phone | Email
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 7
Authors (continued)
Name | Affiliation | Address | Phone | Email
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 8
Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 9: Recap on Spatial Reuse
  Previous presentations[1, 2] have indicated general assumptions:
  The STA determines whether the detected frame is an inter-BSS or an intra-BSS frame by using BSS color (in SIG-A) or MAC address in the MAC header. If the detected frame is an inter-BSS frame, under TBD condition, uses TBD OBSS PD level that is greater than the minimum receive sensitivity level.
    If an OBSS PPDU is received and is below a proposed OBSS PD threshold, then the medium is available for use, provided no other CCA indication indicates a BUSY channel.
  This presentation discusses the deferral rules (including NAV rule and STA behavior upon receipt of an OBSS PPDU) based on general assumptions above.

## Slide 10: Current NAV rule
  Devices will set/reset NAV when the duration field is decoded correctly from inter-BSS frame.
  “A STA that receives at least one valid frame within a received PSDU shall update its NAV with the information received in any valid Duration field from within that PSDU for all frames where the new NAV value is greater than the current NAV value, except for those where the RA is equal to the MAC address of the STA.” —From 802.11-2012
  It means that HE STA also sets its NAV from the valid inter-BSS frame, regardless whether the RSSI is less than the OBSS PD level or not. Obviously, current NAV setting rule will cause to disturb the spatial reuse.

## Slide 11: Example of Current NAV for SR
  Let’s say OBSS PD level is set to -72dBm. Intra-BSS device A located in the OBSS yellow ring with receiving OBSS signal strength from (-82, -72)dBm can change from CCA busy to idle.
  NAV issue: However, if device A decodes the duration field correctly from OBSS signal, device A can’t transmit for spatial reuse due to the higher NAV value, following 11ac NAV rule.
  In order to take advantage of SR feature, it is necessary to make changes on current NAV rules to enable more SR links (e.g. device A).
OBSS
A
OBSS signal@-82dBm
OBSS signal@-72dBm
CCA busy
CCA idle
CCA busy->idle;
duration decoding error
CCA busy->idle;
duration decoding correctly
B
Intra-BSS

## Slide 12: Proposed Solution: OBSS NAV Rule
For 11ax devices,
  When a STA uses its OBSS PD level(e.g., -72dBm) for OBSS signal, it should not update its NAV when receiving a valid duration field from OBSS signal, if the measured RSSI of OBSS signal is less than the OBSS PD level.
  Otherwise, STA should update its NAV following 11ac rule(e.g., STA B with measured RSSI >= -72dBm, or STA C at PD level=-82dBm).
  Benefit: Device A may have a chance to contend/transmit for SR.
AP1
STA1
11ax BSS
AP2
PD = -82dBm
11ax BSS
NAV is updated
PD = -72dBm
NAV is ignored@RSSI<-72dBm
STA A
STA C
STA B
NAV is updated@RSSI>=-72dBm
PD = -72dBm

## Slide 13: Simulation Results
Simulation scenario 1 (Residential) with ~10% gain on mean throughput
All devices set PD level to be -72/62/52 dBm for OBSS frame
DL/UL full buffer traffic
PD level | 5% | 50% | 90% | Mean
-82 | 0.8002 | 6.63 | 19.54 | 8.7542
-72 | 1.176 | 7.586 | 23.66 | 11.214
-62 | 0.907 | 7.366 | 22.89 | 10.612
-52 | 0.793 | 6.97 | 21.52 | 9.781
PD level | 5% | 50% | 90% | Mean
-82 | 0.8002 | 6.63 | 19.54 | 8.7542
-72 | 1.051 | 7.15 | 22.76 | 9.8445
-62 | 1.058 | 6.88 | 21.23 | 9.3572
-52 | 0.7035 | 6.71 | 20.69 | 8.9338
13.9%
13.4%
9.5%
STA throughput(Mbps) with enhanced NAV rule
STA throughput(Mbps) with11ac NAV rule

## Slide 14: Simulation Results
Simulation scenario 2 (Enterprise) with ~20% gain on mean throughput
All devices set PD level to be -72/62/52 dBm for OBSS frame
DL/UL full buffer traffic
Note that additional gain was observed in SS2 than SS1, as SS2 is more dense with more SR links
PD level | 5% | 50% | 90% | Mean
-82 | 0.3145 | 1.545 | 4.634 | 1. 965
-72 | 0.5823 | 2.1746 | 6.037 | 2.861
-62 | 0.4669 | 2.0659 | 6.148 | 2.9415
-52 | 0.2896 | 1.821 | 5.496 | 1.854
STA throughput(Mbps) with enhanced NAV rule
PD level | 5% | 50% | 90% | Mean
-82 | 0.3145 | 1.545 | 4.634 | 965
-72 | 0.5017 | 1.852 | 5.132 | 2.312
-62 | 0.4618 | 1.934 | 5.883 | 2.425
-52 | 0.3065 | 1.619 | 4.651 | 1.569
STA throughput(Mbps) with11ac NAV rule
23.7%
21.3%
18.1%

## Slide 15: Further Discussion
  What’s the STA’s behavior upon receiving an OBSS PPDU with RSSI below a proposed OBSS PD threshold?
  Previous discussion has focused on OBSS NAV setting:
  If an OBSS PPDU is received and is below a proposed OBSS PD threshold(e.g. -72dBm), then the medium is available for spatial reuse and the STA should not update its NAV, provided no other CCA indication indicates a BUSY channel.
  Furthermore on STA’s behavior: Should the entire PPDU be discarded?
  The implication is that the OBSS PPDU PHY SIG Length information would be ignored along with the entire PPDU Payload
  We found no reason to not discard the entire PPDU: Payload + decoded PHY Header

## Slide 16: Keep some part of OBSS PPDU?
Nearly everything in the PHY SIG field is there for the intended recipient[3], except for possibly:
  LENGTH
  Bandwidth

## Slide 17: Bandwidth Field
It seems that this is a don’t care, since the only time it would matter is when you want to mark a channel as BUSY because of the receipt of this PPDU
  I.e. if you want to say that the channel is NOT BUSY, then the bandwidth does not matter because it is meaningless to say which channels are NOT BUSY due to this PPDU…
I.e. Bandwidth field can be discarded if the PPDU is to be discarded

## Slide 18: Summary
We propose the following OBSS NAV rule:
  If an Inter-BSS PPDU is received and is below a proposed OBSS PD level (e.g. -72dBm), the STA should not update its NAV by receiving a valid duration field from Inter-BSS PPDU.
Further, we propose the following STA behavior:
  A STA should regard an Inter-BSS PPDU with a valid PHY header and that has a receive power/RSSI below the OBSS PD level used by the receiving STA and that meets additional TBD conditions, as not having been received at all, except that the medium condition shall indicate BUSY during the period of time that is taken by the receiving STA to validate that the PPDU is from an Inter-BSS, but not longer than the time indicated as the length of the PPDU payload

## Slide 19: Reference
  [1] 11-15-0797-00-00ax-nav-operation-for-spatial-reuse
  [2] 11-15-1063-00-00ax-11ax-Channel-access-procedure
  [3] 11-15-1077-00-00ax-he-sig-a-content

## Slide 20: Straw Poll
Do you agree to add the TGax Specification Framework:
  5.1 Features for operation in dense environments [802.11ax SFD]
  A STA should regard an Inter-BSS PPDU with a valid PHY header and that has a receive power/RSSI below the OBSS PD level used by the receiving STA and that meets additional TBD conditions, as not having been received at all (e.g., should not update its NAV), except that the medium condition shall indicate BUSY during the period of time that is taken by the receiving STA to validate that the PPDU is from an Inter-BSS, but not longer than the time indicated as the length of the PPDU payload
    The OBSS PD level is greater than the minimum receive sensitivity level
  Y
  N
  A