## Slide 1: SIG-B Resource unit allocation coding
Name | Affiliations | Address | Phone | email
Amin Jafarian | Newracom |  |  | amin.jafarian@newracom.com
Reza Hedayat |  |  |  | 
Minho Cheong |  |  |  | 
Young Hoon Kwon |  |  |  | 
Daewon Lee |  |  |  | 
Vida Ferdowsi |  |  |  | 
Yongho Seok |  |  |  | 

## Slide 2: Motivation
For UL-MU MIMO scheduling, the bandwidth allocation should be done in SIG-B field of the triggering frame
In general, there are many sub-bandwidths to be allocated
We need to make sure this field to stays reasonably short when there are multiple STAs allocated
In this presentation we go over general concepts of two schemes and compare their performances. For simplicity, we call them with the following short names:
  Fixed length
    The length of the allocation is constant and is not a function of number of STAs or the allocated BWs
  Flexible length
    The length of the allocation is not constant and changes based on the number of STAs and the allocated BWs

## Slide 3: Fixed length allocation
For each 8MHz sub band of 20MHz, there are total of 1 (no STA) + 7 (1 STA) + 11 (2 STAs) + 6 (3 STAs) + 1 (4 STAs) = 26 ways that can be compressed in 5 bits, this means for 20MHz BW, we need 5+1+5=11 bits and for 40MHz, we need 2*11=22 bits to convey all the possible sub-band allocations
Pros:
  Length of SIG-B depends only on the BW of the allocation and not number of STAs or the locations of the allocation
Cons:
  It can be very long
    Variable length can result in shorter SIG-B in many scenario

## Slide 4: Flexible length
Its not as easy to put some figure in Flexible length encoding. It highly depends on the encoding scheme
We took a simple encoding algorithm to show some comparison of the schemes. We call it Tree encoding:
STA2
STA1
STA3
No STA
STA4
1 1 1 00 11 10 00
2MHz
2MHz
2MHz
2MHz
2MHz
2MHz
2MHz
2MHz
4MHz
4MHz
8MHz
4MHz
4MHz
8MHz
2MHz
20MHz
STA2
STA1
STA3
STA4
1
0
0
1
1
1
1
1
0
0
0

## Slide 5: Comparing the fixed length and flexible min/max length
 | 4 STA, 40MHZ | 4 STA, 80MHz | 4 STA, 160MHz
Fixed Length (bits) | 2+5*4=22 | 4+5*8=44 | 8+5*16=88
Flexible Length maximum (bits) | 2+6+4*4=24 | 4+6+4*6=34 | 8+6+4*8=46
Flexible Length minimum (bits) | 1+4+6=11 | 11+2=13 | 13+2=15
Here is the comparison, when there are 4 STAs in the allocation:

## Slide 6: Average Flexible length Comparison
Number of STAs | Compress Method | 20Mhz | 40Mhz | 80Mhz | 160Mhz
1 | Fixed | 10.00 | 20.00 | 40.00 | 80.00
 | Flexible | 5.47 | 7.29 | 9.17 | 11.10
2 | Fixed | 10.00 | 20.00 | 40.00 | 80.00
 | Flexible | 8.87 | 12.14 | 15.52 | 19.05
3 | Fixed | 10.00 | 20.00 | 40.00 | 80.00
 | Flexible | 11.11 | 15.90 | 20.80 | 25.89
4 | Fixed | 10.00 | 20.00 | 40.00 | 80.00
 | Flexible | 12.59 | 18.98 | 25.38 | 32.01
5 | Fixed | 10.00 | 20.00 | 40.00 | 80.00
 | Flexible | 13.45 | 21.52 | 29.43 | 37.57
6 | Fixed | 10.00 | 20.00 | 40.00 | 80.00
 | Flexible | 13.86 | 23.61 | 33.05 | 42.70
7 | Fixed | 10.00 | 20.00 | 40.00 | 80.00
 | Flexible | 14.00 | 25.30 | 36.32 | 47.47
8 | Fixed | 10.00 | 20.00 | 40.00 | 80.00
 | Flexible | 14.00 | 26.66 | 39.27 | 51.93
9 | Fixed | 0.00 | 20.00 | 40.00 | 80.00
 | Flexible | 0.00 | 27.72 | 41.96 | 56.12

## Slide 7: Flexible Length
Note: In the Average scenario, we consider all cases, many of those may not be out of interest. Looking into only practical cases, the average length for flexible case is even less
Pros:
  It reduces the length of SIG-B in many scenarios
Cons:
  Its length depens on:
    Number of STAs in the allocation
    BW and location of STAs

## Slide 8: Summary
Two ways of encoding BW allocation inside the SIG-B is presented
  Fixed length and flexible length
We provide one specific flexible length coding (tree encoding) and compare min/max and average performance of that with the fixed length encoding
In general, the flexible length performs much better than the fixed length