## Slide 1: Use Case of LRLP Operation for IoT
Date: 2015-09-14
Authors:

## Slide 2: Contents of this Contribution
Introduction to LRLP
Use Case I: Building Energy Management System
Metrics for LRLP

## Slide 3: Long Range Low Power Operation
Longer Range operation
  In mainstream 802.11
Lower Power operation
  Enable battery powered IoT
Integrated with mainstream networks
  Interoperable in mixed BSS case
Integrated with mainstream products
  Negligible incremental cost for implementation at an AP
  Acceptable to have a specialized low-cost silicon for LRLP STA, but the AP should be based on standard silicon.
Intended for M2M – managed impact on existing network
  Medium Occupancy Limit, average occupancy limit
  Other mechanisms as appropriate

## Slide 4: Use Case I: Building Energy Management Systems (BEMS)
User: Owner of a multi-storied home remotely sets a dynamic temperature threshold for rooms in each floor from his office and the IoT-enabled HVACs operate to maintain desired temperature, energy efficiency, and reliability
Environment: The multi-storied home consists of an HVAC (heating, ventilation, and air conditioning) unit with embedded temperature sensors and also temperature sensors in each room. These sensors remotely monitor and control installed HVACs within buildings. The sensors connect to the IoT Gateway that deliver data directly to the cloud or local data center. The cloud analyzes the collected data, as well as external data, such as weather data or grid signals, and implements changes to improve efficiency, comfort. The IoT network enhances the control and automation of HVACs installed in buildings and homes.
Use Case:
  Temperature sensors within a room report data at periodic intervals to the IoT Gateway from where the data is entered into a database.
  The sensors embedded in an HVAC are connected and controlled directly to the IoT Gateway. These sensors do not communicate with the temperature sensors in rooms of a building.
  Temperature sensors send alarms when the temperature exceeds a pre-defined threshold (set by the owner). The alarm is then relayed by the IoT Gateway to the HVAC through the embedded sensors.
  The IoT Gateway utilizes data from traditional automation systems, smart meter internal electricity consumption in order to analyze the alarm communicated by temperature sensors
  The HVAC takes appropriate corrective action by changing the temperature of the specific room from which the alarm was raised by temperature sensors

## Slide 5: Metrics for LRLP
Data transmission rate: Low data throughput typical of applications in sensor or actuator networks, e.g., 100kbps of limited size file transfer
Transmission range: Narrow bandwidth is a key solution to achieve increase transmission range, given a fixed transmit power
Peak power consumption: This metric controls the power consumption during activity periods in specified duty cycle of LRLP operation
Average current consumption: Battery life time is inversely related to this metric and is measured in mA
  Lower average current consumption for a fixed battery capacity improves battery life time
Battery capacity: Battery life time is directly related to this metric and is measured in mAh (mA hours)
  Dependent on rate of discharging the battery (e.g., 230-240mAh at 500uA rate of discharge, while 150mAh at 3mA rate of discharge) [1]
  Dependent on pulse duration (ON time of an LRLP device)

## Slide 6: Summary
We have presented an use case for LRLP operation with IoT devices in a smart building

## Slide 7: References
[1] IEEE 11-15/0775r1: Integrated Long Range Low Power Operation for IoT