## Slide 1: Discussion on Concurrent STA-to-STA Transmissions in 11ax
Date: 2015-09-15
Authors:

## Slide 2: Background
STA-to-STA (S2S) transmissions without signal relays via AP may provide significant benefits
  Higher spectrum (reuse) efficiency, higher order MCS, power saving, etc.
Some mechanisms have been proposed to support frame exchanges between two STAs
  WiFi direct, DLS/TDLS, IBSS, etc.
Issues of existing mechanisms
  Low spectrum efficiency
    Based on CSMA/CA
    Each STA pair has individual operations
  Do not support concurrent TX among multiple STA pairs
    S2S TX are usually operated by STAs closely located with each other
    Low TX power can be used

## Slide 3: Possible Scenarios of Concurrent Transmissions in 11ax
To boost spectrum (reuse) efficiency, concurrent S2S transmissions might be one of the possible solutions
Concurrent S2S TX may be operated with or without AP
  With AP
    Concurrent UL pairs and S2S pairs (Fig. 1)
    Concurrent DL pairs and S2S pairs (Fig. 2)
    Concurrent multiple S2S pairs (Fig. 3)
  Without AP
    Concurrent multiple S2S pairs (Fig. 4)
Developing mechanisms supporting concurrent TX in 11ax is thus highly desirable to enhance throughput in the dense environment
Fig.1
Fig.2
Fig.3
Fig.4

## Slide 4: Considerations on AP Centric Concurrent Transmissions in 11ax
More capabilities of transmission coordination beyond CSMA/CA such as scheduling based MU transmission on OFDMA PHY are considered to be supported by AP in 11ax
In the case of S2S concurrent TX with AP, AP may provide transmission coordination to further enhance the performance
  Which also fully utilize the feature (AP centric) of 11ax
In concurrent TX, the factor significantly impacting the performance lies in interference among transmission pairs

## Slide 5: Interference in S2S Concurrent Transmissions
There are multiple receivers in S2S concurrent transmissions, for example
  For UL TX from STA_1 to AP, receiver is AP
  For S2S TX from STA_3 to STA_2, receiver is STA_2
AP may suffer interference from STA_3
STA_2 may suffer interference from STA_1
Concurrent are allowable if
  Interference level at two receivers are both acceptable
  (concurrent TX opportunity)
Possible solutions to create/find concurrent TX opportunity
  Communication ranges of S2S are usually small, a smaller TX power can be used.
  Adjustable ED supported by dynamic CCA and TPC

## Slide 6: Adjustable ED in CCA and TPC
Adjustable ED supported by dynamic CCA and TPC could support concurrent TX even when interference levels at receiver sides are high, if the received signal strength is also high
  Concurrent TX are allowable when SINRs at all receivers are acceptable
How to find a concurrent TX opportunity?

## Slide 7: More Considerations on Adjustable ED in CCA and TPC
To find a concurrent TX opportunity, the following information might be needed
  AP
    Specific power level adopted by STA1, PWRsta_1
    Path loss from STA_1 to AP
    Path loss from STA_3 to AP
  STA2
    Specific power level adopted by STA1, PWRsta_1
    Path loss from STA_1 to STA_2
    Path loss from STA_3 to STA_2
AP may coordinate above information exchanges

## Slide 8: Considerations on AP Coordinated Concurrent TX
There can be two design alternatives under the AP coordination
  AP collects above information to determine the TX power level for a S2S pair for concurrent TX
    A MAC layer signaling exchange protocol is needed to collect all the information
  A S2S pair autonomously determines its TX power level for concurrent TX, and call for AP’s permission
    AP decides whether to grant S2S for concurrent TX or not
    A MAC layer signaling exchange protocol is needed for a S2S pair and AP to estimate SINR at their own receivers

## Slide 9: Conclusions
Based on the potential benefits on the enhancement of spectrum (reuse) efficiency, we may proceed to discuss the possibilities to support concurrent S2S TX in 11ax
To support concurrent S2S TX, how to find a concurrent TX opportunity is an issue
  Adjustable ED supported by dynamic CCA and TPC
  Concurrent TX are allowed when SINRs at all receiver sides are acceptable
AP can coordinate the information exchanges between STAs to find a concurrent TX opportunity
  11ax might need a MAC layer signaling exchange protocol

## Slide 10: Straw-poll 1
▪ Do you agree that 802.11ax should support concurrent STA-to-STA transmissions?
Yes:
No:
Abstain: