## Slide 1: Proposed Merge of Simulation Scenarios
Date: 2015-09-14
Authors:

## Slide 2: Abstract
This document discusses the simulation requirements for 11ay usage models and suggests some potential merges for the required simulation scenarios.

## Slide 3: Usage Model 1: Ultra Short Range (USR) Communications
Summary:
User downloads mass data from a fixed source device to a semi-stationary sink device indoors, at very short range.
Requirements:
10 Gbps P2P link < 10 cm
Latency < 100 ms
Power < 400 mW
Advantages:
LOS
Stationary
Low/no interference
Evaluation Methodology: LLS
Given that the P2P link is LOS, short, and potentially protected, chances are there is little/no interference. Also, since the sink device is stationary, there is no significant change with respect to the environment.
When there is not interaction with other users (e.g. interference) or the environment (e.g. blocking), there is no need for an SLS.
This usage model can be evaluated using a simple LLS to test data rate, latency, and power.

## Slide 4: Usage Model 2: 8K UHD Wireless Transfer at Smart Home
Summary:
User streams 8K UHD from a fixed source device to a semi-stationary sink device indoors, at moderate range.
Requirements:
28 Gbps P2P link < 20 m
Latency and jitter < 5 ms
Challenges:
NLOS
Moving (pedestrian speeds)
Advantages:
Low/no interference
Evaluation Methodology:
While there is little/no interference from other devices, the sink device could be moving, thus there may be significant interaction with the environment. As a result, this usage model is best evaluated in an SLS.
However, the requirements and challenges of this usage model will be met if the requirements and challenges of Usage Model 3 (VR/AR) are met. Thus, it can be subsumed by Usage Model 3.

## Slide 5: Usage Model 3: Augmented Reality/Virtual Reality Wearables
Summary:
AR/VR traffic between a fixed source and slowly moving sink device at moderate range, indoors, with little/no interference; OR between slowly moving source and sink devices at very short range, indoors, in heavy interference conditions.
Requirements:
20 Gbps P2P link < 20 m
Latency and jitter < 5 ms
PER < 10E-2
Challenges:
NLOS
Moving (pedestrian speeds)
Heavy interference
Evaluation Methodology: SLS
This usage model poses some of the toughest challenges of any in the group. Not only are the source and sink devices potentially moving, there exists the potential for very high interference in some environments (e.g. commuter). Thus, this usage model must be evaluated in an SLS.

## Slide 6: Usage Model 4: Data Center 11ay Inter-Rack Connectivity
Summary:
Mixed traffic between a fixed source device and one or more fixed sink devices, indoors at short range.
Requirements:
20 Gbps P2P/P2MP links < 2 m
Latency < 100 ms
PER < 10E-2
Advantages:
LOS
Stationary devices
Evaluation Methodology:
Due to the possibility of multi-hop configuration, this usage model needs an SLS for proper evaluation.
However, the requirements and challenges of this usage model will be met if the requirements and challenges of Usage Model 8 (Backhauling) are met. Thus, it can be subsumed by Usage Model 8.

## Slide 7: Usage Model 5: Mass Data Distribution/Video on Demand
Summary:
Mass data distribution between fixed source device and many semi-stationary sink devices, indoors at large range.
Requirements:
20 Gbps P2P/P2MP links < 100 m
Latency < 100 ms
Challenges:
NLOS
Moving (pedestrian speeds)
Potentially heavy competition for channel resources
Evaluation Methodology:
Due to the mobility of users and heavy competition for channel resources, this usage model must be evaluated in an SLS.
However, the requirements and challenges of this usage model will be met if the requirements and challenges of Usage Model 6 (Offloading) are met. Thus, it can be subsumed by Usage Model 6.

## Slide 8: Usage Model 6: Mobile Offloading and Multi-Band Operation
Summary:
Offloading cellular traffic onto 60 GHz APs, indoors and outdoors at large range.
Requirements:
20 Gbps P2P/P2MP links < 100 m
Latency < 100 ms
PER < 10E-2
Challenges:
NLOS
Moving (pedestrian speeds)
Heavy interference
Evaluation Methodology: SLS
Due to the heavy interference and mobility of users, this usage model requires evaluation via SLS.

## Slide 9: Usage Model 7: Mobile Fronthauling
Summary:
Forwarding mixed traffic from fixed baseband unit to fixed remote radio heads, outdoors at large range.
Requirements:
20 Gbps P2P/P2MP links < 200 m
Advantages:
LOS
Stationary devices
Low/no interference
Evaluation Methodology:
Since there is little/no interference and devices are stationary, there is no need to model the environment; an LLS should suffice for the purpose of evaluating range extension.
However, the requirements and challenges of this usage model will be met if the requirements and challenges of Usage Model 8 (Backhauling) are met. Thus, it can be subsumed by Usage Model 8.

## Slide 10: Usage Model 8: Wireless Backhauling
Summary:
Forwarding mixed traffic from fixed AP to fixed AP outdoors at large range.
Requirements:
20 Gbps P2P/P2MP links < 1000 m
Latency < 35 ms
Advantages:
LOS
Stationary devices
Low/no interference
Challenges:
Potential multi-hop
Evaluation Methodology: SLS
While there is little/no interference and no mobility, this usage model should be modeled in an SLS due to the potential for multi-hop.

## Slide 11: Usage Model 9: Docking Station
Summary:
Sending mixed traffic between fixed docking station and fixed peripherals, indoors at short range.
Requirements:
20 Gbps P2P/P2MP links < 2 m
Latency < 35 ms
Challenges:
NLOS
Heavy interference
Moving (pedestrian speeds)
Evaluation Methodology:
This usage model requires SLS evaluation given the potential for heavy interference and moving devices.
However, the requirements and challenges of this usage model will be met if the requirements and challenges of Usage Model 3 (VR/AR) are met. Thus, it can be subsumed by Usage Model 3.

## Slide 12: Potential MAC Simulation Scenarios
SLS for AR/VR commuter usage model to evaluate MAC performance (throughput, latency, jitter, PER) in high densities of mobile, NLOS, short range P2P links. This SLS incorporates the MAC challenges and requirements of 8K UHD and Docking Station usage models.
SLS for Offloading usage model to evaluate MAC performance (throughput, latency, PER) in high densities of mobile, NLOS, long range P2MP links. This SLS incorporates the MAC challenges and requirements of Mass Distribution usage model.
SLS for Backhauling usage model to evaluate MAC performance (throughput, latency) in multi-hop, LOS, very long range P2MP links. This SLS incorporates the MAC challenges and requirements of Data Center and Fronthauling usage models.