## Slide 1: IEEE 802.11 multicast properties
September 2015
Adrian Stephens, Intel Corporation
Date: 2015-09-15
Authors:
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r2
September 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 2: Introduction
An initial version of these slides was provided to certain IETF members in preparation for an IETF/802 leadership meeting.
Updates as discussed in ARC SC 2015-09-15 and 2015-09-16
September 2015
Adrian Stephens, Intel Corporation
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r2
September 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 3: 802.11 properties
802.11 operates in unlicensed frequency bands. There are no guarantees that any traffic gets through.
802.11 MAC layer packets can be lost due to collision, interference, poor rate adaptation decisions, changes in the radio channel (e.g. walking behind a steel-reinforced pillar).
A 10% “packet error ratio” is not unreasonable, but this is metric with a *lot* of noise in it.
Unicast traffic is retried up to some limit (typically 4-12 times). This improves reliability, but it’s still subject to higher-layer packet loss
Adrian Stephens, Intel Corporation
September 2015
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r2
September 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 4: 802.11 multicast properties
Multicast / broadcast traffic is generally not retransmitted, because there is no acknowledgement
Multicast / broadcast traffic is generally sent at a “lowest common denominator” rate, known as a basic rate. This might be as low as 6 Mbps, when unicast links are operating at 600 Mbps.
There are options, that are not commonly implemented or certified to improve multicast reliability –
  GroupCast with Retries (GCR) - Greater reliability is provided via unsolicited retries or the block ack mechanism
  Directed Multicast Service (DMS) – convert unicast to multicast
  Flexible Multicast Service (FMS) that allows a multicast rate to be selected that is higher than a basic rate.
Adrian Stephens, Intel Corporation
September 2015
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r2
September 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 5: 802.11 and power save
Both unicast and multicast traffic can be delayed by power-saving mechanisms.
Unicast is delayed until a STA wakes up and asks for it. Additionally, unicast traffic may be delayed to improve power save, efficiency and increase probability of aggregation.
Multicast traffic is delayed in a wireless network if any of the STAs in that network are power savers. All STAs are awake at a known time to receive multicast traffic.
Packets can also be discarded due to buffer limitations in the AP and non-AP STA.
Adrian Stephens, Intel Corporation
September 2015
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r2
September 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 6: 802.11 implementer options
An 802.11 AP manufacturer might optimize certain multicast-related behaviors
There’s nothing in the standard to stop an implementer from turning multicast into unicast traffic
  Most enterprise AP vendors implement multicast to unicast (proprietary mechanisms)
There is support in the 802.11 standard for Proxy ARP and Proxy Neighbor Discovery
  Implemented in some devices but not widely deployed at this time
Adrian Stephens, Intel Corporation
September 2015
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r2
September 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 7: References
Also see https://mentor.ieee.org/802.11/dcn/15/11-15-1015-01-00ax-proxy-arp-in-802-11ax.pptx which describes some multicast issues and Proxy ARP/Neighbor Discovery operation in WLANs
Adrian Stephens, Intel Corporation
September 2015
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r2
September 2015
        Adrian Stephens, Intel Corporation
Page <number>