## Slide 1: IETF Nov 2015: IEEE 802.11 multicast capabilities
November 2015
Dorothy Stanley, HP (Aruba Networks)
Date: 2015-11-09
Authors:
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 2: Abstract
This file contains a description of selected IEEE 802.11 multicast optimization capabilities and their benefits, for presentation at a November 2015 IETF INT area session.
Development of this material is in response to questions from IETF participants on IEEE 802.11 multicast performance, see https://www.iab.org/wp-content/IAB-uploads/2013/01/multicast-problem-statement.pptx.
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 3: Agenda: 802.11 multicast optimization features
Multicast in 802.11
IEEE Std 802.11-2012 Proxy ARP Description
Directed Multicast Service (DMS)
GroupCast with Retries (GCR) Description
Implementation Status of Optimization Features
Back-up GCR Details
References
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 4: 802.11 Packet Transmission
802.11 operates in unlicensed frequency bands. There are no guarantees that any traffic gets through.
802.11 MAC layer packets can be lost due to collision, interference, poor rate adaptation decisions, changes in the radio channel (e.g. walking behind a steel-reinforced pillar).
A 10% “packet error ratio” is not unreasonable, but this is metric with a *lot* of noise in it.
Unicast traffic is retried up to some limit (typically 4-12 times). This improves reliability, but it’s still subject to higher-layer packet loss
Dorothy Stanley, HP (Aruba Networks)
November 2015
Slide <number>
From 11-15-1161r2
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 5: How does Multicast affect WLANs?
AP extends wired segment
  All broadcast frames on LAN side copied to WLAN
  In WLAN, broadcast messages transmitted at most robust MCS
  Most robust MCS implies large frames sent at slow rate
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
From 11-15-1015r1
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
Guido R. Hiertz et al., Ericsson
Page <number>

## Slide 6: 802.11 multicast properties
Multicast / broadcast traffic is generally not retransmitted, because there is no acknowledgement
Multicast / broadcast traffic is generally sent at a “lowest common denominator” rate, known as a basic rate. This might be as low as 6 Mbps, when unicast links are operating at 600 Mbps.
Lower rate  larger frame, less airtime for everything else.
There are options, that are not commonly implemented or certified to improve multicast reliability –
  GroupCast with Retries (GCR) - Greater reliability is provided via unsolicited retries or the block ack mechanism
  Directed Multicast Service (DMS) – convert multicast to unicast
Dorothy Stanley, HP (Aruba Networks)
November 2015
Slide <number>
From 11-15-1161r2
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 7: 802.11 and power save
Both unicast and multicast traffic can be delayed by power-saving mechanisms.
Unicast is delayed until a STA wakes up and asks for it. Additionally, unicast traffic may be delayed to improve power save, efficiency and increase probability of aggregation.
Multicast traffic is delayed in a wireless network if any of the STAs in that network are power savers. All STAs are awake at a known time to receive multicast traffic.
Packets can also be discarded due to buffer limitations in the AP and non-AP STA.
Dorothy Stanley, HP (Aruba Networks)
November 2015
Slide <number>
From 11-15-1161r2
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 8: Agenda: 802.11 multicast optimization features
Multicast in 802.11
IEEE Std 802.11-2012 Proxy ARP & ND Description
Directed Multicast Service (DMS)
GroupCast with Retries (GCR) Description
Implementation Status of Optimization Features
Back-up GCR Details
References
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 9: Proxy ARP in 802.11-2012
The AP knows all associated STA’s MAC address and IP address
  AP acts as central “manager” in BSS
AP acts on behalf of STAs
  Power save relies on AP buffering data for STAs
Proxy ARP easy to implement at AP
Advantages
  Less low MCS broadcast traffic on wireless medium
  STA benefits from extended power save in sleep mode as ARP requests are replied to by AP
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
From 11-15-1015r1
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
Guido R. Hiertz et al., Ericsson
Page <number>

## Slide 10: Proxy ARP in 802.11-2012
When the AP supports Proxy ARP “[…] the AP shall maintain a Hardware Address to Internet Address mapping for each associated station, and shall update the mapping when the Internet Address of the associated station changes. When the IPv4 address being resolved in the ARP request packet is used by a non-AP STA currently associated to the BSS, the proxy ARP service shall respond on behalf of the non-AP STA”
  Keeps ARP frames off the wireless medium
  See 10.23.13 in [2]
Slide <number>
Dorothy Stanley, HP (Aruba Networks)
November 2015
From 11-15-1015r1
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
Guido R. Hiertz et al., Ericsson
Page <number>

## Slide 11: ARP and IPv6?
IPv6 doesn’t need ARP
  IPv6 uses Neighbor Discovery Protocol (NDP) instead
Every IPv6 node subscribes to special multicast address
  Neighbor-Solicitation message replaces ARP
NDP may be used to request additional information
  Maximum Transmission Unit
  Router Solicitation
  Router Advertisement, etc.
NDP messages are sent as group addressed (broadcast) frames in 802.11
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
From 11-15-1015r1
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
Guido R. Hiertz et al., Ericsson
Page <number>

## Slide 12: IPv6 support in 802.11-2012
“When an IPv6 address is being resolved, the Proxy Neighbor Discovery service shall respond with a Neighbor Advertisement message […] on behalf of an associated STA to an [ICMPv6] Neighbor Solicitation message […]. When MAC address mappings change, the AP may send unsolicited Neighbor Advertisement Messages on behalf of a STA.”
  802.11 Proxy ARP prepared for IPv6
  Keep NDP messages off the wireless medium
  See 10.23.13 in IEEE P802.11-2012
Slide <number>
Dorothy Stanley, HP (Aruba Networks)
November 2015
From 11-15-1015r1
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
Guido R. Hiertz et al., Ericsson
Page <number>

## Slide 13: Agenda: 802.11 multicast optimization features
Multicast in 802.11
IEEE Std 802.11-2012 Proxy ARP & ND Description
Directed Multicast Service (DMS)
GroupCast with Retries (GCR) Description
Implementation Status of Optimization Features
Back-up GCR Details
References
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 14: Directed Multicast Service (DMS)
DMS enables a client to request that the AP transmit group addressed frames destined to the requesting client as individually addressed frames.
AP transmits group addressed frames to the requesting client as individually addressed frames
  Requires 11n A-MSDUs
  Individually addressed frames are acknowledged and are buffered for power save clients
  Requesting STA specifies traffic characteristics for DMS traffic
  DMS was defined in IEEE Std 802.11v-2011
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Notes: <number>

## Slide 15: Groupcast with Retries (GCR)
AP transmits each group addressed frame as conventional group addressed transmission. Retransmissions are group addressed, but hidden from non-11aa clients
A directed block acknowledgement scheme is used to harvest reception status from receivers, and the retransmissions are based upon these responses.
GCR is suitable for all group sizes including medium to large groups. As the number of devices in the group increases, GCR can send block acknowledgement requests to only a small subset of the group.
GCR increases probability of broadcast frame reception success, but still not a guarantee
GCR was defined in IEEE Std 802.11aa-2012
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Notes: <number>

## Slide 16: Issues and continuing improvement re: GCR with Block Acknowledgement
May introduce unacceptable latency
  After sending a group of data frames to the group, the AP has to unicast Block Ack Request to a subset of members; wait for the corresponding Block Ack; retransmit any missed frames and then resume
  This latency may not be acceptable for some traffic
There are ongoing extensions in 802.11 to improve GCR performance
  BAR is send using downlink MU-MIMO (DL MU-MIMO is already in 802.11-REVmc 4.3)
  BA is sent using uplink MU-MIMO (uplink MU-MIMO is a .11ax feature)
  Additional 802.11ax extensions are under consideration, see https://mentor.ieee.org/802.11/dcn/15/11-15-0800-00-00ax-multiplexing-of-acknowledgements-for-multicast-transmission.pptx . The latency is reduced by simultaneously receiving BA information from multiple clients
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Ganesh Venkatesan, Intel
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 17: Agenda: 802.11 multicast optimization features
Multicast in 802.11
IEEE Std 802.11-2012 Proxy ARP & ND Description
Directed Multicast Service (DMS)
GroupCast with Retries (GCR) Description
Implementation Status of Optimization Features
Back-up GCR Details
References
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 18: Multicast Optimization Implementation
An 802.11 AP manufacturer might optimize certain multicast-related behaviors
There’s nothing in the standard to stop an implementer from turning multicast into unicast traffic
  Most enterprise AP vendors implement multicast to unicast (proprietary mechanisms)
Implementation Status of Proxy ARP and Proxy ND
  Implemented primarily in enterprise-grade systems
  Not widely implemented in small office/home systems at this time
GCR and DMS not currently implemented in product
Dorothy Stanley, HP (Aruba Networks)
November 2015
Slide <number>
From 11-15-1161r2
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 19
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Questions?
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 20: More information on GCR implementation
For reference/back-up
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>

## Slide 21: GCR mechanism details
GCR announcement, set up, modification and tear down use DMS Request / DMS Response frames
  DMS Request / DMS Response elements with addition of GCR Request / GCR Response sub-elements
AP can discover the STAs receiving a group address
  Explicit 11aa Group Membership Request / Response frame exchanges
  Non-802.11 methods (e.g. IGMP snooping)
Additional policies for group addressed frames:
  GCR Block ACK
    Suited to medium number of group members. Initiates BA agreement with each group member. Transmitting AP regularly sends BAR to the STAs.
  GCR unsolicited retry
    Suited to large number of group members Retransmit MSDU one or more times to increase probability of success.
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 22: GCR Concealment
“Hidden” frames from non-11aa STAs
  Retransmissions using GCR Block Ack or GCR Unsolicited Retry
  All GCR-SP transmissions
“Original” MSDU is encapsulated inside an A-MSDU
  To preserve the original destination address
  Same Sequence Control value of frame containing A-MSDU as the frame that contained original MSDU
  Retry field = 1
A-MSDU is sent to the “GCR Concealment Address”
  Allocated GCR Concealment MAC address 01-0F-AC-47-43-52
    but can be any group address from an allocated OUI.
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 23: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
1
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 24: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
1
1
1
1
2
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 25: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
2
1
2
1
2
1
2
1
3
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 26: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
3
2
1
2
1
3
2
1
2
1
BAR=3
BA
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 27: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
3
2
1
2
1
3
2
1
2
1
4
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 28: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
3
2
1
4
2
1
4
3
2
1
2
1
4
5
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 29: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
3
2
1
4
5
2
1
4
5
3
2
1
5
2
1
4
5
BAR=5
BA
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 30: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
3
2
1
4
5
2
1
4
5
3
2
1
5
2
1
4
5
4
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 31: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
3
2
1
4
5
2
1
4
5
3
2
1
4
5
2
1
4
5
6
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 32: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
3
2
1
4
5
6
2
1
4
5
3
2
1
4
5
6
2
1
4
5
6
BAR=6
BA
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 33: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
3
2
1
4
5
6
2
1
4
5
3
2
1
4
5
6
2
1
4
5
6
3
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 34: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
3
2
1
4
5
6
3
2
1
4
5
3
2
1
4
5
6
3
2
1
4
5
6
6
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 35: Block ACK for Multicast
AP
STA 4
STA 2
STA 1
STA 3
3
2
1
4
5
6
3
2
1
4
5
6
3
2
1
4
5
6
3
2
1
4
5
6
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 36: GCR Service Period
If one device uses power save, all multicast/broadcast traffic gets buffered until DTIM
  DTIM typically every 3/10 second
  Not great for video/voice
GCR-SP allows much smaller delays between delivery
  Scheduled so devices can sleep between service periods
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 37: GCR-SP
In GCR Request STA specifies if it does/doesn’t want the AP to use GCR-SP, or “doesn’t care”
If AP uses GCR-SP, a Schedule element is included in the GCR Response sub-element
  Schedule of when these group addressed frames might be transmitted – STA must be Awake at these times
  If Service Interval=0, frames could be transmitted at any time – STA must stay Awake (GCR-A)
GCR-SP frames are always concealed
  Because they might be transmitted before the “legacy” transmission
November 2015
Dorothy Stanley, HP (Aruba Networks)
Slide <number>
Source: Graham Smith, SR Technologies
Notes: <number>

## Slide 38: References
https://mentor.ieee.org/802.11/dcn/15/11-15-1161-02-0arc-802-11-multicast-properties.ppt
http://standards.ieee.org/getieee802/download/802.11-2012.pdf (includes 802.11v amendment)
https://mentor.ieee.org/802.11/dcn/15/11-15-1015-01-00ax-proxy-arp-in-802-11ax.pptx
http://standards.ieee.org/getieee802/download/802.11aa-2012.pdf
https://www.iab.org/wp-content/IAB-uploads/2013/01/multicast-problem-statement.pptx
Dorothy Stanley, HP (Aruba Networks)
November 2015
Slide <number>
Notes: doc.: IEEE 802.11-11/1161r3
November 2015
        Adrian Stephens, Intel Corporation
Page <number>