## Slide 1: RTS*/CTS* for UL/DL OFDMA Control
Date: 2015-10-28
Authors:
Name | Affiliation | Address | Phone | Email
Cheeha Kim | POSTECH | Networking & Distributed Systems Lab., Room 341, PIRL, POSTECH, Hyoja-Dong, Pohang, KOREA, 790-784 | 82-54-279-5655 | chkim@postech.ac.kr
Jiseon Lee |  |  |  | happyjskr@postech.ac.kr

## Slide 2: Abstract
MU features include UL and DL OFDMA in 11ax SFD [1]
To improve the channel utilization as much as possible for UL/DL in dense OBSS environment
  AP functions asymmetrically
AP needs to collect STA’s Tx demands to schedule UL MU STAs’ Tx efficiently
This contribution proposes effective channel allocation method and efficient STA’s Tx demands report method using RTS*/CTS* (modified RTS/CTS)

## Slide 3: Backgrounds
802.11ax Spec Framework Document [1]
  Multi-user (MU) features include UL and DL OFDMA
  An UL MU PPDU (MU-MIMO or OFDMA) is sent as an immediate response (IFS TBD) to a Trigger frame (format TBD) sent by the AP
802.11ac standard
  Mandatory support for 20 MHz, 40 MHz and 80 MHz channel widths
  Optional support for 160 MHz and 80+80 MHz channel widths
  RTS/CTS exchange negotiates dynamic bandwidth operation

## Slide 4: Backgrounds (cont’d)
Bandwidth (BW)
  Non-contiguous BW provides higher gain than contiguous BW [2]
  Finer granularity of BW occupation (1/2, 1/4, 1/8 of 20MHz ) [3]
Dense environments [4]
  Configuration control by the AP can help the overall interference situation
  AP could control the use of RTS/CTS for STAs associated with the AP in a way that optimizes network resources
Dense OBSS environments [5]
  AP and STAs might see the busy/idle state of secondary channels differently
  RTS/CTS have no functionalities compensating unused secondary bands

## Slide 5: Motivation
To utilize channels as much as possible
  For DL-OFDMA
    Allocate all the channels if possible
  For UL-OFDMA,
    Collect STA’s Tx demands efficiently
    Schedule channel allocation based on STA’s TX demands

## Slide 6: RTS* - CTS* Configurations
RTS*
  AP/STA initiates transmission with RTS*
    Format is the same as the legacy RTS
    Subtype value may be defined for RTS*
CTS*
  CTS* is issued in response to RTS*
    Every STA is associated exclusively with a sub-channel (tone unit) within 20 MHz at association operation
      20 MHz OFDMA building blocks can carry a mix of different tone unit sizes within each 242 tone unit boundary [1]
    CTS* is sent using associated sub-channel in each 20 MHz band
    Function of CTS* is the same as the original CTS’s plus reporting Tx demand
    But implemented CTS* may contain only Tx demand reports

## Slide 7: AP-initiated Coordination
DL-OFDMA in dense OBSS environment
  AP sends a copy of RTS * in every 20 MHz band
  Receiving STAs respond with CTS* for each accessible 20 MHz band
  Based on CTS*, AP arranges DL-OFDMA channels
    AP is to schedule DL to meet equal data length requirement
  STA’s Tx demands are reported in CTS* as well for UL-OFDMA scheduling
UL-OFDMA in dense OBSS environment
  Trigger* frame contains channel allocation information
  Trigger* must be equal to CTS* in length

## Slide 8: AP-initiated Coordination (cont’d)
Time
DIFS
Back-off
20 MHz
160 MHz
CTS* 1
CTS* 1
CTS* 1
CTS* 1
CTS* 1
CTS* 1
CTS* 1
RTS*
RTS*
RTS*
RTS*
RTS*
RTS*
RTS*
RTS*
CTS* 1
DL DATA → STA1
DL DATA → STA1
DL DATA → STA1
DL DATA → STA1
DL DATA → STA3
DL DATA → STA3
DL DATA → STA2
DL DATA → STA2
CTS* 2
CTS* 2
CTS* 3
CTS* 3
ACK
ACK
ACK
Trigger*
Trigger*
Trigger*
Trigger*
Trigger*
Trigger*
Trigger*
Trigger*
STA1 → UL DATA
STA1 → UL DATA
STA1 → UL DATA
STA1 → UL DATA
STA3 → UL DATA
STA3 → UL DATA
STA3 → UL DATA
STA2 → UL DATA
ACK
160 MHz
DL:
To STA 1
CTS* 1
160 MHz
DL data can receive & UL: To AP
CTS* 3
CTS* 3
CTS* 2
40 MHz
UL: To AP
CTS* 3
80 MHz
UL: To AP

## Slide 9: STA-initiated Coordination
UL-OFDMA in dense OBSS environment
  Unrequested channels may be allocated based on outstanding Tx demands using trigger* along with CTS*
    Trigger* structure is the same as CTS*
      UL STA Tx address is defined
Time
DIFS
Back-off
20 MHz
160 MHz
40 MHz
UL: To AP
DATA
DATA
ACK
RTS*
RTS*
Trigger for unrequested
120 MHz UL
CTS*
CTS*
Trigger*
Trigger*
Trigger*
Trigger*
Trigger*
Trigger*
DATA
DATA
DATA
DATA
DATA
DATA

## Slide 10: Conclusion
Using modified RTS/CTS coordination, efficient DL/UL-OFDMA transmission can be scheduled

## Slide 11: References
[1] 802.11-15/0132-06-00ax-spec-framework
[2] 802.11-13/1058r0 Efficient wider bandwidth operation
[3] 802.11-15/0354r1 Bandwidth granularity on UL-OFDMA data allocation
[4] 802.11-15/0059r1 Uplink RTS/CTS Control
[5] 802.11-14/1442r1 Considerations on DL OFDMA control mechanism