## Slide 1: Authors
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
11ax LDPC Tone Mapper for 160MHz
Date: 2015-11-09

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Blvd, Suite 475, RichardsonTX, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com

## Slide 3: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 5: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Zhou Lan |  |  |  | Zhou.lan@mediaTek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com

## Slide 10: Introduction
11ax has defined the following resource unit (RU) sizes
  26, 52, 106, 242, 484, 996 and 2x996 tones
Except for the RU size of 2x996 tones (160/80+80MHz), the BCC interleaver and LDPC tone mapper designs of all the other RU sizes have been determined in [1]
  LDPC is the only coding scheme for 2x996 tone RU [2]
In this contribution, two LDPC tone mapping options for the 2x996 tone RU are examined
  Option 1: 11ac alike segment parsing + tone mapping within each segment across 980 data tones
  Option 2: no segment parsing, tone mapping (with DTM) across 1960 data tones

## Slide 11: LDPC Tone Mapper Design
Option 1: DTM=20 across each 80MHz with segment parsing
Option 2: Without segment parsing, DTM design for NSD=1960
  Has to be an integer divisor of the number of subcarriers, NSD
    Candidates: 10,14,20,28,35,40,49,56,70

## Slide 12: Simulation Assumptions
Simulation setup
  160MHz, 1960 data tones
  Channel Model, CP, and MIMO Configurations
    DNLoS, CP=0.8us, 1x1, 2x2 (2ss), 4x4 (3ss)
    UMi-NLoS, CP=3.2us, 1x1
  Payload: 2914B(MCS 0/2/4)/3238B(MCS7/9)
  MMSE receiver
  5000 channel realizations
  Ideal timing/frequency/phase
  Ideal channel estimation

## Slide 13: 1x1 in DNLoS

## Slide 14: Performance Summary in 1x1 DNLoS
Lowest SNR values in each column has background colors
Option 1: with segment parsing
Option 2: without segment parsing
  Best SNR performance values are mainly at DTM = {10,14,20,28}
The difference between Option 1 and option 2 (with optimal DTM) is negligible
 | MCS2 |  | MCS4 |  | MCS7 |  | MCS9 | 
D_TM | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER
10 | 10.1071 | 11.5813 | 16.4907 | 18.1432 | 24.5571 | 26.3332 | 29.6539 | 31.3845
14 | 10.111 | 11.6386 | 16.43 | 18.0258 | 24.4183 | 26.1862 | 29.5677 | 31.3121
20 | 10.0754 | 11.5937 | 16.417 | 18.0258 | 24.4047 | 26.1862 | 29.4723 | 31.2096
28 | 10.0865 | 11.5174 | 16.5035 | 18.1696 | 24.4709 | 26.2184 | 29.5427 | 31.2835
35 | 10.1345 | 11.6793 | 16.5364 | 18.2096 | 24.6431 | 26.4205 | 29.6046 | 31.2956
40 | 10.1421 | 11.6806 | 16.6051 | 18.2774 | 24.6897 | 26.4279 | 29.6965 | 31.5313
49 | 10.2045 | 11.8414 | 16.7095 | 18.397 | 24.9946 | 26.8793 | 29.9407 | 31.8352
56 | 10.2563 | 11.7984 | 16.8967 | 18.6743 | 25.2052 | 27.1417 | 30.1699 | 32.2212
70 | 10.4492 | 12.1611 | 17.1174 | 18.8923 | 25.6341 | 27.8008 | 30.5748 | 32.7541
1st
2nd
3rd
4th
 | MCS2 |  | MCS4 |  | MCS7 |  | MCS9 | 
D_TM | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER
20 | 10.0687 | 11.5728 | 16.4432 | 18.0838 | 24.4167 | 26.202 | 29.4587 | 31.1477

## Slide 15: 2x2 2ss in DNLoS

## Slide 16: Performance Summary in 2x2 2ss DNLoS
Lowest SNR values in each column has background colors
Option 1: with segment parsing
Option 2: without segment parsing
  Lowest SNR values are mainly at DTM = {10,14,20,28}
The difference between Option 1 and option 2 (with optimal DTM) is negligible
1st
2nd
3rd
4th
 | MCS2 |  | MCS4 |  | MCS7 |  | MCS9 | 
D_TM | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER
10 | 12.7462 | 14 | 20.5927 | 21.926 | 29.0163 | 30.5294 | 34.5803 | 36.6396
14 | 12.757 | 14.0129 | 20.5669 | 21.8604 | 28.7513 | 30.2369 | 34.1769 | 36.6223
20 | 12.7429 | 14.0066 | 20.5538 | 21.8591 | 28.9671 | 30.4924 | 34.1662 | 36.7519
28 | 12.7954 | 14.06 | 20.5421 | 21.7771 | 28.9863 | 30.6444 | 34.2709 | 36.7179
35 | 12.8139 | 14.07 | 20.6606 | 22.0419 | 29.1666 | 30.8448 | 34.3218 | 36.8023
40 | 12.8782 | 14.1497 | 20.82 | 22.3228 | 29.3757 | 31.1547 | 34.6139 | 37.2041
49 | 12.9839 | 14.3183 | 20.9021 | 22.4197 | 29.6765 | 31.4634 | 34.7158 | 37.033
56 | 13.0588 | 14.3951 | 21.1601 | 22.7512 | 30.0123 | 31.7701 | 35.0795 | 37.322
70 | 13.3133 | 14.6448 | 21.4893 | 23.1058 | 30.3738 | 32.3262 | 35.5009 | 37.909
 | MCS2 |  | MCS4 |  | MCS7 |  | MCS9 | 
D_TM | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER
20 | 12.754 | 14.0427 | 20.5422 | 21.8314 | 28.9255 | 30.4621 | 34.1311 | 36.6819

## Slide 17: 4x4 3ss in DNLoS

## Slide 18: Performance Summary in 4x4 3ss DNLoS
Lowest SNR values in each column has background colors
Option 1: with segment parsing
Option 2: without segment parsing
  With MMSE receiver, performance is impaired by inter-stream interference and performance trend at high MCS is not very reliable
  For MCS2, lowest SNR values are mainly at DTM = {14,20,28,35}
The difference between Option 1 and option 2 (with optimal DTM) is negligible
1st
2nd
3rd
4th
 | MCS2 |  | MCS4 |  | MCS7 |  | MCS9 | 
D_TM | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER
10 | 12.1808 | 12.8901 | 18.8647 | 19.9099 | 26.9774 | 29.2802 | 41.8064 | 47.3992
14 | 12.1392 | 12.8096 | 18.7667 | 19.7641 | 26.7168 | 28.7063 | 41.7485 | 47.3994
20 | 12.143 | 12.8609 | 18.808 | 19.8178 | 26.6486 | 28.9639 | 41.7888 | 47.1982
28 | 12.1484 | 12.8536 | 18.728 | 19.6657 | 26.7082 | 28.7532 | 41.6509 | 47.4572
35 | 12.1557 | 12.8218 | 18.8246 | 19.8748 | 26.7169 | 28.9972 | 41.8759 | 47.5544
40 | 12.184 | 12.9571 | 18.7852 | 19.7676 | 26.7651 | 29.3752 | 41.725 | 47.5277
49 | 12.1883 | 12.9136 | 18.7736 | 19.7162 | 26.8507 | 29.276 | 41.5004 | 47.1816
56 | 12.2302 | 12.9993 | 18.9316 | 20.0469 | 26.8088 | 28.8984 | 41.7364 | 47.5088
70 | 12.2817 | 13.0285 | 19.0794 | 20.3432 | 26.9236 | 29.0566 | 41.7203 | 47.227
 | MCS2 |  | MCS4 |  | MCS7 |  | MCS9 | 
D_TM | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER
20 | 12.131 | 12.8165 | 18.8272 | 19.8644 | 26.6799 | 29.0819 | 41.8091 | 47.404

## Slide 19: 1x1 in UMi-NLoS

## Slide 20: Performance Summary in 1x1 UMi-NLoS
Lowest SNR values in each column has background colors
Option 1: with segment parsing
Option 2: without segment parsing
  For MCS2/4/7/9, lowest SNR values are mainly at DTM = {10,14,20,28}
The difference between Option 1 and option 2 (with optimal DTM) is negligible
1st
2nd
3rd
4th
 | MCS0 |  | MCS2 |  | MCS4 |  | MCS7 |  | MCS9
D_TM | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 3% PER | SNR @ 10% PER | SNR @ 6% PER | SNR @ 10% PER
10 | 3.1035 | 5.562 | 10.5853 | 14.702 | 17.3817 | 19.9669 | 25.9438 | 28.6178 | 31.9935
14 | 3.0955 | 5.533 | 10.6482 | 14.8517 | 17.3373 | 19.9476 | 25.8612 | 27.9552 | 32.1886
20 | 3.0982 | 5.484 | 10.6481 | 14.5155 | 17.3999 | 20 | 25.9233 | 27.9312 | 32.2655
28 | 3.0982 | 5.484 | 10.6366 | 14.7989 | 17.4874 | 19.9534 | 26.0612 | 28 | 32.3817
35 | 3.0793 | 5.479 | 10.6962 | 14.6905 | 17.5324 | 20.1916 | 26.3285 | 28.6533 | 32.546
40 | 3.0681 | 5.425 | 10.6821 | 14.8465 | 17.6001 | 20 | 26.5103 | 28.6224 | 32.8622
49 | 3.0859 | 5.410 | 10.7187 | 14.5986 | 17.6823 | 20.3102 | 26.6581 | 29.2865 | 33.2277
56 | 3.0473 | 5.439 | 10.7893 | 14.9424 | 17.7682 | 20.5035 | 26.7549 | 29.5674 | 33.3638
70 | 3.0708 | 5.427 | 10.8452 | 14.9576 | 17.8651 | 20.6247 | 26.974 | 29.6128 | 33.4515
 | MCS0 |  | MCS2 |  | MCS4 |  | MCS7 |  | MCS9
D_TM | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 1% PER | SNR @ 10% PER | SNR @ 3% PER | SNR @ 10% PER | SNR @ 6% PER | SNR @ 10% PER
20 | 3.0945 | 5.4574 | 10.6525 | 14.6905 | 17.3819 | 19.9656 | 25.9185 | 27.9579 | 31.9573

## Slide 21: Summary
Two options of LDPC tone mapping design are studied for 2x996 tone size RU used in 160/80+80MHz transmission
Results show that similar performance are achieved with or without segment parser
The segment parsing based solution, option 1, is preferred for its implementation benefit
  Same design as in 11ac
  Contiguous 160MHz and non-contiguous 80+80MHz implementation interoperable
  Hardware reuse makes the implementation simpler

## Slide 22: Straw-poll
Do you support to add the following text to 11ax SFD?
  2x996RU employs a segment parser (as in 11ac) between two 996 tones (frequency segments) and the LDPC tone mapper in each 996 tone segment uses DTM=20
Y/N/A

## Slide 23: References
[1] IEEE 802.11-15/0816r0 Interleaver and Tone Mapper for OFDMA
[2] IEEE 802.11-15/0580r2 11ax Coding Discussion
Lin Yang, Bin Tian (Qualcomm)