## Slide 1: Scheduled Trigger frames – Follow up
Name | Affiliation | Address | Phone | Email
Alfred Asterjadhi | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alice Chen |  | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Date: 2015-11-08

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Zhou Lan |  |  |  | Zhou.lan@mediaTek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 8: Authors (continued)
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 9: Introduction
The following concepts are present in the TGax SFD:
  “The spec shall include a mechanism that allows a target transmission time for a Trigger frame to be indicated. The mechanism is based on implicit TWT operation and additionally enables:
    Broadcast triggered TWT by including a TWT element in the Beacon
    Solicited triggered TWT by using implicit TWT negotiation procedure
    When the broadcast triggered TWT is enabled, STA and AP may exchange TWT request/response to indicate the target Beacon frame to be monitored by the PS STA.”
  “The spec shall indicate cascaded sequence of Trigger frames for random access by using a bit in the Trigger frame.”
In this presentation we follow up with enhancements to TWT:
  Using some straightforward or existing concepts approved in the SFD

## Slide 10: Summary: TWT modes
Solicited TWT mode:
  Non-AP STA and AP negotiate implicit TWT session(s)
  Non-AP STA follows the TWT schedule(s) of established TWT session(s)
    During a TWT session, re-negotiations and terminations are performed via unicast frames
    Note: spec will rely on the implicit TWT procedure, with certain additions for triggered TWT signaling
Broadcast TWT mode:
  AP includes TWT element in the Beacon to specify the implicit TWT parameters for the beacon interval (BI)
  Non-AP STAs that could read the Beacon use the broadcast TWT schedule(s) during the BI
Both modes inherit and use implicit TWT signaling provided by TWT element:
  One additional bit in the TWT element indicates that a Trigger frame is sent at the start of each TWT SP
 | B0 | B1 B3 | B4 | B5 | B6 | B7 B9 | B10 B14 | B15
 | TWT Request | TWT Setup Command | Reserved Triggered | Implicit | Flow Type | TWT Flow Identifier | Wake Interval Exponent | TWT Protection
Bits: | 1 | 3 | 1 | 1 | 1 | 3 | 5 | 1
 | Element ID | Length | Control | Request Type | Target Wake Time | TWT Group Assignment | Nominal Minimum Wake Duration | TWT Wake Interval Mantissa | TWT Channel | NDP Paging (optional)
Octets: | 1 | 1 | 1 | 2 | 8 or 0 | 9 or 3 or 0 | 1 | 2 | 1 | 0 or 4
TWT element
TWT parameter set

## Slide 11: TWT Flow Identifier field
Quoting from IEEE802.11ah D5.0:
  “The TWT Flow Identifier subfield contains a 3-bit value which identifies the specific information for this TWT request uniquely from other requests made between the same TWT requesting STA and TWT responding STA pair.”
However, in broadcast TWT mode there is no concept of STA’s pair
  Hence, we can use this field to specify different flows for the broadcast TWT
Proposal 1: In a TWT IE contained in Beacon the TWT Flow Identifier indicates a flow type
  For example, as listed in the table below:
 | B0 | B1 B3 | B4 | B5 | B6 | B7 B9 | B10 B14 | B15
 | TWT Request | TWT Setup Command | Triggered | Implicit | Flow Type | TWT Flow Identifier | Wake Interval Exponent | TWT Protection
Bits: | 1 | 3 | 1 | 1 | 1 | 3 | 5 | 1
Request Type
in TWT IE
TWT Flow ID value | Flow Type for broadcast TWT
0 | No constrains on the type of frame that can be exchanged
1 | Only frames that contain feedback/management can be exchanged (ps-poll, CQI, buffer status, sounding, action, etc.). If trigger TWT then Trigger frame contains no RUs for random access.
2 | Only frames that contain feedback/mgmt. can be exchanged (ps-poll, CQI, buffer status, sounding, action, pre-association frames, etc.). If trigger TWT then Trigger frame contains at least one RU for random access [1].
3 | QoS-constrained frames (e.g., short frames of a particular AC/type etc.)
… | TBD

## Slide 12: Broadcast TWT with multiple TWTs
AP indicates target trigger time(s) in TWT IE included in the Beacon [1]
  The pattern can be periodic
    TWT element contains TWT field and TWT Wake Interval which already enables it
  The pattern can be aperiodic
    Currently TWT element can signal only one of this target wake time. To add flexibility per BI we may want to enable signaling for more than one (aperiodic) TWT.
Proposal 2: Enable more than one TWT parameter set in the Beacon
  The TWT element is modified so that it carries multiple TWT parameter sets
    I.e., the TWT IE carries multiple occurrences of the fields that follow the Control field
      Length field of the TWT element already provides the necessary signaling to determine its content
  Provides full flexibility for signaling multiple TWTs in the TWT IE
Beacon
TF
Next TWT
Beacon
TF
TF
TF
TWT IE
TWT Wake Interval
DL/ULMU
DL/ULMU
DL/ULMU
DL/ULMU
Next TWT
Next TWT
Aperiodic
Periodic
(Valid for BI)

## Slide 13: Cascaded field in Trigger frame
AP specifies the STAs expected to wake at the TWT in the TWT IE in the Beacon
  Generally the AP overestimates the number of STAs to be allocated in the TWT SP
    This is natural with broadcast TWT, as only a portion of STAs will likely be served during the TWT SP
      Note: It is also possible with solicited TWT
The AP sends a Trigger frame at the start of the TWT SP
  The Trigger frame contains the list of AIDs of the STAs that are enabled to transmit in UL
    It also contains a Cascaded field [2] that indicates if an additional Trigger frame follows in the TWT SP
A non-AP STA that receives a Trigger frame during a TWT SP
  Transmits an UL frame as a response to the Trigger frame intended to it
  Continues to be Awake if the Trigger is not intended to it and has the Cascaded field equal to 1
  May go to Doze if the Trigger frame is not intended to it and has the Cascaded field equal to 0
Beacon
TF
Next TWT
TWT IE:
Implicit TWT,
Next TWT,
TWT Wake Interval
TWT Service Period
STA 4
STA 3
STA 2
STA 1
TF
STA 7
STA 3
STA 6
STA 5
Cascade = 1
Cascade = 0
MBA
MBA
PIFS or more
Random RU
Allocated RU

## Slide 14: Summary
We propose:
  Certain enhancements to the TWT IE for added flexibility in broadcast TWT
  Unify scheduling mechanisms independently of the type of trigger frame
  Define the use of the Cascaded field in the Trigger frame for non-random access cases

## Slide 15: Straw Poll 1
Do you support to add to the 11ax SFD:
  The TWT Flow Identifier field in the TWT IE included in the Beacon frame specifies the different types of flows allowed during the TWT SP

## Slide 16: Straw Poll 2
Do you support to add to the SFD:
  Multiple TWTs can be indicated in the TWT IE in the Beacon frame by allowing multiple TWT parameter sets in the same TWT IE

## Slide 17: Straw Poll 3
Do you support to amend the existing text in the 11ax SFD as follows:
  The spec shall indicate cascaded sequence of Trigger frames for random access by using a bit in the Trigger frame.

## Slide 18: References
[1] A. Asterjadhi (Qualcomm) et. al., 11-15-0880-02-00ax-Scheduled Trigger frames
[2] C. Ghosh (Intel) et. al., 11-15-1107-00-00ax-power-save-with-random-access