## Slide 1: Link Adaptation for HE WLAN
Date: 2015-11-09
Authors:

## Slide 2: Background
Link adaptation has been adopted to fully exploit channel variations and facilitate the best possible QoS.
For 11ax, UL/DL OFDMA and HE variant of HT control field have been discussed for efficient exchange of data and control information between AP and HE-STAs.
In this submission, several points on link adaptation are discussed.

## Slide 3: Link Adaptation Procedure
Node 1
Node 2
Preamble
Data Frame
+HTC (MRQ, MSI = 3)
Data Frame
+HTC (MFB, MFSI = 3)
Solicit MCS Procedure
Step 1)
Node 1, the MCS requester, sends a PPDU containing MCS request (MRQ) and MCS request sequence number (MSI)
Node 2, the MCS responder, takes CSI measurements from the preamble and uses RXVECTOR properties to compute MCS.
  CSI measurements taken may be beamformed signals and therefore, MCS feedback will be limited to that specific beamforming.
Step 2) Node 2, the MCS responder, report back MCS feedback (MFB) with MCS feedback sequence number (MFSI) set as the same value as MSI of MRQ.
Step 1)
Step 2)

## Slide 4: Link Adaptation in VHT
Solicited feedback based on request from a transmitter.
  MCS feedback (MFB) values are computed from the frame that contained MCS request (MRQ) set to 1.
  MCS feedback Sequence ID (MFSI) field is set with MRQ sequence ID (MSI) value for MCS requester.
Unsolicited feedback.
  Autonomous MFB to the transmitter based on frames that the receiver has chose to measure.
  Some basic description (e.g.GID, Coding Type, STBC, FB Tx type etc) about the frame is conveyed. This facilitates identification of the frame (or at least the RXVECTOR of the frame) that MCS measurement has taken place.

## Slide 5: Issues of Link Adaptation in HE
Information needed for Unsolicited MCS feedback for 11ax
Reference for MCS feedback
Duplication of SNR and MCS
Limited space for HE variant of HT Control Field

## Slide 6: Information Needed for Unsolicited MCS Feedback
Additional information is needed for Unsolicited MCS feedback to facilitates identification of the frame that MCS was measured on.
  BW (2 bits), GID (6 bits), Coding (1 bit), BF (1 bits), STBC (1 bit)
    Note that all the above bit fields are only used in unsolicited MCS feedback. For solicited MCS feedback they are reserved.
With the support of OFDMA and DCM, additional information needs to be conveyed for Unsolicited MCS feedback.
  RU size and RU location (at least 8 bits), DCM (1 bit)
If no GID is supported in 11ax, we may able to remove GID from HE link adaptation. However, we may need additional information for MU-MIMO indication.
  GID not only conveyed information on whether SU or MU-MIMO was used, but also on STA pairing information.

## Slide 7: Information Needed for Unsolicited MCS Feedback (cont.)
GID
BW
Coding
STBC
BF
VHT Unsolicited MCS
HE Unsolicited MCS
Bits
6
2
1
1
1
11 Bits
RU size/location
SU/MU
Coding
STBC
BF
Bits
at least 8
at least 1
1
1
1
DCM
1
at least 13 Bits
If we want to indicate the STA pairing information for MU-MIMO without GID, it would be NSTAID x 4 (or 8). By optimistic estimate (with NSTAID = 4 bits, and maximum 4 users), SU/MU indication will be 16 bits.
MU-MIMO pairing information

## Slide 8: Payload Size Reference for MCS
MCS 3
MCS 1
MCS 7
MCS 5
Required SNR for a given MCS varies significantly based on payload size.
If MCS responder feedback MCS=5, how does the MCS requester know which payload size the MCS is applicable for?

## Slide 9: Payload Size Reference for MCS
Current link adaptation does not provide appropriate MCS reference for a transmitter to utilize the MCS feedback by the responder.
  Received MCS may not be directly applicable to the transmission because payload size may vary due to random traffic characteristics.
With well-defined MCS payload reference, the transmitter may utilize the reported MCS feedback and adjust for the transmission payload size characteristics.

## Slide 10: Payload of Frame with MRQ as Payload References for MCS
For solicited MCS feedback, payload reference for MCS can be the payload of PPDU containing MRQ
  In case PPDU contains multiple MPDU, we will have to define whether payload reference is based on PSDU size (the entire A-MPDU length) or MPDU size.
For unsolicited MCS feedback, this solution is difficult to apply directly
  VHT link adaptation parameters in HT Control field does not give sufficient information to determine the reference payload size of the MCS feedback.
  We will need to devise new mechanism to allow unsolicited MCS feedback to uniquely identify the reference payload size.
Node 1
Node 2
Preamble
+HTC (MRQ =1, MSI = 3)
PSDU 1000 bytes
+HTC (MFB, MFSI = 3)
MCS based on1000 bytes
Solicit MCS Procedure
Data Frame
Adjust MCS (from reported MCS) to a different payload size
time
time

## Slide 11: Fixed Payload References for MCS (Fixed in Specifications)
Good starting point for reference for Solicited and unsolicited MCS:
  Minimum sensitivity definitions in Section 22.3.18.1
    The packet error ratio (PER) shall be less than 10% for a PSDU length of 4096 octets with the rate dependent input levels listed in Table 22-23 (Receiver minimum input level sensitivity)
    Required minimum level of a WLAN signal that receiver will detect and demodulate
Problems with PSDU
  Some PSDU sizes cannot be supported in certain MCS and RU allocation sizes. PSDU must be a integer multiple of NDBPS parameter. PSDU per OFDM symbol (NDBPS) calculations are shown in the Appendix.
  Achieving 10% PER for a PSDU should not be the target for MCS. PSDU may contain multiple MPDUs (in A-MPDU). We have block ACK to cope with selective retransmission of MPDUs. So PSDU does not reflect the retransmission unit of 802.11 systems.
Alternative reference: MPDU size

## Slide 12: Fixed Payload References for MCS (cont.)
Potential MCS reference:
  The reported MCS in MFB corresponds to the highest data-rate for a given RU size and number of spatial streams (i.e. Nss) that results in MPDU error rate of X % or lower for a MPDU length of Y octets.
Possible Values for “X”, “Y”
  X = 10%
  Y = 3895 (maximum MPDU limit for VHT, see appendix)
  Note that these are not actual PER values used in the system, but simply a reference for all vendors to understand MCS. Each vendor may use the reported MCS and transform it to effective SNR to be used for different system target settings

## Slide 13: MCS and SNR in HE Link Adaptation
VHT link adaptation contains both MCS and SNR subfield.
MCS and SNR subfield convey somewhat duplicate information.
SNR subfield (6 bits) is defined as mean value of all the SNR values (frequency and spatial stream) in dB-scale.
Because SNR subfield is a log-average of SNR values (over all frequency and spatial domain), it does not reflect channel capacity correctly.
Example formulation
4 bits
6 bits

## Slide 14: Log-Average SNR and Link Quality
Packet #k
TX
RX
Step 1)
Measure effective SNR #k
Record Packet #k Pass/Fail
…
12.10
12.15
SNR [dB]
…
12.05
12.20
log-average
SNR
Packet
Pass/Fail
Find SNR belonging to this SNR range
Record short-term PER
Step 2)
Measure log-average SNR #k
Run simulation for 100,000 packets

## Slide 15: Log-Average SNR and Link Quality (cont.)
When average SNR (in dB-scale) is plotted against AWGN performance, it doesn’t quite reflect link quality (i.e. packet error rate).
Ideally a link quality metric should always refer to the same PER for a give value (a single point in line). The instantaneous PER shows that the log-average PER widely varies packet to packet. Making it unreliable for link quality measurement.
Instantaneous PER shows the PER based on measured effective SNR of packet #k (using RBIR mapping function) vs. measured log-average SNR of packet #k
Note:
Did not plot any results with accumulative error less than 25 frames.

## Slide 16: Log-Average SNR and Link Quality (cont.)
Similar results with different MCS configuration
Usefulness of average SNR for link adaptation purposes is questionable.
Instantaneous PER shows the PER based on measured effective SNR of packet #k (using RBIR mapping function) vs. measured log-average SNR of packet #k
Note:
Did not plot any results with accumulative error less than 25 frames.

## Slide 17: Limited Bit Space for HE Link Adaptation
There are some proposals that allow to multiplex different control information in the HE variant of the HT control field [1].
With such bit field structure, HE link adaptation may only have maximum of 24 bits (3 Bytes).
Given that unsolicited MCS feedback for 11ax requires even more bits compared with 11ac, there will be some challenges to the link adaptation bit field design.
We may need to consider removal of some field from HE link adaptation, such as SNR subfield, RDG subfields, etc.
Control ID
VHT (1)
HE (1)
Ctrl. Info.
EOH (0)
B2 B6
B7
B0
B1
variable
Reserved value indicates
HE A-Control variant of HT Control field
…
HE A-Control field
Ref: slide 10 of [1]

## Slide 18: Proposed MFB Subfield of HE Link Adaptation
Given the limitation of the bit space and limited uses for SNR subfield for HE link adaptation, we propose to define the MFB subfield to be composed of NSS and MCS subfields.
  BW indication in VHT MFB is actually not a feedback. In case of solicited MCS feedback, BW is set to reserved. The BW is used in unsolicited MCS feedback case to identify and characterize the PPDU that MCS was measured on.
The rest of the subfield for HE link adaptation is TBD.
VHT
HT
TBD
HT Control Field
TBD
MFB
HE Link Adaptation Field
MFB subfield
NSS
MCS
3 bits
4 bits

## Slide 19: Conclusion
We have analyzed some required bit subfield of the HE link adaptation.
The MCS definition in 11n and 11ac lacks proper payload size references. We propose to define such reference.
The limited bit space for link adaptation requires TGax to either compress the required information for link adaptation or define alternative solutions (compared with 11ac).

## Slide 20: Straw Poll #1
Do you agree to include the following text to TGax SFD:
HE link adaptation shall define reference payload size for the reported MCS in MFB.
  Reference payload size may be dependent on the frames involved in link adaptation or fixed in specification. Details TBD.
Y/N/A

## Slide 21: Straw Poll #2
Do you agree to include the following text to TGax SFD:
HE link adaptation field, which is part of HE variant of HT control field, consists of MFB and TBD subfields. The MFB subfield is composed of NSS and MCS subfield and shown in figure below.
Y/N/A
TBD
MFB
HE Link Adaptation Field
NSS
MCS
3 bits
4 bits
7 bits
TBD bits

## Slide 22: Straw Poll #3
Do you agree to the following concept:
The reported MCS in MFB corresponds to the highest data-rate for a given RU size and number of spatial streams (i.e. Nss) that results in MPDU error rate of X % or lower for a MPDU length of Y octets.
  X and Y are TBD.
Y/N/A

## Slide 23: Reference
[1] 11-15-1121r0, HE-A-Control Field

## Slide 24: APPENDIX

## Slide 25
Receiver Minimum Input Level Sensitivity

## Slide 26: PSDU per OFDM (NDBPS) Symbol (1/3)
Nss = 1 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 1 | 3 | 4 | 6 | 9 | 12 | 13 | 15 | 18 | 20
 | 52 | 3 | 6 | 9 | 12 | 18 | 24 | 27 | 30 | 36 | 40
 | 106 | 6 | 12 | 19 | 25 | 38 | 51 | 57 | 63 | 76 | 85
 | 242 | 14 | 29 | 43 | 58 | 87 | 117 | 131 | 146 | 175 | 195
 | 484 | 29 | 58 | 87 | 117 | 175 | 234 | 263 | 292 | 351 | 390
 | 996 | 61 | 122 | 183 | 245 | 367 | 490 | 551 | 612 | 735 | 816
 | 1992 | 122 | 245 | 367 | 490 | 735 | 980 | 1102 | 1225 | 1470 | 1633
Nss = 2 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 3 | 6 | 9 | 12 | 18 | 24 | 27 | 30 | 36 | 40
 | 52 | 6 | 12 | 18 | 24 | 36 | 48 | 54 | 60 | 72 | 80
 | 106 | 12 | 25 | 38 | 51 | 76 | 102 | 114 | 127 | 153 | 170
 | 242 | 29 | 58 | 87 | 117 | 175 | 234 | 263 | 292 | 351 | 390
 | 484 | 58 | 117 | 175 | 234 | 351 | 468 | 526 | 585 | 702 | 780
 | 996 | 122 | 245 | 367 | 490 | 735 | 980 | 1102 | 1225 | 1470 | 1633
 | 1992 | 245 | 490 | 735 | 980 | 1470 | 1960 | 2205 | 2450 | 2940 | 3266
Nss = 3 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 4 | 9 | 13 | 18 | 27 | 36 | 40 | 45 | 54 | 60
 | 52 | 9 | 18 | 27 | 36 | 54 | 72 | 81 | 90 | 108 | 120
 | 106 | 19 | 38 | 57 | 76 | 114 | 153 | 172 | 191 | 229 | 255
 | 242 | 43 | 87 | 131 | 175 | 263 | 351 | 394 | 438 | 526 | 585
 | 484 | 87 | 175 | 263 | 351 | 526 | 702 | 789 | 877 | 1053 | 1170
 | 996 | 183 | 367 | 551 | 735 | 1102 | 1470 | 1653 | 1837 | 2205 | 2450
 | 1992 | 367 | 735 | 1102 | 1470 | 2205 | 2940 | 3307 | 3675 | 4410 | 4900
Rounded to nearest byte

## Slide 27: PSDU per OFDM (NDBPS) Symbol (2/3)
Nss = 4 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 6 | 12 | 18 | 24 | 36 | 48 | 54 | 60 | 72 | 80
 | 52 | 12 | 24 | 36 | 48 | 72 | 96 | 108 | 120 | 144 | 160
 | 106 | 25 | 51 | 76 | 102 | 153 | 204 | 229 | 255 | 306 | 340
 | 242 | 58 | 117 | 175 | 234 | 351 | 468 | 526 | 585 | 702 | 780
 | 484 | 117 | 234 | 351 | 468 | 702 | 936 | 1053 | 1170 | 1404 | 1560
 | 996 | 245 | 490 | 735 | 980 | 1470 | 1960 | 2205 | 2450 | 2940 | 3266
 | 1992 | 490 | 980 | 1470 | 1960 | 2940 | 3920 | 4410 | 4900 | 5880 | 6533
Nss = 5 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 7 | 15 | 22 | 30 | 45 | 60 | 67 | 75 | 90 | 100
 | 52 | 15 | 30 | 45 | 60 | 90 | 120 | 135 | 150 | 180 | 200
 | 106 | 31 | 63 | 95 | 127 | 191 | 255 | 286 | 318 | 382 | 425
 | 242 | 73 | 146 | 219 | 292 | 438 | 585 | 658 | 731 | 877 | 975
 | 484 | 146 | 292 | 438 | 585 | 877 | 1170 | 1316 | 1462 | 1755 | 1950
 | 996 | 306 | 612 | 918 | 1225 | 1837 | 2450 | 2756 | 3062 | 3675 | 4083
 | 1992 | 612 | 1225 | 1837 | 2450 | 3675 | 4900 | 5512 | 6125 | 7350 | 8166
Nss = 6 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 9 | 18 | 27 | 36 | 54 | 72 | 81 | 90 | 108 | 120
 | 52 | 18 | 36 | 54 | 72 | 108 | 144 | 162 | 180 | 216 | 240
 | 106 | 38 | 76 | 114 | 153 | 229 | 306 | 344 | 382 | 459 | 510
 | 242 | 87 | 175 | 263 | 351 | 526 | 702 | 789 | 877 | 1053 | 1170
 | 484 | 175 | 351 | 526 | 702 | 1053 | 1404 | 1579 | 1755 | 2106 | 2340
 | 996 | 367 | 735 | 1102 | 1470 | 2205 | 2940 | 3307 | 3675 | 4410 | 4900
 | 1992 | 735 | 1470 | 2205 | 2940 | 4410 | 5880 | 6615 | 7350 | 8820 | 9800
Rounded to nearest byte

## Slide 28: PSDU per OFDM (NDBPS) Symbol (3/3)
Nss = 7 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 10 | 21 | 31 | 42 | 63 | 84 | 94 | 105 | 126 | 140
 | 52 | 21 | 42 | 63 | 84 | 126 | 168 | 189 | 210 | 252 | 280
 | 106 | 44 | 89 | 133 | 178 | 267 | 357 | 401 | 446 | 535 | 595
 | 242 | 102 | 204 | 307 | 409 | 614 | 819 | 921 | 1023 | 1228 | 1365
 | 484 | 204 | 409 | 614 | 819 | 1228 | 1638 | 1842 | 2047 | 2457 | 2730
 | 996 | 428 | 857 | 1286 | 1715 | 2572 | 3430 | 3858 | 4287 | 5145 | 5716
 | 1992 | 857 | 1715 | 2572 | 3430 | 5145 | 6860 | 7717 | 8575 | 10290 | 11433
Nss = 8 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 12 | 24 | 36 | 48 | 72 | 96 | 108 | 120 | 144 | 160
 | 52 | 24 | 48 | 72 | 96 | 144 | 192 | 216 | 240 | 288 | 320
 | 106 | 51 | 102 | 153 | 204 | 306 | 408 | 459 | 510 | 612 | 680
 | 242 | 117 | 234 | 351 | 468 | 702 | 936 | 1053 | 1170 | 1404 | 1560
 | 484 | 234 | 468 | 702 | 936 | 1404 | 1872 | 2106 | 2340 | 2808 | 3120
 | 996 | 490 | 980 | 1470 | 1960 | 2940 | 3920 | 4410 | 4900 | 5880 | 6533
 | 1992 | 980 | 1960 | 2940 | 3920 | 5880 | 7840 | 8820 | 9800 | 11760 | 13066
Rounded to nearest byte

## Slide 29: Maximum Data Unit Sizes in 802.11
 | MSDU | A-MSDU | MPDU | PSDU
Non-HT | 2304 | 3839 or 4065 or 7935 | N/A | 212–1
HT | 2304 | 3839 or 7935 | N/A | 216–1
VHT | 2304 | N/A | 3,895 or 7,991 or 11,454 | 4,692,480