## Slide 1: Secondary Channel CCA of HE STA
Date: 2015-11-09
Authors:

## Slide 2: Background
11ax needs to define wide channel access rules, especially CCA procedures in secondary channels.
The following issues should be considered when designing secondary channel CCA procedures
  HE STA can apply dynamic CCA threshold (OBSS_PD) when detecting OBSS PPDU in the primary channel [1].
  Within PIFS duration, it is hard to detect HE PPDU using the current mid-packet CCA method [2][3].
In this contribution, we discuss secondary channel CCA procedure of HE STA
  Energy Detection within PIFS duration
  Legacy PPDU Detection within PIFS duration
  HE PPDU Detection within TBD duration
  CCA thresholds

## Slide 3: Secondary Channel CCA in VHT
22.3.19.5.4 CCA sensitivity for signals not occupying the primary 20 MHz channel
The PHY shall issue a PHY-CCA.indication(BUSY, {secondary}) if the conditions for issuing PHY- CCA.indication(BUSY, {primary}) are not present and one of the following conditions are present in an otherwise idle 40 MHz, 80 MHz, 160 MHz, or 80+80 MHz operating channel width:
— Any signal within the secondary 20 MHz channel at or above a threshold of –62 dBm within a period of aCCATime after the signal arrives at the receiver’s antenna(s); then the PHY shall not issue a PHY-CCA.indication(BUSY ,{secondary40}), PHY-CCA.indication(BUSY ,{secondary80}), or PHY-CCA.indication(IDLE) while the threshold continues to be exceeded.
— A 20 MHz NON_HT, HT_MF, HT_GF or VHT PPDU detected in the secondary 20 MHz channel at or above –72 dBm with >90% probability within a period aCCAMidTime (see 22.4.4).
Preamble
Data
Preamble
AIFS
Primary
20MHz
Secondary
20MHz
PIFS
PPDU Detection (-72dBm)
Energy Detection (-62dBm)
OBSS PPDU
PPDU Detection
Energy Detection
Legacy PPDU
Short GI: 6.94 Symbols
Long GI: 6.25 Symbols
Any signal
25us

## Slide 4: Energy Detection
Energy Detection in Secondary Channels
  Detection of any signal at or above -62dBm within PIFS before transmission
  HT and VHT STA perform Energy Detection in secondary channels
  HE PPDU (12.8us+GI symbol) will be detected with energy detection threshold by legacy STAs
  HE STA should detect any signal in secondary channels with the same energy detection threshold as legacy STAs
  However, with Energy Detection only, nearby BSSs with different Primary Channels will experience severe interferences
Preamble
Data
Preamble
AIFS
Primary
20MHz
Secondary
20MHz
PIFS
Energy Detection (-62dBm)
Any signal
25us

## Slide 5: Legacy PPDU Detection
Legacy PPDU Detection in Secondary Channels
  Detection of Legacy PPDU (3.2us+GI symbol) at or above -72dBm within PIFS before transmission [2]
  VHT STA performs Legacy PPDU Detection to protect OBSS transmissions in secondary channels better than Energy Detection
  VHT STA applies the intermediate threshold level (-72dBm) considering the unfairness from HT STA’s ED threshold (-62dBm) [4]
    It is the same case because HE PPDU is only protected with ED threshold from Legacy STAs
  Following the decision of VHT, HE STA should also implement Legacy PPDU detection and at least apply the same threshold of -72dBm
Preamble
Data
Preamble
AIFS
Primary
20MHz
Secondary
20MHz
PIFS
Legacy PPDU Detection
OBSS PPDU
3.2us+GI Symbols
Short GI: 6.94 Symbols
Long GI: 6.25 Symbols
25us

## Slide 6: HE PPDU Detection
HE PPDU Detection in Secondary Channels
  Detection of HE PPDU (12.8us+GI symbol) by using the GI correlation based detection method [2]
    We need further study on the required duration to detect 4x symbols with acceptable error rates
    If TBD duration is longer than AIFS, HE PPDU detection can be optionally performed only when TBD duration is secured from the Primary Channel’s backoff count
  HE STA should protect OBSS HE PPDU in its secondary channels
    When two HE BSSs utilize different Primary Channels, each BSS should protect each others’ HE PPDUs on Secondary Channels
    Future Wi-Fi standards will utilize 4x OFDM symbols, therefore 11ax needs to define proper detection procedures to avoid much collisions on secondary channels
Preamble
Preamble
AIFS
TBD duration
PIFS
HE PPDU Detection
Data
Primary
20MHz
Secondary
20MHz
OBSS PPDU
25us
TBD duration
12.8us+GI Symbols

## Slide 7: CCA thresholds
Secondary Channel’s CCA threshold should be proportional to OBSS_PD
  Case 1) When PPDU is present in Primary Channel
    Secondary channel’s CCA is performed when the PPDU is detected as OBSS PPDU and its RSSI is below OBSS_PD in the primary channel.
    Secondary Channel’s CCA threshold should be proportional to OBSS_PD. Otherwise, spatial reuse transmission attempt would be blocked from secondary channel’s low threshold.
  Case2) When PPDU is NOT present in Primary Channel
    Any PPDU detected in secondary channels is OBSS PPDU.
    If the PPDU’s RSSI is below OBSS_PD, the secondary channel’s CCA should indicate IDLE channel for spatial reuse transmission.
Further consideration of Legacy STAs
  If Legacy PPDU is detected in the secondary channel, HE STA should apply the maximum of -72dBm and OBSS_PD for fairness with VHT STAs
  If HE PPDU is detected in the secondary channel, HE STA should apply OBSS_PD in accordance with the primary channel
Preamble
Preamble
AIFS
Apply OBSS_PD
Primary
20MHz
Secondary
20MHz
OBSS PPDU
TBD
AIFS
PIFS
Data
Detects
OBSS PPDU
TBD
Preamble
Data
Preamble
AIFS
Apply OBSS_PD
PIFS
OBSS PPDU
No PPDU
Apply OBSS_PD

## Slide 8: Summary
PIFS duration for legacy PPDU detection
  Energy Detection unchanged
  Legacy PPDU Detection should apply Max(-72dBm, OBSS_PD) CCA threshold in the secondary channel
  (PIFS is enough duration to detect Legacy PPDU, but not enough to detect HE PPDU)
Extended duration for HE PPDU detection
  Extended TBD duration to detect HE PPDU if the duration is available
  HE PPDU Detection should apply (OBSS_PD) CCA threshold in the secondary channel
Preamble
Preamble
AIFS
TBD duration
PIFS
HE PPDU Detection (OBSS_PD)
Energy Detection (-62dBm)
Legacy PPDU Detection (Max(-72dBm, OBSS_PD))
Data
Primary
20MHz
Secondary
20MHz
OBSS PPDU
25us
TBD duration

## Slide 9: Conclusions
11ax needs to define wide channel access rules, especially CCA procedures in secondary channels.
In this submission, we provide a framework for 11ax secondary channel CCA procedure as:
  Mandatory PIFS duration to detect Legacy PPDU or any signal
  Optional TBD duration to detect HE PPDU (if the duration is available)
  Applying OBSS_PD threshold in secondary channels

## Slide 10: Straw poll - 1
  Do you agree to add the following text into 11ax SFD ?
5.x HE STA shall have the same Energy Detection capability as VHT STA in secondary channels.
  Y/N/A

## Slide 11: Straw poll - 2
  Do you agree to add the following text into 11ax SFD ?
5.x HE STA shall detect Legacy PPDU in secondary channels at or above TBD thresholds within PIFS before transmission.
  Note: Legacy PPDU is NON_NT, HT_MF, HT_GF or VHT PPDU.
  Y/N/A

## Slide 12: Straw poll - 3
  Do you agree to add the following text into 11ax SFD ?
5.x HE STA may detect HE PPDU in secondary channels at or above TBD thresholds within TBD duration before transmission.
  Y/N/A

## Slide 13: References
  [1] 11-15/0132r9, Spec Framework Doc
  [2] 11-10/0012r0, Enhanced CCA for Non-Primary Channels Using Guard Interval
  [3] 11-15/1228r2, Issues on 256-FFT per 20MHz
  [4] 11-11/0061r0, CCA Threshold Levels