## Slide 1: NDP Announcement for HE Sequence
Date: 2015-11-11
Authors:

## Slide 2: Abstract
This presentation questions the necessity of signaling in the NDP Announcement frame, the presence of trigger frame for HE DL sounding sequence.

## Slide 3: VHT DL Sounding Sequence
9.31.5.2 [1]
  If the STA’s AID is in the first (or only) STA Info field, then it shall transmit the feedback a SIFS after the VHT NDP. The other STAs in the STA Info field will be polled.
VHT NDP-A
NDP
VHT Compressed Beamforming
Beamforming Report Poll
VHT Compressed Beamforming
Beamforming Report Poll
VHT Compressed Beamforming
AP
STA 1
STA 2
STA 3
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS

## Slide 4: HE DL Sounding Sequence
We have the following in the current SFD [2]:
Figure 14 -- Illustration of DL Sounding Sequence
NDP-A is the initiation frame for the HE DL Sounding process.
Trigger frame is used to solicit the STAs to send their Beamforming feedback frame using the UL MU mode

## Slide 5: Trigger frame in HE DL Sounding Sequence
HE DL Sounding sequence:
  Beamforming frames sent in UL MU PPDU by all the STAs solicited by the Trigger frame
  Is this the only way to receive feedback from STAs?
AP may also want to obtain the feedback frames one-by-one/ successively from each STA
  Similar to the VHT sounding sequence
  For robustness sake
  The combination of target STAs that are triggered may not be appropriate for UL-MU.

## Slide 6: If HE DL Sounding Sequence with Trigger Frame?
The amendment shall define a new shall follow a channel sounding sequence (Refer Fig. 14) initiated by an HE AP that includes a trigger information frame, a SIFS after NDP frame, in order to facilitate UL MU mode of Compressed Beamforming Action frame from multiple HE STAs.
[MU Motion 18, September 17, 2015]
Figure 14 -- Illustration of DL Sounding Sequence
[MU Motion 20, September 17, 2015]

## Slide 7: No Trigger frame in HE DL Sounding Sequence
If such a sequence is allowed for HE DL sounding procedure, need a mechanism to distinguish this sequence from the one with Trigger frame
  The arrival of Trigger frame after NDP frame is not known to the STAs until the actual start time of the Trigger frame
This case is different from multiplexing of BA/ACK responses for DL data
  Trigger frames are aggregated with the data frames
HE
NDP-A
HE NDP
HE Compressed Beamforming
Beamforming Report Poll
HE Compressed Beamforming
Beamforming Report Poll
HE Compressed Beamforming
AP
STA 1
STA 2
STA 3
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
To allow such sequence, a signaling bit is necessary in the HE NDP Announcement frame.

## Slide 8: Summary
The necessity to enable successive feedback response in HE DL sounding sequence was considered.
A signaling bit in the HE NDP Announcement frame to distinguish between the sequence with a trigger frame is necessary.

## Slide 9: References
[1] IEEE Std 802.11ac-2013
[2] 802.11-15/0132r9 “Specification Framework for TGax”

## Slide 10: Straw Poll 1
Do you agree to add a sequence similar to the VHT sounding sequence that does not include a trigger frame and where the sounding feedback frames are sent in SU PPDUs for HE DL sounding sequence?
Y:N:A =
HE
NDP-A
HE NDP
HE Compressed Beamforming
Beamforming Report Poll
HE Compressed Beamforming
Beamforming Report Poll
HE Compressed Beamforming
AP
STA 1
STA 2
STA 3
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS

## Slide 11: Straw Poll 2
Do you agree to amend the following text in the SFD as follows?:
4.6. Lines 47-49
The amendment shall define a new shall follow a channel sounding sequence (Refer Fig. 14) initiated by an HE AP that includes a trigger information frame, a SIFS after NDP frame, in order to facilitate UL MU mode of Compressed Beamforming Action frame from multiple HE STAs

## Slide 12: Straw Poll 3
Do you agree to add the following text to the SFD?:
4.6 The amendment shall define a mechanism to signal the presence of a trigger frame, a SIFS interval after the NDP frame in the HE DL sounding sequence. When there is no trigger frame, the sounding feedback frames are sent in SU PPDUs same as in the VHT sounding sequence.
Y:N:A =