## Slide 1: Long range low power Use Cases for Indoor & Outdoor
Date: 2015-11-09
Authors:

## Slide 2: Abstract
IoT is expected to be one of the most significant drivers of growth in technology markets
802.11 community has not seriously considered supporting IoT applications so far
In this presentation, we list various IoT use cases for indoor/outdoor and requirements for them

## Slide 3: Characteristics for IoT Devices
 | Has data input and output? | Radio Trans. Tech. (WLAN/WPAN) | Data Speed | Power Limited
Central Controller | I, O | L, P | W.-Control | 
Set-top Box | I, O | L, P | W-UHD | 
Home Theater | I, O | L, P | W-UHD, W-Audio | 
Display, TV | I | L, P | W-UHD | 
Speaker | I | P | W-Audio | 
Door, Window Sensor | O | P | W.-Control | Y
Gas Sensor | O | P | W.-Control | Y
Smoke Sensor | O | P | W.-Control | Y
Gas Valve Sensor/Controller | I, O | P | W.-Control | Y
Heater/Air conditioner | I, O | L, P | W.-Control | 
Home Appliances | I, O | L, P | W-Data | 
Surveillance Camera | I, O | L, P | W-Video, W.-Control | 
Printer/Scanner | I, O | L, P | W-Data, W-Control | 
Wireless UHD: 10’s Gbps, Low latency
Wireless Video: 10-100Mbps, Low latency
Wireless Audio: Below 1Mbps, Low latency
Wireless Data: Below 10Mbps
Wireless Control: Below 1Mbps

## Slide 4: Use case for home theater (1)
Home theater devices are associated with the LRLP AP
Home theater
Speakers
TV
Set top box
LRLP for control
data
Controller (indoor mobile device)
LRLP AP

## Slide 5: Use case for home theater (2)
The central controller is most likely a mobile device
Pairing is performed through an LRLP AP by the central controller (mobile device)
After connection setup, either Wi-Fi Direct or Bluetooth may be used for user data transfer between non-AP STAs

## Slide 6: Use case for home security (1)
Door/window sensor, Gas sensor, Smoke detector, home appliances
Window
Smoke detector
Gas sensor
Door
LRLP for control
LRLP AP
Home appliances
Outdoor
mobile device
mobile+cable modem/xDSL
for control

## Slide 7: Use case for home security (2)
Any abnormal state sends an alarm to the mobile device
Requirements
  Fast wakeup time: From a dormant state, the communication must be reestablished quickly through bypassing login procedure, pairing, DHCP, etc.
  Reconnection procedure must be secure as well

## Slide 8: Use case for indoor device control
Gas value controller, Heater/AC, Home appliances, Surveillance cameras
Heater
A/C
Gas valve
controller
control
LRLP AP
Controller (outdoor
mobile device)
Washing machine
LTE+cable modem/xDSL
for control

## Slide 9: Use case for manufacturing (1)
Data collection from sensors in a manufacturing house
A chip maker is an example
Vibration sensor
Vibration sensor
LRLP AP
LRLP data collection
Wired/wireless connection
Data analysis server

## Slide 10: Use case for manufacturing (2)
A chip maker monitors the vibration pattern from various facilities
Use the collected data to predict possible failures of the facilities
Reduces downtime of manufacturing process and improves the yield

## Slide 11: Use case for manufacturing (3)
Requirements
  The stable data rate must be maintained even in multipath environment due to the dense and interfering facilities
  The number of sensors connected to the LRLP AP at the same time must be large enough
  To extend the coverage, an LRLP AP may be connected to another LRLP AP (multihop) and adaptive route selection between a server and sensors for multihop environment
  A connection between sensors and an analysis server must be secure
  Fast wakeup time on sensor devices
  Lightweight and low-power authentication scheme for sensors

## Slide 12: Summary
For home theater use case, pairing between LRLP STAs is performed through LRLP AP by a mobile device (an LRLP STA in the same indoor) for direct connection between A/V devices
For home security use case, fast wakeup and secure reconnection for LRLP STAs are required
For indoor device control use case, a mobile device can control the indoor devices collocated with LRLP STAs
For manufacturing house, the connection should not be interfered by the manufacturing facilities, multihop is supported, and authentication is light