## Slide 1: PAD and Probe Request/Response frames
Date: 2015-11-11
Authors:

## Slide 2: Abstract
Number of comments received for P802.11aq/D3.0 identified potential issues with the use of Probe Request/Response frames for PAD. Additional issues were brought up in TGaq discussion during the Dallas meeting. This submission provides a summary of the comments and proposes a straw poll to help figure out direction for resolving the open comments.
CIDs: 2098, 2142, 2143, 2158

## Slide 3: P802.11aq/D3.0 design
A non-AP STA can use Probe Request (active scan; solicited PAD) or GAS to query available services
New information elements added to Probe Request frame to provide rules for the AP (or PCP) to decide whether to respond and what information to include in the Probe Response frame

## Slide 4: Pros of Probe Request/Response
Part of existing network selection and connection mechanism
Already in P802.11aq/D3.0
  Though, may need changes, e.g., to prevent legacy APs from responding (CID 2142, 2143)

## Slide 5: Cons of Probe Request/Response
Can increase management frame traffic
  Legacy APs would reply regardless of service request constraints (ignore unknown IE); unless current design is modified somehow to avoid this (CID 2142, 2143)
Does not leave AP time to query an external server
  Probe Response is expected immediately in scan
  Non-AP STA likely to leave the channel in less than 20 ms
Extra complexity for AP
  Most existing Probe Response cases use a fixed frame body; changing this based on service request does not fit in nicely with many AP implementation architectures

## Slide 6: Cons of Probe Request/Response (2)
FILS broadcast Probe Response mechanism would be unlikely to use full optimizations
  Contents of response changes based on service request and might not be applicable for other FILS uses (CID 2158)

## Slide 7: Straw poll
P802.11aq solicited PAD should:
continue to use Probe Request/Response frames as-is
continue to use Probe Request/Response frames with changes to prevent legacy APs from replying
use a new Public Action frame defined for this purpose
not be used, i.e., ANQP mechanism should be used instead (only unsolicited PAD would be used in Probe Request/Response and Beacon frames)