## Slide 1: IEEE 802.11 Regulatory State of Affairs
Date: 2016-01-20
Authors:

## Slide 2: Overview
This document summarizes the challenges faced by the industries dependent on the IEEE 802.11 family of standards, in January 2016 and beyond.

## Slide 3: Agenda
Unlicensed / License-exempt spectrum access
Spectrum sharing and getting squeezed
New regulations / No regulations
WRC-15 to WRC-19
What we must do

## Slide 4: Spectrum: A Quick History
The 2.4 GHz garbage band
  FCC in 1984: see if you can do something with this
  Minimal rules
    Power, PSD limits
    Accept and cause no interference
5 GHz – challenging and far from global
  WRC-03: open, but not so fast
  DFS: approved, but unspecified, ever changing tests
  Variations
    US vs EU transmit power and bands
    Indoor restrictions
    Minimal participation in Asia

## Slide 5: Spectrum: Sharing & Squeezing
2.4 GHz
  LTE in 2390 MHz (Ofcom pressing hard for no restrictions)
  Globalstar in 2483.5-2495 MHz (FCC not going to protect Wi-Fi)
  LTE-U?
5 GHz
  Satellites throughout the band (ESA bankrolling effort to minimize RLANs in the band)
  Radars difficult for DFS to detect (DFS 2.0 in the works)
  LAA-LTE using broad based standard sharing mechanisms (ETSI BRAN developing fair sharing standard)
  LTE-U (sharing mechanism of dubious efficacy)
  MulteFire standalone LTE in unlicensed spectrum (?)

## Slide 6: Current 5 GHz spectrum in Europe and most of EMEA
MSS – Mobile Satellite Service
EESS - Earth Exploration Satellite Service
FSS – Fixed Satellite Service

## Slide 7: Regulations: New
ETSI EN 300 328 v2.0.0 (2.4 GHz)
  Includes receiver blocking requirements
  May add Adjacent Channel Selectivity in next revision
ETSI EN 301 893 v2.0.0 (5 GHz)
  Includes receiver blocking requirements
  Will add Adjacent Channel Selectivity in next revision
  Adaptivity requirements being fine tuned for Wi-Fi / LAA-LTE (and others) sharing
ETSI EN 302 567 (60 GHz)
  Includes receiver blocking requirements
ETSI EN 301 598 (TVWS)
  Includes receiver blocking requirements
(Proposed) FCC NPRM 15-138
  Adding 7 GHz to the 60 GHz band (64-71 GHz), and more bands above 24 GHz

## Slide 8: Regulations: None
In spite of its incredible success which goes way beyond the expectations set when the unlicensed spectrum bands were opened, the FCC will not revise regulations to protect it (or Bluetooth), e.g.:
  Globalstar incursion into the band on a terrestrial basis (Channel 14), with no proof that it will not interfere with Channel 11
  LTE-U sharing mechanism unproven, could present serious challenge to Wi-Fi in 5 GHz
  Hundreds of millions of devices can be negatively affected, yet FCC is unwilling to even require real proof of non-interference

## Slide 9: WRC-15 Plan for WRC-19
The entire 5 GHz band will be re-studied
Satellite industry continues to push to minimize RLAN use of their band (RLANs are co-primary)
New radars must be addressed
DFS rewrite could provide some help
  Reduction of initial channel check time
  Incorporation of [sensor networks]

## Slide 10: WRC-15 Plan for WRC-19
ITU-R to conduct and complete the following in time for WRC-19:
a) to study WAS/RLAN technical characteristics and operational requirements in the 5 GHz frequency range;
b) to conduct studies with a view to identify potential WAS/RLAN mitigation techniques to facilitate sharing with incumbent systems in the frequency bands 5 150-5 350 MHz, 5 350-5 470 MHz, 5 725-5 850 MHz and 5 850-5 925 MHz, while ensuring the protection of incumbent services including their current and planned use;
c) to perform sharing and compatibility studies between WAS/RLAN applications and incumbent services in the frequency band 5 150-5 350 MHz with the possibility of enabling outdoor WAS/RLAN operations including possible associated conditions;
d) to conduct further sharing and compatibility studies between WAS/RLAN applications and incumbent services addressing:
  i) whether any additional mitigation techniques in the frequency band 5 350-5 470 MHz beyond those analysed in the studies referred to in recognizing a) would provide coexistence between WAS/RLAN systems and EESS (active) and SRS (active) systems;
  ii) whether any mitigation techniques in the frequency band 5 350-5 470 MHz would provide compatibility between WAS/RLAN systems and radio determination systems;
  iii) whether the results of studies under points i) and ii) would enable an allocation of the frequency band 5 350-5 470 MHz to the mobile service with a view to accommodating WAS/RLAN use;
e) to also conduct detailed sharing and compatibility studies, including mitigation techniques, between WAS/RLAN and incumbent services in the frequency band 5 725- 5 850 MHz with a view to enabling a mobile service allocation to accommodate WAS/RLAN use;
f) to also conduct detailed sharing and compatibility studies, including mitigation techniques, between WAS/RLAN and incumbent services in the frequency band 5 850-5 925 MHz with a view to accommodating WAS/RLAN use under the existing primary mobile service allocation while not imposing any additional constraints on the existing services,

## Slide 11: Survival?
Real challenges to 802.11/Wi-Fi
  Globalstar in the 2.4 GHz band (FCC clearly not supportive enough)
  LTE-U/LAA-LTE shrinking available spectrum (FCC will not protect Wi-Fi; LTE support much more active than Wi-Fi)
  WRC-15 outcomes (re-studying 5 GHz band/DFS; potential good and bad)
  Satellite industry pressing for less 5 GHz Wi-Fi (Main Wi-Fi proponent needs funding)
What is needed
  Increased focus on the issues, strong defense for the value Wi-Fi brings the masses
  Significant participation in ITU-R groups addressing 5 GHz band changes
  Reality check: is Wi-Fi headed for the endangered list?
Scorecard
  IEEE 802 regulatory ineffective
  WFA not stepping up [actually, quite the opposite]
  Individual companies can no longer carry the load
  Jeckel and Hyde (Wi-Fi and LTE-U) corporations may dominate