## Slide 1: Link Adaptation for HE WLAN
Date: 2016-01-18
Authors:

## Slide 2: Background (1/3)
Consideration points on the HE link adaptation [1] was generally discussed and added in SFD [2].
  HE link adaptation shall define reference payload size for the reported MCS in MFB. Reference payload size may be dependent on the frames involved in link adaptation or fixed in specification. Details are TBD. [PHY Motion 77]
  The HE link adaptation field, which is part of HE variant of HT control field, consists of MFB and TBD subfields. The MFB subfield includes NSS and MCS subfield. [PHY Motion 78]
In this submission, more details on reference payload size for the reported MCS in MFB are discussed as a next step.

## Slide 3: Background (2/3)
Node 1
Node 2
Preamble
Data Frame
+HTC (MRQ, MSI = 3)
Data Frame
+HTC (MFB, MFSI = 3)
Solicit MCS Procedure for Link Adaptation
Step 1)
Node 1, the MCS requester, sends a PPDU containing MCS request (MRQ) and MCS request sequence number (MSI)
Node 2, the MCS responder, takes CSI measurements from the preamble and uses RXVECTOR properties to compute MCS.
  CSI measurements taken may be beamformed signals and therefore, MCS feedback will be limited to that specific beamforming.
Step 2) Node 2, the MCS responder, report back MCS feedback (MFB) with MCS feedback sequence number (MFSI) set as the same value as MSI of MRQ.
Step 1)
Step 2)

## Slide 4: Background (3/3)
Solicited feedback based on request from a transmitter.
  MCS feedback (MFB) values are computed from the frame that contained MCS request (MRQ) set to 1.
    Note that BW in MFB field set to 0.
  MCS feedback Sequence ID (MFSI) field is set with MRQ sequence ID (MSI) value for MCS requester.
Unsolicited feedback.
  Autonomous MFB to the transmitter based on frames that the receiver has chose to measure.
  Some basic description (e.g.GID, Coding Type, STBC, FB Tx type etc) about the frame is conveyed. This facilitates identification of the frame (or at least the RXVECTOR of the frame) that MCS measurement has taken place.
Link Adaptation in VHT

## Slide 5: Payload Size Reference for MCS
Required SNR for a given MCS varies significantly based on payload size as shown in Appendix.
With well-defined MCS payload reference, the transmitter may utilize and adjust the reported MCS feedback depending on the transmission payload size characteristics.
  Each vendor may use the reported MCS and transform it to effective SNR to be used for different system target settings.
Reference payload size for the reported MCS in MFB may be variable depending on the frames involved in HE link adaptation or fixed in specification.

## Slide 6: Frame of Reference for MCS
Reference Payload size for MCS is
Opt. 1 (MRQ frame): the MPDU size that contains MRQ
  In case of unsolicited MCS feedback, the PPDU of the MCS measurement is used.
Opt. 2 (MFB frame): the MPDU size that contains MFB
Opt. 3 (fixed in Spec.): a fixed MPDU size, which is simply defined in specification

## Slide 7: Opt 1) MRQ Frame as MPDU Size Reference
Given MSI and MFSI in solicited MCS feedback, MPDU size could be easily identified by Node 1.
In unsolicited MCS feedback,
  difficult to identify which MPDU size is the reference for MCS in A-MPDU,
  and given the limited link adaptation parameters in HE control field, Tx node may not able to uniquely identify the length of the frame MCS measured as reference payload size
Node 1
Node 2
Preamble
e.g.) Solicit MCS feedback
time
+HTC (MRQ =1, MSI = 3)
“A” bytes of MPDU
+HTC (MFB, MFSI = 3)
“B” bytes of MPDU
MCS based on “A” bytes of MPDU
Adjust MCS (from reported MCS)
for a different payload size
“C” bytes of MPDU
…
…
+HTC (MRQ =1, MSI = 5)
“D” bytes of MPDU
+HTC (MFB, MFSI = 5)
“E” bytes of MPDU
MCS based on “D” bytes of MPDU

## Slide 8: Opt 2) MFB Frame as the MPDU Size Reference
No ambiguity of reference size for both solicited and unsolicited MCS feedback.
Solicited MCS feedback typically occurs in control frames such as ACK or BA (i.e. small payload size).
The MCS can quickly be saturated (highest MCS) in case of small reference payload size. Therefore, can not accurately represent high effective SNR (i.e. all high effective SNR is MCS 9).
Node 1
Node 2
Preamble
e.g.) Solicit MCS feedback
time
+HTC (MRQ =1, MSI = 3)
“A” bytes of MPDU
+HTC (MFB, MFSI = 3)
“B” bytes of MPDU
MCS based on “B” bytes of MPDU
Adjust MCS (from reported MCS)
for a different payload size
“C” bytes of MPDU
…
…
+HTC (MRQ =1, MSI = 5)
“D” bytes of MPDU
+HTC (MFB, MFSI = 5)
“E” bytes of MPDU
MCS based on “E” bytes of MPDU

## Slide 9: Opt 3) Fixed MPDU Size as Reference
No effort needed to identify the PPDU frame (especially for unsolicited feedback).
The effective SNR range that is represented by MCS is constant. Rx Node may not need to have multiple MCS to effective SNR lookup tables for effective SNR conversion.
 Simplest Method
Node 1
Node 2
Preamble
e.g.) Solicit MCS feedback
time
+HTC (MRQ =1, MSI = 3)
“A” bytes of MPDU
+HTC (MFB, MFSI = 3)
“B” bytes of MPDU
MCS based on “X” bytes of MPDU
Adjust MCS (from reported MCS)
for a different payload size
“C” bytes of MPDU
…
…
+HTC (MRQ =1, MSI = 5)
“D” bytes of MPDU
+HTC (MFB, MFSI = 5)
“E” bytes of MPDU
MCS based on “X” bytes of MPDU

## Slide 10: Choosing the Right Reference Payload
MCS 9 with 32 bytes achieves 10% and 1% PER at 23dB and 24.3dB, respectively
MCS 9 with 3895 bytes achieves 10% and 1% PER at 25.4dB and 26.4dB, respectively
The reference payload size for MCS affects the range of effective SNR that can be represented by MCS.
  Small payload size has better coverage in the low SNR regions
  Large payload size has better coverage in the high SNR regions
Typically, more useful to represent the high SNR regions. In low SNR cases, the transmission of MFB may not even succeed.

## Slide 11: Proposed Payload References for MCS
The reported MCS in HE MCS Feedback (MFB) corresponds to the highest data-rate, for given transmission properties, that results in frame error rate of X % or lower for a MPDU length of Y octets.
  Transmission properties refer to a specific RU, number of spatial streams (i.e. Nss), beamforming type (i.e. SU, MU, or STBC), and coding type (i.e. BCC or LDPC)
  Possible Values for “X”, “Y”
    X = 10% or 1%
    Y = 3895 (maximum MPDU limit for VHT, see appendix)
Note that the definition here are not actual PER values used in the system but simply a reference for all vendors to understand MCS. The Tx Node may configure the transmit MCS to meet its target parameters.

## Slide 12: Conclusion
The MCS definition has not defined with proper payload size references in WLAN.
We propose to use fixed MPDU size as MCS reference in specification.

## Slide 13: Straw Poll #1
Do you agree to include the following text to TGax SFD:
The reported MCS in HE MCS feedback (MFB) corresponds to the highest data-rate that results in frame error rate of X% or lower for a MPDU length of Y octets.
  “X” and “Y” are fixed values defined in specification and TBD.
Y/N/A

## Slide 14: Reference
[1] 11-15-1329r1 Link Adaptation for HE WLAN
[2] 11-15-0132-13-00ax-spec-framework

## Slide 15: APPENDIX

## Slide 16: Payload Size Reference for MCS
MCS 3
MCS 1
MCS 7
MCS 5
Required SNR for a given MCS varies significantly based on payload size.

## Slide 17: Maximum Data Unit Sizes in 802.11
 | MSDU | A-MSDU | MPDU
Non-HT | 2304 | 3839 or 4065 or 7935 | N/A
HT | 2304 | 3839 or 7935 | N/A
VHT | 2304 | N/A | 3,895 or 7,991 or 11,454

## Slide 18: PSDU per OFDM symbol (NDBPS) (1/3)
Nss = 1 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 1 | 3 | 4 | 6 | 9 | 12 | 13 | 15 | 18 | 20
 | 52 | 3 | 6 | 9 | 12 | 18 | 24 | 27 | 30 | 36 | 40
 | 106 | 6 | 12 | 19 | 25 | 38 | 51 | 57 | 63 | 76 | 85
 | 242 | 14 | 29 | 43 | 58 | 87 | 117 | 131 | 146 | 175 | 195
 | 484 | 29 | 58 | 87 | 117 | 175 | 234 | 263 | 292 | 351 | 390
 | 996 | 61 | 122 | 183 | 245 | 367 | 490 | 551 | 612 | 735 | 816
 | 1992 | 122 | 245 | 367 | 490 | 735 | 980 | 1102 | 1225 | 1470 | 1633
Nss = 2 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 3 | 6 | 9 | 12 | 18 | 24 | 27 | 30 | 36 | 40
 | 52 | 6 | 12 | 18 | 24 | 36 | 48 | 54 | 60 | 72 | 80
 | 106 | 12 | 25 | 38 | 51 | 76 | 102 | 114 | 127 | 153 | 170
 | 242 | 29 | 58 | 87 | 117 | 175 | 234 | 263 | 292 | 351 | 390
 | 484 | 58 | 117 | 175 | 234 | 351 | 468 | 526 | 585 | 702 | 780
 | 996 | 122 | 245 | 367 | 490 | 735 | 980 | 1102 | 1225 | 1470 | 1633
 | 1992 | 245 | 490 | 735 | 980 | 1470 | 1960 | 2205 | 2450 | 2940 | 3266
Nss = 3 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 4 | 9 | 13 | 18 | 27 | 36 | 40 | 45 | 54 | 60
 | 52 | 9 | 18 | 27 | 36 | 54 | 72 | 81 | 90 | 108 | 120
 | 106 | 19 | 38 | 57 | 76 | 114 | 153 | 172 | 191 | 229 | 255
 | 242 | 43 | 87 | 131 | 175 | 263 | 351 | 394 | 438 | 526 | 585
 | 484 | 87 | 175 | 263 | 351 | 526 | 702 | 789 | 877 | 1053 | 1170
 | 996 | 183 | 367 | 551 | 735 | 1102 | 1470 | 1653 | 1837 | 2205 | 2450
 | 1992 | 367 | 735 | 1102 | 1470 | 2205 | 2940 | 3307 | 3675 | 4410 | 4900

## Slide 19: PSDU per OFDM symbol (NDBPS) (2/3)
Nss = 4 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 6 | 12 | 18 | 24 | 36 | 48 | 54 | 60 | 72 | 80
 | 52 | 12 | 24 | 36 | 48 | 72 | 96 | 108 | 120 | 144 | 160
 | 106 | 25 | 51 | 76 | 102 | 153 | 204 | 229 | 255 | 306 | 340
 | 242 | 58 | 117 | 175 | 234 | 351 | 468 | 526 | 585 | 702 | 780
 | 484 | 117 | 234 | 351 | 468 | 702 | 936 | 1053 | 1170 | 1404 | 1560
 | 996 | 245 | 490 | 735 | 980 | 1470 | 1960 | 2205 | 2450 | 2940 | 3266
 | 1992 | 490 | 980 | 1470 | 1960 | 2940 | 3920 | 4410 | 4900 | 5880 | 6533
Nss = 5 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 7 | 15 | 22 | 30 | 45 | 60 | 67 | 75 | 90 | 100
 | 52 | 15 | 30 | 45 | 60 | 90 | 120 | 135 | 150 | 180 | 200
 | 106 | 31 | 63 | 95 | 127 | 191 | 255 | 286 | 318 | 382 | 425
 | 242 | 73 | 146 | 219 | 292 | 438 | 585 | 658 | 731 | 877 | 975
 | 484 | 146 | 292 | 438 | 585 | 877 | 1170 | 1316 | 1462 | 1755 | 1950
 | 996 | 306 | 612 | 918 | 1225 | 1837 | 2450 | 2756 | 3062 | 3675 | 4083
 | 1992 | 612 | 1225 | 1837 | 2450 | 3675 | 4900 | 5512 | 6125 | 7350 | 8166
Nss = 6 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 9 | 18 | 27 | 36 | 54 | 72 | 81 | 90 | 108 | 120
 | 52 | 18 | 36 | 54 | 72 | 108 | 144 | 162 | 180 | 216 | 240
 | 106 | 38 | 76 | 114 | 153 | 229 | 306 | 344 | 382 | 459 | 510
 | 242 | 87 | 175 | 263 | 351 | 526 | 702 | 789 | 877 | 1053 | 1170
 | 484 | 175 | 351 | 526 | 702 | 1053 | 1404 | 1579 | 1755 | 2106 | 2340
 | 996 | 367 | 735 | 1102 | 1470 | 2205 | 2940 | 3307 | 3675 | 4410 | 4900
 | 1992 | 735 | 1470 | 2205 | 2940 | 4410 | 5880 | 6615 | 7350 | 8820 | 9800

## Slide 20: PSDU per OFDM symbol (NDBPS) (3/3)
Nss = 7 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 10 | 21 | 31 | 42 | 63 | 84 | 94 | 105 | 126 | 140
 | 52 | 21 | 42 | 63 | 84 | 126 | 168 | 189 | 210 | 252 | 280
 | 106 | 44 | 89 | 133 | 178 | 267 | 357 | 401 | 446 | 535 | 595
 | 242 | 102 | 204 | 307 | 409 | 614 | 819 | 921 | 1023 | 1228 | 1365
 | 484 | 204 | 409 | 614 | 819 | 1228 | 1638 | 1842 | 2047 | 2457 | 2730
 | 996 | 428 | 857 | 1286 | 1715 | 2572 | 3430 | 3858 | 4287 | 5145 | 5716
 | 1992 | 857 | 1715 | 2572 | 3430 | 5145 | 6860 | 7717 | 8575 | 10290 | 11433
Nss = 8 |  | MCS |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
RU | 26 | 12 | 24 | 36 | 48 | 72 | 96 | 108 | 120 | 144 | 160
 | 52 | 24 | 48 | 72 | 96 | 144 | 192 | 216 | 240 | 288 | 320
 | 106 | 51 | 102 | 153 | 204 | 306 | 408 | 459 | 510 | 612 | 680
 | 242 | 117 | 234 | 351 | 468 | 702 | 936 | 1053 | 1170 | 1404 | 1560
 | 484 | 234 | 468 | 702 | 936 | 1404 | 1872 | 2106 | 2340 | 2808 | 3120
 | 996 | 490 | 980 | 1470 | 1960 | 2940 | 3920 | 4410 | 4900 | 5880 | 6533
 | 1992 | 980 | 1960 | 2940 | 3920 | 5880 | 7840 | 8820 | 9800 | 11760 | 13066