## Slide 1: Remaining HE-LTF Sequence Design
Date: 2016-01-18
Authors:
Name | Affiliation | Address | Phone | Email
Le Liu | Huawei | F1-17, Huawei Base, Bantian, Shenzhen | +86-18028794213 | liule@huawei.com
Wei Lin |  |  |  | lin.linwei@huawei.com
Xin Xue |  |  |  | xuexin@huawei.com
Ningjuan Wang |  |  |  | wangningjuan@huawei.com
Shimi Shilo |  | 4 Ha'harash st., Hod Hasharon, Israel |  | shimi.shilo@huawei
Genadiy Tsodik |  |  |  | genadiy.tsodic@huawei.com
Doron Ezri |  |  |  | Doron.Ezri@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | zhangjiayin@huawei.com
Jun Luo |  |  |  | jun.l@huawei.com
Yingpei Lin |  |  |  | 
 |  |  |  | linyingpei@huawei.com
Jiyong Pang |  |  |  | pangjiyong@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
Junghoon Suh |  |  |  | Junghoon.Suh@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yi Luo |  |  |  | Roy.luoyi@huawei.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Lin Yang | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Alice Chen |  | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Leo Montreuil |  |  |  | leo.montreuil@broadcom.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Andrew Blanksby |  |  |  | 
Zhou Lan |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 6: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com

## Slide 10: Re-cap
Basic mode: 2x/4x HE-LTF for SU/MU PPDUs
  4x and 2x HE-LTF sequences have been defined for 20/40/80MHz [1] But 2x/4x HE-LTF sequences for 160/80+80MHz are TBD
Optional mode: 1x HE-LTF for SU PPDUs (TBD for MU-MIMO)
  Motion: 1x LTF + 0.8 µs GI is one optional combination as indicated by the “GI and LTF size” sub-field in HE-SIG-A
  But 1x HE-LTF sequences for 20/40/80/160/80+80MHz are TBD
    Conventional 1x VHT-LTF cannot be directly used as 1x HE-LTF for channel estimation.
      VHT-LTF56(-28:28) = { +1, +1, LTFleft, 0, LTFright, -1, -1 }  56 tones*(Ng=4)=224 < 242 data tones

## Slide 11: Objective
We propose 160/80+80MHz 2x/4x HE-LTF sequences based on agreed primary 80MHz 2x/4x HE-LTF sequences respectively with optimized PAPR for all size of RUs.
We also design 20/40/80/160/80+80MHz 1x HE-LTF sequences with optimized PAPR of all BWs considering single-stream pilot tones within 1x HE-LTF.
  242 tones in 20 MHz
  484 tones in 40 MHz
  996 tones in 80 MHz
  2*996 tones in 160/80+80 MHz

## Slide 12
2x/4x HE-LTF of 160/80+80MHz

## Slide 13: 160/80+80MHz 4x HE-LTF sequence
4x HE-LTF160MHz(-1012:1:1012) =[ 4x LTF80MHz_primary , zeros(1,23), 4x LTF80MHz_secondary ]
  4x LTF80MHz_primary = [L-LTF80M, 0, R-LTF80M] as agreed for 80MHz 4x HE-LTF [1];
  4x LTF80MHz_secondary = [L-LTF80M, 0, (-1)* R-LTF80M]
4x HE-LTF80+80MHz = [4x LTF80MHz_primary , 4x LTF80MHz_secondary]
  Note: two 80MHz LTFs (1024 tones each including nulls) are combined together

## Slide 14: 160 MHz 4X HE-LTF PAPR
3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 4.25, 4.43 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78
4.97 |  | 4.44 |  |  | 4.97 |  | 4.44 |  | 4.97 |  | 4.44 |  |  | 4.97 |  | 4.44 |  |  | 4.97 |  | 4.44 |  |  | 4.97 |  | 4.44 |  | 4.97 |  | 4.44 |  |  | 4.97 |  | 4.44 | 
5.38 |  |  |  |  | 5.35 |  |  |  | 5.31 |  |  |  |  | 5.53 |  |  |  |  | 5.48 |  |  |  |  | 5.50 |  |  |  | 5.48 |  |  |  |  | 5.50 |  |  | 
5.50 |  |  |  |  |  |  |  |  | 5.51 |  |  |  |  |  |  |  |  |  | 5.60 |  |  |  |  |  |  |  |  | 5.53 |  |  |  |  |  |  |  | 
5.96 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 6.00 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6.29 for primary 80MHz, 7.10 for secondary 80MHz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PAPR (dB) for 26, 52, 108, 242, 484 and 996 tones RU
160 MHz PAPR = 7.09 dB (primary + secondary)
Worst case PAPR for 1 to 6 phases of RHELTF vs. PHELTF
PAPR for secondary 80 MHz LTF are identical for all RUs except for center RU26 and RU996.

## Slide 15: 160/80+80MHz 2x HE-LTF sequence
2x HE-LTF160MHz(-1012:2:1012) = [ 2x LTF80MHz_primary, zeros(1,11), 2x LTF80MHz_secondary ]
  2x LTF80MHz_primary as agreed 80MHz 2x HE-LTF [1] = [{1st 242-RU}, {2nd 242-RU}, {central 26-RU}, {3rd 242-RU}, {4th 242-RU} ];
  2x LTF80MHz_second ary = [{1st 242-RU}, (-1)*{2nd 242-RU}, {central 26-RU}, {3rd 242-RU}, (-1)*{4th 242-RU} ];
2x HE-LTF80+80MHz= [2x LTF80MHz_primary , 2x LTF80MHz_secondary]
  Note: two 80MHz LTFs (1024 tones each including nulls) are combined together

## Slide 16: 160 MHz 2X HE-LTF PAPR
4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.37 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46
4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 | 
5.42 |  |  |  |  | 5.41 |  |  |  | 5.42 |  |  |  |  | 5.41 |  |  |  |  | 5.41 |  |  |  |  | 5.42 |  |  |  | 5.41 |  |  |  |  | 5.42 |  |  | 
5.58 |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  | 
6.29, 6.40 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 6.40, 6.32 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6.08 for primary 80MHz, 6.70 for secondary 80MHz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PAPR (dB) for 26, 52, 108, 242, 484 and 996 tones RU
160 MHz PAPR = 6.72 dB (primary + secondary)
Worst case PAPR for 1 to 6 phases of RHELTF vs. PHELTF
PAPR for secondary 80 MHz LTF are identical for all RUs except for RU484 and RU996.

## Slide 17: 80+80MHz 4X HE-LTF PAPR
  For [Primary 80M, Secondary 80M], let HE-LTF = [ HE-LTF80M_primary, HE-LTF80M_secondary ]
Channel Interval(MHz) | MAX PAPR (dB)
80 (adjacent) | 7.09
100 | 7.20
120 | 6.93
140 | 7.08
160 | 6.89
180 | 6.95
200 | 7.11
220 | 7.09
240 | 7.20
> 240 | 7.03

## Slide 18: 80+80MHz 2X HE-LTF PAPR
  For [Primary 80M, Secondary 80M], let HE-LTF = [ HE-LTF80M_primary, HE-LTF80M_secondary ]
Channel Interval(MHz) | MAX PAPR (dB)
80 (adjacent) | 6.72
100 | 6.71
120 | 7.10
140 | 6.99
160 | 6.86
180 | 7.13
200 | 7.27
220 | 6.99
240 | 7.14
> 240 | 7.23

## Slide 19
1x HE-LTF of 20/40/80/160MHz

## Slide 20: HE-LTF Tone Plan and Pilot Position
20MHz
  4x HE-LTF with -122:1:122 and pilot tones on {±22,±48,±90,±116} [2][3]
  2x HE-LTF with -122:2:122 and pilot tones on {±22,±48,±90,±116} [2][3]
  1x HE-LTF with -120:4:120 and pilot tones on {±48,±116}
40MHz
  4x HE-LTF with -244:1:244 and pilot tones on {±10, ±36, ±78, ±104, ±144, ±170, ±212, ±238} [2][3]
  2x HE-LTF with -244:2:244 and pilot tones on {±10, ±36, ±78, ±104, ±144, ±170, ±212, ±238} [2][3]
  1x HE-LTF with -244:4:244 and pilot tones on {±36,±104,±144,±212}
80MHz
  4x HE-LTF with -500:1:500 and pilot tones on {±24, ±92, ±158, ±226, ±266, ±334, ±400, ±468} [2][3]
  2x HE-LTF with -500:2:500 and pilot tones on {±24, ±92, ±158, ±226, ±266, ±334, ±400, ±468} [2][3]
  1x HE-LTF with -500:4:500 and pilot tones on {±24, ±92, ±400, ±468}
160MHz (Adjacent 80M+80M)
  4x HE-LTF with -1012:1:1012 and pilot tones on {±44, ±112, 178, 246, 286, 354, ±420, ±488, ±536, ±604, ±670, ±738, ±778, ±846, ±912, ±980} [2][3]
  2x HE-LTF with -1012:2:1012 and pilot tones on {±44, ±112, 178, 246, 286, 354, ±420, ±488, ±536, ±604, ±670, ±738, ±778, ±846, ±912, ±980} [2][3]
  1x HE-LTF with -1012:4:1012 and pilot tones on {±44, ±112, ±420, ±488, ±536, ±604, ±912, ±980}

## Slide 21: 20MHz 1x HE-LTF sequence
1x HE-LTF20MHz(-120:4:120) = [ -1, +1, +1, -1, +1, -1, +1, +1, +1, +1, -1, -1, +1, +1, +1, -1, -1, -1, +1, -1, -1, +1, +1, -1, -1, +1, -1, -1, +1, -1, 0, -1, +1, +1, +1, +1, +1, +1, -1, -1, -1, -1, -1, +1, -1, -1, -1, +1, -1, -1, +1, -1, -1, +1, -1, +1, -1, -1, -1, -1, -1 ] ;
Worst PAPR on 242-RU = 3.98dB

## Slide 22: 40MHz 1x HE-LTF sequence
1x HE-LTF40MHz(-244:4:244) = [ +1, +1, +1, +1, -1, +1, +1, -1, -1, +1, -1, +1, -1, +1, -1, -1, +1, -1, +1, +1, +1, -1, -1, +1, +1, +1, +1, +1, +1, +1, +1, -1, +1, +1, -1, -1, +1, -1, +1, -1, +1, -1, -1, +1, -1, +1, +1, +1, -1, -1, +1, +1, +1, +1, -1, +1, -1, +1, -1, -1, -1, 0, +1, +1, -1, -1, +1, -1, +1, +1, +1, +1, +1, +1, -1, +1, +1, -1, -1, +1, -1, +1, +1, +1, +1, +1, -1, +1, -1, -1, -1, +1, +1, -1, -1, -1, +1, -1, -1, -1, -1, +1, -1, -1, +1, +1, -1, +1, -1, -1, -1, -1, -1, +1, -1, +1, +1, +1, -1, -1, +1, +1, +1]
Worst PAPR on 484-RU = 4.54dB

## Slide 23: 80MHz 1x HE-LTF sequence
1x HE-LTF80MHz(-500:4:500) = [-1, -1, +1, +1, +1, +1, +1, -1, -1, -1, +1, +1, -1, -1, +1, -1, +1, -1, -1, -1, -1, -1, -1, +1, +1, -1, -1, +1, -1, +1, -1, -1, -1, -1, -1, +1, +1, -1, -1, +1, -1, +1, -1, +1, +1, +1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, -1, -1, -1, -1, +1, -1, -1, -1, -1, -1, -1, +1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, +1, +1, +1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, +1, +1, +1, -1, +1, +1, -1, -1, +1, -1, +1, -1, +1, +1, +1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, -1, -1, -1, -1, +1, -1, +1, -1, -1, 0, -1, +1, +1, -1, -1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, +1, +1, +1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, +1, +1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, -1, -1, -1, -1, -1, +1, +1, -1, -1, +1, -1, +1, -1, +1, +1, +1, +1, -1, +1, -1, -1, +1, -1, -1, +1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, +1, +1, +1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, +1, +1, +1, -1, +1, +1, -1, -1, +1, -1, +1, -1, +1, +1, +1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, -1, -1, -1, -1, +1, -1, +1, -1, -1, -1, +1, +1]
Worst PAPR on 996-RU = 5.00dB

## Slide 24: 160/80+80MHz 1x HE-LTF sequence
1x HE-LTF160MHz(-1012:4:1012) =[ 1x LTF80MHz_primary , zeros(1,5), 1x LTF80MHz_secondary ]
  1x LTF80MHz_primary = [L-LTF80M, 0, R-LTF80M]  Reuse 80MHz 1x HE-LTF;
  1x LTF80MHz_secondary = [L-LTF80M, 0, (-1)* R-LTF80M]
Worst PAPR for 2*996 RU = 5.12dB
1x HE-LTF80+80MHz= [1x LTF80MHz_primary , 1x LTF80MHz_secondary]
  Note: two 80MHz LTFs (1024 tones each including nulls) are combined together.

## Slide 25: 80+80MHz 1x HE-LTF PAPR
  For [Primary 80M, Secondary 80M], let HE-LTF = [ HE-LTF80M_primary, HE-LTF80M_secondary ]
Channel Interval(MHz) | MAX PAPR (dB)
80 (adjacent) | 5.12
100 | 5.15
120 | 5.29
140 | 5.24
160 | 5.30
180 | 5.33
200 | 5.41
220 | 5.40
240 | 5.43
> 240 | 5.45

## Slide 26: Summary
We proposed 2x/4x HE-LTF sequences for SU/MU PPDUs on 160/80+80MHz
We proposed to 1x HE-LTF sequences for SU PPDUs on 20/40/80/160/80+80MHz.
BW | 4x HE-LTF Worst PAPR in dB | 2x HE-LTF Worst PAPR in dB | 1x HE-LTF Worst PAPR in dB
20MHz | 5.36 for SU (5.36 for all RUs) | 5.24 (5.24) | 3.98
40MHz | 5.47 (6.00) | 5.84 (5.99) | 4.54
80MHz | 6.29 (6.29) | 6.08 (6.40) | 5.00
160MHz | 7.09 (7.10) | 6.72 (6.72) | 5.12
80+80MHz | 7.20 (7.20) | 7.27 (7.27) | 5.45

## Slide 27: References
[1] IEEE 802.11ax, 11-15-1334-01-00ax, HE-LTF Design, Dallas Nov. 2015.
[2] 11-15-0819-01-00ax-11ax-ofdma-tone-plan-leftover-tones-and-pilot-structure
[3] 11-15-0812-01-00ax-pilot-design-for-data-section

## Slide 28: Straw Poll - 1
Do you agree
  4x HE-LTF160MHz(-1012:1:1012) =[ 4x LTF80MHz_primary , zeros(1,23), 4x LTF80MHz_secondary ]
    4x LTF80MHz_primary = [L-LTF80M, 0, R-LTF80M] as agreed for 80MHz 4x HE-LTF;
    4x LTF80MHz_secondary = [L-LTF80M, 0, (-1)* R-LTF80M]
  4x HE-LTF80+80MHz = [4x LTF80MHz_primary , 4x LTF80MHz_secondary]
Y
N
A

## Slide 29: Straw Poll - 2
Do you agree
  2x HE-LTF160MHz(-1012:2:1012) = [ 2x LTF80MHz_primary , zeros(1,11), 2x LTF80MHz_secondary ]
    2x LTF80MHz_primary as agreed for 80MHz 2x HE-LTF = [{1st 242-RU}, {2nd 242-RU}, {central 26-RU}, {3rd 242-RU}, {4th 242-RU}];
    2x LTF80MHz_secondary = [{1st 242-RU}, (-1)*{2nd 242-RU}, {central 26-RU}, {3rd 242-RU}, (-1)*{4th 242-RU} ];
  2x HE-LTF80+80MHz= [2x LTF80MHz_primary , 2x LTF80MHz_secondary]
Y
N
A

## Slide 30: Straw Poll - 3
Do you agree to use the 20/40/80/160/80+80MHz 1x HE-LTF sequences in slide 21-24?
Y
N
A