## Slide 1: UL MU CCA Response
Date: 2016-01-18
Authors:
Name | Affiliation | Address | Phone | Email
Kaiying Lv | Kaiying Lv (ZTE) | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | lv.kaiying@zte.com.cn
Bo Sun |  |  |  | sun.bo1@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Hyeyoung Choi | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hy0117.choi@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: UL MU CCA
Date: 2016-01-18
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Hongyuan Zhang |  |  |  | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Bo Yu |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | Jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 7: Authors (continued)
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com
Name | Affiliation | Address | Phone | Email
Thomas Derham | Orange |  |  | thomas.derham@orange.com

## Slide 8: Background (1)
11ax SFD has defined that a STA shall consider CCA status to respond to a Trigger frame under a non-null TBD set of conditions. The text specifies two scenarios:
    Scenario-1: Under a non-null TBD set of conditions, a STA can transmit UL MU PPDU in response to a trigger frame, without considering CCA, i.e., without carrier sensing;
    Scenario-2: Otherwise, a STA shall consider CCA, i.e., with carrier sensing, before transmitting UL MU PPDU in response to a trigger frame
This contribution provides some discussions about UL MU CCA response rules.
Typical 11ax UL MU frame exchange sequences: Basic and Cascading
UL MU PPDU
Trigger
TXOP
AP Gains the channel access
DL
UL
DL
ACK
/BA
UL MU PPDU
Trigger + DL MU Data
TXOP
AP Gains the channel access
DL
UL
DL
ACK
/BA
Basic: Trigger ++ UL MU data ++ DL ACK/BA
Cascading: (Trigger + DL MU data) ++ UL MU data ++ DL ACK/BA

## Slide 9: Open Issues about UL MU CCA
What is the non-null set of conditions for a STA not to consider CCA before UL MU transmission in response to a Trigger Frame?
When to sense the channel if CCA is required before UL MU transmission in responses to a trigger frame?
Which channel to sense if CCA is required before UL MU transmission in responses to a trigger frame?
How to sense the channel, Physical CS and Virtual CS, if CCA is required before UL MU transmission in responses to a trigger frame?
What’s the IFS between Trigger and UL MU PPDU?
What if the allocated channel is busy?
What if the allocated channel is partially busy?
 This contribution will focus on the Open Issue #6 and #7.

## Slide 10: What If the Allocated Channel is Busy?
If the allocated UL subchannel is not all idle, then 3 Options:
  Option-1: the STA will not transmit anything in the allocated UL resource;
  Option-2: the STA will transmit an UL MU PPDU only in the available channel;
  Option-3: the STA will transmit in the allocated UL resource as if the allocated channel is available.
AP
STA2
STA1
STA0
STA3
Ch
HE-SIG
L-Preamble
HE-Preamble
UL PPDU from STA 2 for Option-2
on the available channel
HE-Data
Occupied by OBSS
Illustration of partial busy channel
TXOP
Primary 20MHz channel.
STA2 A-MPDU to AP
DL
UL
STA3 A-MPDU to AP
STA0 A-MPDU to AP
STA1 A-MPDU to AP
DL
Trigger
Trigger
Trigger
Trigger
M-BA
M-BA
M-BA
M-BA
Ch1
Ch2
Ch3
Ch4
20MHz channel busy for STA2

## Slide 11: Comparison of options
TXOP
HE-SIG
Options | Pros | Cons
Option 1 | Simple design | Conservative performance
Option 2 | Higher spectrum efficiency | AP has to do blind decoding which make things complicated - note that partial BW response is actually not feasible, because the UL MU preamble does not have an indication of the transmission BW (it is only in the trigger), so AP would not even know on which sub-channel to decode.
Option 3 | No physical carrier sensing Simple and aggressive | Interference to the on-going transmission
  Recommendation: Option-1

## Slide 12: Conclusion
We discussed some options for UL MU response when physical carrier sensing on the allocated channels indicating channel busy or partially busy.
Comparison on different options is described
We proposed a simple UL MU response rule.
.

## Slide 13: References
11-15-1058-00-00ax-cca-consideration-for-ul-mu-transmission
11-15-0132-09-00ax-spec-framework
IEEE P802.11-REVmc/D4.2, Sept 2015

## Slide 14: Straw Poll 1
Do you support to add the following text into Section 4.3 of the SFD:
  When required to sense the medium before its UL MU transmission in response to a trigger frame, if a STA detects the 20MHz channels containing the allocated UL RU are not all idle, then the STA shall not transmit anything in the allocated UL RU.