## Slide 1: Considerations on LRLP Transmissions
Date: 2016-01-16
Authors:
Name | Affiliation | Address | Phone | Email
Yakun Sun Hongyuan Zhang Lei Wang Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | yakunsun@marvell.com
Jianhan Liu Tianyu Wu | MediaTek |  |  | 

## Slide 2: Overview
Long range low power transmission has drawn wide attentions with a large variety of IoT use cases e.g., [1-3].
  Sensor network
  industry
  agriculture
  security
  smart home
  Smart/wearable devices
Alternative wireless/cellular technologies are also under developments.
  For example, LTE MTC and its enhancements.

## Slide 3: LRLP Design Criteria and Challenges
Extremely low power consumption
  For example, coin battery running for months/years.
Extended coverage
  Even with lower power, the coverage may need be extended over the regular WLAN.
Asymmetric coverage
  UL (from devices to AP/central hub) has a much lower link budget compared to DL (from AP to devices)
Achievable data rates
  It is not expected to achieve high data rates.
Very simple and asymmetric implementation
  Low cost devices enables very wide deployment.
  AP may need to do most of work and can be quite advanced.
Coexistence with legacy networks

## Slide 4: Narrowband Transmission
It is straightforward to consider LRLP transmission in sub-20MHz only.
  Power boost per tone given the same transmit power.
How wide the bandwidth needs to be?
  1MHz? 2MHz? 5MHz? 10MHz?
Need to balance the power gain vs. the capability of carrier sensing and the impact of impairments.
  For example, a low cost device may have larger CFO than regular WLAN devices. CFO correction becomes more challenging with narrower bandwidth.

## Slide 5: Single Carrier Transmission
Single carrier transmission, (SC-FDMA)
  Add a (smaller) DFT before IFFT.
  Minimum performance difference (given ML is not needed for single stream LRLP transmission).
  Reduce PAPR: improve PA efficiency (or reduce PA cost), reduce peak power or current for coin battery.
Is SC-FDMA for uplink only or both?
  DL coverage may not be the bottleneck with a strong AP.
  UL only SC removes the additional DFT for device as the receiver, and may be better for coexistence.
Choice of additional DFT: power of 2?
  A non-power-of-2 DFT may still be acceptable since there is only 1 (small) DFT to be implemented.
  Depends on other factors such as the tone plan.

## Slide 6: Localized vs. distributed SC-FDMA
>5dB gain
1~2dB gain
Distributed SC-FDMA may have close to constant envelop and a larger PAPR gain.
There are other factors to consider:
  For example, fixed or dynamic tone mapping?
Maps DFT output on consecutive vs. every few tones.

## Slide 7: Other Considerations on PHY
Coding and modulation
  May only require one coding scheme from BCC and LDPC.
    Given the low SNR and short packet, maybe only BCC to simply PHY.
  A small set of MCS’s will be sufficient, with some data rates lower than 6Mbps.
    Only support low rate modulation and reduce the requirements on TxEVM.
    Repetition coding/modulation or a lower rate mother code may be defined.
Beamforming?
  Devices of small form factors may not have more than 1 antenna  no UL BF.
  AP can equip with multiple transmit antennas  DL BF
  But sounding feedback is also too heavy for low rate UL.
    A DL trigger frame initiated implicit sounding;
    Some simplified sounding feedback,
    Or transmit diversity scheme may be used.
Enhanced transmission schemes?

## Slide 8: Coexistence
LRLP device may not need to detect legacy frames, even for 11a/g
  Greatly reduce the complexity and the power consumption.
LRLP protection of DL transmission
  DL frame may start with legacy preambles for legacy devices to back off.
LRLP protection of UL transmission
  LRLP devices does not transmit legacy preambles, so legacy device may only use ED for backoff.
    A trigger frame from AP to initiate UL transmission can serve the UL protection.
  LRLP devices can also transmit legacy preambles for protection.
Legacy Preamble
LRLP Preamble
LRLP Data
Legacy preamble protected LRLP Frame
LRLP Data
LRLP Preamble
Un-protected LRLP Frame

## Slide 9: Considerations on MAC
Support a small set of MAC features and protocols.
  For example, no BA or simplified BA.
Power saving scheme is very crucial.
  A lot of IoT devices only transmit very occasionally and sleep for a very long time.
  Allow a device to stay connected in the BSS with a long sleep, to reduce the efforts of reassociation.
  Regular power saving schemes may need to be down-selected and simplified.

## Slide 10: References
[1] 11-15-1365-00-lrlp-use-cases-of-lrlp-operation-for-iots
[2] 11-15-1380-00-lrlp-lrlp-digital-health-use-case
[3] 11-15-1383-00-lrlp-long-range-low-power-use-cases-for-indoor-outdoor