## Slide 1: Views on UL-MU features
Date: 2016-01-15
Authors:
Name | Affiliation | Address | Phone | Email
Joonsuk Kim | Apple | 1 Infinite Loop, Cupertino, CA 95014 |  | joonsuk@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Tomoko Adachi | Toshiba |  |  | tomo.adachi@toshiba.co.jp
Narendar Madhavan |  |  |  | narendar.madhavan@toshiba.co.jp
Kentaro Taniguchi |  |  |  | kentaro.taniguchi@toshiba.co.jp
Toshihisa Nabetani |  |  |  | toshihisa.nabetani@toshiba.co.jp
Tsuguhide Aoki |  |  |  | tsuguhide.aoki@toshiba.co.jp
Koji Horisaki |  |  |  | kouji.horisaki@toshiba.co.jp
David Halls |  |  |  | david.halls@toshiba-trel.com
Filippo Tosato |  |  |  | filippo.tosato@toshiba-trel.com
Zubeir Bocus |  |  |  | zubeir.bocus@toshiba-trel.com
Fengming Cao |  |  |  | fengming.cao@toshiba-trel.com

## Slide 2
Authors (cont):
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane Santa Clara, C95054 |  | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 3
Authors (cont):
Name | Affiliation | Address | Phone | Email
Kaushik Josiam | Samsung | 1301 E. Lookout Dr Richardson TX 76110 |  | k.josiam@samsung.com
Rakesh Taori |  |  |  | rakesh.taori@samsung.com
Sai Nandagopalan |  |  |  | s.nanda@partner.samsung.com
SangHyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea |  | s29.chang@samsung.com
Fei Tong |  | Innovation Park, Cambridge CB4 0DS (U.K.) |  | f.tong@samsung.com
Mark Rison |  |  |  | m.rison@samsung.com
Minho Cheong | Newracom | 9008 Research Drive, Irvine, CA 92618 |  | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com
Sigurd Schelstraete | Quantenna | 3450 W. Warren Ave, Fremont, CA 94538 |  | sigurd@quantenna.com

## Slide 4
Authors (cont):
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | 
Leo Montreuil |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel |  |  | Robert.stacey@intel.com
Qinghua Li |  |  |  | 
Xiaogang Chen |  |  |  | 
Chitto Ghosh |  |  |  | 
Laurent Cariou |  |  |  | 
Po-Kai Hunag |  |  |  | 
Brian Hart | Cisco |  |  | brianh@cisco.com
Pooya Monejemi |  |  |  | 
Yasushi Takatori | NTT |  |  | takatori.yasushi@lab.ntt.co.jp
Yusuke Asai |  |  |  | 
Koichi Ishihara |  |  |  | 
Yasuhiko Inoue |  |  |  | 
Junichi Iwatani |  |  |  | 
Shoko Shinohara |  |  |  | 

## Slide 5
Authors (cont):
Name | Affiliation | Address | Phone | Email
Tomas Pare | Mediatek |  |  | thomas.pare@mediatek.com
Chauchun Wang |  |  |  | 
Jianhan Liu |  |  |  | 
James Wang |  |  |  | 
Tianyu Wu |  |  |  | 

## Slide 6: Abstract
This presentation describes the view on UL MU features in 11ax

## Slide 7: Background
Tx beamforming has been introduced in 802.11n as one of MIMO features
  All the sounding and feedback schemes are settled with 802.11ac
  Tx beamforming is very useful to achieve better link quality, by utilizing the channel information (CSI)
In 802.11ac, MU-MIMO is also introduced
  This new feature is only for downlink transmission
  This scheme can improve the network throughput significantly
With 802.11ax, we are talking about an additional feature, UL MU-MIMO
In this presentation, we’d like to review when UL MU-MIMO is useful with possible scenarios

## Slide 8: DL MU-MIMO
Beamforming with MIMO requires basically multiple antennas
  With HW requirement and power consumption perspective, multiple antennas are often preferred to be at STAs with outlet power, rather than portable STAs with battery
  In that sense, currently, most of extensive implementation of MIMO (i.e, more than 4 antennas) is considered at AP, but not at clients
Most of beamforming applications we currently observe are for downlink from AP to clients
  All supportive frames for beamforming, including DL MU-MIMO, is well covered in 802.11ac
  The requirement of MU beamformee in addition of SU beamformee is marginal
    More higher resolution of feedback report

## Slide 9: UL MU-MIMO
By definition, uplink implies that the receiver is an AP
  UL MU-MIMO can enable an AP to isolate multiple spatial streams from multiple STAs in the same time & frequency BW
  When the AP receives response packets from STAs, it may reuse the steering matrix, Q, that was used for DL MU-MIMO, until it processes HE-LTFs of the response packets
    Once AP processes HE-LTFs, it is basically receive beamforming
    No need to support HE-NDP transmitted by Non-AP STAs for UL MU-MIMO
  If Non-AP STAs needs Tx beamforming, 11ac already provides SU beamforming feedback mechanism
HW requirement of Non-AP STAs [2,3]
  Time/frequency sync (Quite more expensive than DL MU-MIMO capable only clients)
  More intensive power control
    Complicated handshake rule for NDPs from multiple STAs in UL sounding

## Slide 10: Usage Model of UL MU-MIMO
If we need UL MU PPDU operation, followed by a trigger frame, we have excellent alternative scheme: OFDMA
One useful scenario of UL MU-MIMO we see is a response for DL MU-MIMO, e.g.,
    UL MU-ACK/BA followed by DL MU-MIMO PPDU
    MU BF feedback followed by Trigger in DL sounding sequence
  There is no need for Non-AP STAs to send an NDP in MU-MIMO
For UL MU Tx capable devices, it should meet more complex HW requirement
  DL MU Rx capable requirement is just marginal compared to it
DL MU-MIMO PPDU
UL MU- ACK/BA
SIFS
An RU
The same
RU

## Slide 11: Review of Capability on MU-MIMO in 11ac
Copied from 802.11ac-2013 [2]
  B.4.27.1 VHT MAC features
CF29: VHT, CF1: AP, CF2: non-AP STA, nor mesh STA
CF: implementation under test (IUT) configuration
VHTM: VHT MAC features
MU BF capable devices require to be SU BF capable

## Slide 12: Proposal of Capability on MU-MIMO in 11ax
Define two MU capabilities under MIMO: DL-MU and UL-MU
  Sounding portion from previous table is not covered in the table below
item | Protocol capability | Status
HEMy | HE MIMO Beamforming | 
HEMy.1 | SU Beamformer Capable | CFxx:TBD
HEMy.2 | SU Beamformee Capable | CFxx:TBD
HEMy.3 | DL-MU Beamformer Capable | CF1 & HEMy.1:TBD
HEMy.4 | DL-MU Beamformee Capable | CF2 & HEMy.2:TBD
HEMy.5 | UL-MU PPDU Transmitter Capable* | CF2 & HEMy.2 & HEMy.4:TBD
HEMy.6 | UL-MU PPDU Receiver Capable* | CF1 & HEMy.1 & HEMy.3:TBD
CFxx: HE, HEMy: HEM item #y, CF1: AP, CF2: non-AP STA, nor mesh STA
* Name may be subject to change
CF: implementation under test (IUT) configuration
HEM: HE MAC features

## Slide 13: References
802.11ac-2013 Part11 WLAN MAC and PHY Specification, Amendment 4: Enhancements for VHT for operation in bands below 6 GHz
11-15-0363-01-00ax-UL-MU-synchronization-requirements by ZTE
11-15-0132-13-00ax-spec-framework

## Slide 14: Straw Poll #1
Do you agree to add following text in SFD?
  NDP shall only be in SU PPDU format and sent by the same STA transmitting NDP-A, for CSI measurement for beamforming

## Slide 15: Straw Poll #2
Do you agree that UL MU-MIMO capable non-AP devices shall also support DL MU-MIMO?
  i.e., In order to be UL-MU-MIMO Tx capable, non-AP STAs need to be DL-MU-MIMO Rx capable

## Slide 16: Straw Poll #3
Do you agree that UL MU-OFDMA capable non-AP devices shall also support DL MU-OFDMA?
  i.e., In order to be UL-MU-OFDMA Tx capable, non-AP STAs need to be DL-MU-OFDMA Rx capable