## Slide 1: BSS color and multiple BSSID
Date: 2016-01-18
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Hongyuan Zhang |  |  |  | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Bo Yu |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 6: Authors (continued)
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Name | Affiliation | Address | Phone | Email
Hyeyoung Choi | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hy0117.choi@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 8: Dynamic CCA and BSS Coloring
Originally static CCA (with normal CCA level) is used for channel idle/busy detection.
  -82dbm/-79dbm/-76dnm/-73dbm (normal CCA level) of 802.11 signal are used for 20MHz/40MHz/80Mhz/160MHz(80+80MHz) idle/busy detection and -62 dbm of any signal is used for idle/busy medium detection.
When the transmission is from neighbor BSS, 802.11ax/HE may use dynamic CCA level (higher CCA level) to decide whether the medium is busy, e.g. -62dbm which can increase spatial reuse among neighboring BSSs. However normal CCA level, e.g. -82dbm for 20MHz is used when the transmission is from self BSS.
BSS color in HE PHY SIG is used for a STA/AP to decide whether the detected 802.11 transmission is from the self BSS or neighbor BSS.
  When the transmission is from the self BSS and the CCA level is lower than the defined lower CCA level, a STA/AP can decide the medium is busy.
  When the transmission is from the neighbor BSS and the CCA level is lower than the defined higher CCA level, a STA/AP can decide the medium is idle.
  The decoding of PHY header before HE SIG is based on normal CCA level.

## Slide 9: Virtual APs in 802.11
A 11ax STA shall support Multiple BSSI Delement.
Multiple BSSID uses a single beacon to efficiently advertise multiple BSSIDs (virtual APs) and SSIDs.
Virtual APs share many properties:
  The Timestamp and Beacon Interval fields, DSSS Parameter Set, FH Parameter Set, IBSS Parameter Set, Country, FH Parameters, FH Pattern Table, Channel Switch Assignment, Extended Channel Switch Announcement, Supported Operating Classes, IBSS DFS, ERP Information, HT Capabilities and HT Operation elements are not included in the Nontransmitted BSSID Profile field; the values of these elements for each nontransmitted BSSID are always the same as the corresponding transmitted BSSID element values.
The first 2n bits of the TIM are reserved for broadcast/multicast for each BSS. The rest of the AID space is shared by all BSSs.
  Each BSS can have its own DTIM interval.
11ax already allows frames from/to STAs associated with multiple virtual APs to be included in one MU transmission.
 | Element ID | Length | Max BSSID indicator | Nontransmitted BSSID Profile
Octets: | 1 | 1 | 1 | variable
Multiple BSSID element

## Slide 10: BSS Color with Virtual APs
When each virtual AP selects its own BSS color, more collision may occur.
STA1
STA2
AP1
HE PPDU to AP1
AP2
The transmission is from different BSS, and the detected signal is lower than dynamic CCA level and higher than -82dbm.
HE PPDU to AP2
Collision occurs.
STA1 associates with AP1.
STA2 associates with AP2.
When each virtual AP selects its own BSS color, it is difficult to allow the STAs from different virtual BSSs to transmit MPDUs/A-MPDUs in a downlink/uplink OFDMA transmission.
Primary 20MHz for STA1
Primary 20MHz for STA2
HE SIGs are different because of different BSS color.
STA1
STA2
Virtual AP1 with color1
Virtual AP2 with color2
STA1
STA2
Virtual AP1 with color1
Virtual AP2 with color2
We propose that a same BSS Color shall be used for the virtual APs which are defined by Multiple BSSID element.

## Slide 11: Collision Avoidance with Virtual APs
Collision can be avoided since all virtual APs have same BSS color.
STA1
STA2
AP1
HE PPDU to AP1
AP2
HE PPDU to AP2
STA1 associates with AP1.
STA2 associates with AP2.
The transmission is from virtual BSS, and the detected signal is lower than dynamic CCA level and higher than -82dbm.
Busy medium
STA1
STA2
Virtual AP1 with color1
Virtual AP2 with color2
BA
BA
STA1
STA2
Virtual AP1 with color1
Virtual AP2 with color1

## Slide 12: MU Transmission with multiple Virtual APs
STA1 associates with AP1.
STA2 associates with AP2.
When all virtual APs have same BSS color, frames from/to STAs associated with multiple virtual APs can be included in one MU transmission.
Primary 20MHz for STA1
Primary 20MHz for STA2
HE SIGs are same when all virtual APs have same BSS color.
STA1
STA2
Virtual AP1 with color0
Virtual AP2 with color0

## Slide 13: References
[1] Draft P802.11REVmc_D5.0
[2]11-15/132r13 Specification Framework for TGax

## Slide 14: Straw Poll 1
Do you agree to add the following text into the SFD:
A same BSS Color shall be used for the virtual APs which are defined by Multiple BSSID element