## Slide 1: Allocation sizes for BCC in OFDMA
Date: 2016-01-18
Authors:

## Slide 2: Background
Agreement on Coding Scheme [1]:
  LDPC is the only coding scheme in the HE PPDU Data field for allocation sizes of 484 tones, 996 tones and 996*2 tones.
  Support of BCC code is limited to less than or equal to four spatial streams, and is mandatory for RU sizes less than or equal to 242 tones (20MHz).
It is still TBD whether multiple RU allocation to a user is allowed.
  e.g. 242+106tones, 106+106+106tones
In this contribution, we are talking about the coding scheme under multiple RU allocation scenarios.

## Slide 3: BCC
BCC code is limited to Nss <=4 and is mandatory for RU sizes less than or equal to 242 tones (20MHz), based on the following reasons [2]:
  Usage of BCC is mainly limited to low-end 11ax devices.
  Low-end 11ax devices will implement 20MHz only.
  We don't have any MCS exclusion when BCC is used for RU sizes <= 20MHz.

## Slide 4: OFDMA RU Allocation
Agreement on OFDMA RU sizes [1]:
  - 26, 52, 106, 242, 484 and 996 tones.
It is still TBD whether multiple RU allocation to a user is allowed.
If multiple RU allocation to a user is allowed, we should choose coding scheme carefully to avoid MCS exclusion.
  11ax MCS table shall not have any MCS exclusion[1].
106
26
26
106
106
106
40MHz
e.g.) Multiple RUs to a user: NCBPS=306
MCS | R | Ndbps (Ncbps x R) | possible FEC
5 | 2/3 | 204 | BCC, LDPC
6 | 3/4 | 229.5 | LDPC
7 | 5/6 | 255 | BCC, LDPC

## Slide 5: BCC usage under multiple RU allocation
If multiple RU allocation to a user is allowed, allocation sizes more than 242 lead to multiple BCC encoders, when assuming 600Mbps per encoder:
  e.g.)
106
26
106
106
106
26
Unbearable burden for single encoder.
(also needs new interleaver size)
40MHz
242
40MHz
242
No need for multiple encoders.
Single RU to a user. (MCS=11, 242tones, Nss=4 => 574Mbps)
Multiple RUs to a user. (MCS=9, 106+26+106+106tones, Nss=4 => 677Mbps)

## Slide 6: Summary
We have talked about the coding scheme under multiple RU allocation scenarios.
If we allow multiple RU allocation to a user, usage of BCC may lead to
    MCS exclusion, multiple encoders, new interleaver size
We prefer
  not to allow multiple RU allocation for one STA,
  or even if we allow it, we should disallow BCC in the HE PPDU Data field for multiple RU allocation sizes more than 242 tones.
    In other words, LDPC should be the only coding scheme for multiple RU allocation sizes more than 242 tones.

## Slide 7: References
[1] 11-15/0132r13 “Specification Framework for TGax”
[2] 11-15/0580r1 “11ax Coding Discussions”

## Slide 8: Straw Poll 1
Do you agree to add the following text into 11ax SFD?
  Multiple RU allocation for one STA shall not be allowed in 11ax.
Y:N:A =

## Slide 9: Straw Poll 2
Do you agree the following text?
  LDPC is the only coding scheme in the HE PPDU Data field for allocation sizes more than 242 tones when multiple RU allocation is allowed to a user.
Y:N:A =