## Slide 1: Regarding HE NDPA frame for DL Sounding Sequence
Date: 2016-01-18
Authors:

## Slide 2: VHT Compressed Beamforming frame format
In 11ac , STAs (or beamformees) decide how much to feedback
  8.4.1.47 [1] VHT MIMO control field is included in the VHT compressed beamforming frame format
  The channel width, number of sub-carrier grouping, codebook etc., are decided by the STAs depending on their capability
  Depending on the values chosen for these parameters, the size of the feedback matrix varies

## Slide 3: VHT Compressed Beamforming frame format
There are three main factors that determine its size:
  Bandwidth: wider channels have more subcarriers, so the feedback matrix must be larger to accommodate them.
  Higher the number of sub-carriers, larger the matrix.
  802.11ac allows two different bit representations of the angle values to enable devices to use higher resolution when necessary.
Multi-user MIMO requires higher resolution to avoid inter-user interference
In 11ac, All these parameters are decided by the beamformee or STA.
In 11ax, if the same rule is followed
there is an imminent problem:
Multiple STAs send compressed
beamforming frames of varying duration sizes
in UL MU mode

## Slide 4: HE DL Sounding
To solicit the STAs to send Compressed Beamforming frames in the UL MU mode simultaneously, Trigger frame includes the PPDU length and MCS
AP decides the UL PPDU length and MCS to be notified to the STAs
STAs may not be able to adjust to the PPDU length mentioned in the Trigger frame
  Feedback matrices are prepared with different parameters determined at multiple beamformees immediately after the reception of NDP frame
STAs may not be able to adjust to the MCS in the Trigger frame
We have the following in the current SFD [2]:

## Slide 5: Setting compressed beamforming frames’ UL MU PPDU length
AP has to notify the PPDU length in the Trigger frame to solicit Compressed beamforming feedback frames in UL MU
Option 1: AP sets the longest possible PPDU length of compressed beamforming frames to all the STAs in the trigger frame
Option 2: STA adjusts to the PPDU length provided in the trigger frame irrespective of the feedback frame generated locally
Option 3: AP specifies the Codebook and Grouping information to the STAs in the Trigger frame
Option 4: AP specifies the Codebook and Grouping information to the STA in the HE NDPA frame

## Slide 6: Notifying UL MU PPDU length for Sounding
Option 1:
  Choose the largest PPDU duration possible and notify using the Trigger frame
  Pros:
  Lowest MCS, with high resolution for the feedback matrix, all STAs will be able to align to the PPDU length
  Cons:
  Inefficient as most of the STAs will have to pad
  Option 2:
  STAs decide the feedback parameters and adjusts to the PPDU length indicated in the Trigger frame
  Pros:
  Feedback matrix can be constructed immediately after NDP frame
  Cons:
  After receiving the trigger frame, STAs have to reconstruct the frame using the given PPDU length
  Might be difficult to perform this within TBD IFS after Trigger
  If the STAs are not able to prepare the feedback matrix frame or match the PPDU length they have to be polled again.

## Slide 7: Notifying UL MU PPDU length for Sounding
Option 3: AP notifies necessary parameters (Grouping, Codebook) for sounding to the STAs in the Trigger frame
Pros:
    Can be included in the Per-STA info fields
  Cons:
    STAs may not be able to construct the desired feedback frame within TBD IFS after receiving Trigger
    STAs start making the feedback matrix after receiving NDP frame and have to adjust to the parameters indicated in the Trigger frame later
Option 4: AP notifies necessary parameters (Grouping, Codebook) for sounding to the STAs in the HE NDPA frame.
  Pros:
    Can include it in the Per-STA info fields
    Ample time to prepare the feedback matrix after receiving NDP frame
  Cons:
    A new HE NDPA frame needs to be designed.

## Slide 8: Summary
The necessity of an HE AP to notify certain parameters to solicit STAs (or beamformees) to generate beamforming feedback matrices was discussed
Parameters include sub-carrier grouping , Codebook, channel width etc.
These parameters notified before the reception of HE NDP frame is preferred
  Option 4: AP notifies the necessary parameters (Grouping, Codebook) for sounding to the STAs in the HE NDPA frame.
  Enables STAs to start preparing the compressed beamforming frames immediately after the reception of HE NDP
  Need to design a new NDPA frame for HE DL Sounding

## Slide 9: References
[1] IEEE Std 802.11ac-2013
[2] 802.11-15/0132r9 “Specification Framework for TGax”

## Slide 10: Straw Poll 1
Do you agree to add to the TG Specification Frame work document?
x.y.z. AP indicates the necessary parameters (Grouping, codebook, channel bandwidth) so that multiple HE STAs can construct the compressed beamforming feedback frames immediately after receiving the NDP frame

## Slide 11: Extra Slides

## Slide 12: Compressed Beamforming Feedback frame Sizes (20 MHz)
(Num of Tx Ant) x (stream) | Codebook | Subcarrier Grouping | Frame size in bits | Frame duration in us |  |  |  | 
 |  |  |  | MCS0 | MCS1 | MCS3 | MCS5 | MCS8
4x1 | 0 | 1 | 2264 | 392 | 216 | 128 | 84 | 72
 |  | 2 | 1416 | 264 | 152 | 96 | 68 | 60
 |  | 4 | 888 | 180 | 112 | 76 | 60 | 52
 | 1 | 1 | 2888 | 488 | 264 | 152 | 96 | 80
 |  | 2 | 1776 | 320 | 180 | 112 | 76 | 64
 |  | 4 | 1080 | 212 | 128 | 84 | 64 | 56
In 11ax, the beamformees or the STAs decide the resolution, bandwidth and grouping to calculate the feedback matrix.
In 11ax, if we follow the same rule there is an imminent problem of multiple STAs trying to send varying frame duration packets in UL MU mode