## Slide 1: Frequency Multiple Access in 11ay
Date: 2016-01-18
Authors:

## Slide 2: Introduction
11ay has considered multi-channel operation like wide bandwidth channel bonding and aggregation.
  It is important to improve channel utilization because multiple channels can be used simultaneously.
DL MU-MIMO considered in 11ay can achieve higher throughput by multiplexing in spatial domain, but flexible multiplexing capability is getting important in dense environment.
  It is not easy to guarantee to obtain the rank for MU-MIMO.
  Multiplexing capability in spatial domain can be extended to frequency domain.
We consider frequency multiple access to improve channel utilization and to maximize multiplexing flexibility.

## Slide 3: Proposed technique: Frequency multiple access
Purpose
  Enhancement on channel utilization efficiency through allocating multi-channels to multi-users.
Achievement of following features
  Mitigating high dense environments by concurrent channel access from multiple users and increase flexibility of channel utilization.
Main differences from 11ad and MU-MIMO.
  Multiple users can access to medium in multi-channels within a TxOP.

## Slide 4: Proposed resource unit per user: size of channel
Considering complexity in 11ay if frequency resource unit is size of channel, it can be feasible simply to support frequency multiple access.
  Multiplexing capability
    - Supporting up to 4 STAs simultaneously if the channels in 11ay are fully used.
  Scheduling and feedback overhead
    - It can be low compared to smaller RU because maximum number of STAs is 4.
  Impact on frame structure
    - MU-MIMO frame structure considered in 11ay is easily reused.
  Complexity
    - Mostly reuse the parameter in 11ad and channel bonding (e.g. encoding block size, tone mapping).

## Slide 5: Conclusion
We proposed frequency multiple access as one of techniques to enhance performance in 11ay.
We proposed the size of granularity is the size of channel for simplicity of implementation and compatibility with other techniques.
We are open comments and feedbacks toward enhancing this proposal.

## Slide 6: Straw poll
Do you agree to insert the following in section 6.1 of the SFD:
  “11ay supports that when using multiple channels, a PCP/AP can simultaneously transmit to multiple STAs allocated to different channels individually.”

## Slide 7: Motion
Instruct the editor to insert the following in section 6.1 of the SFD:
  “11ay supports that when using multiple channels, a PCP/AP can simultaneously transmit to multiple STAs allocated to different channels individually.”