## Slide 1: Dwell Time In Probe Request Presentation
Date: 2016-01-18
Authors:

## Slide 2: Abstract
Communication of client channel dwell time in a probe request would help decrease the amount of airtime consumed by management frames particularly in a congested environment.

## Slide 3: Airtime Utilization in High Density Environment
Management Traffic can consume substantial amounts of airtime.
  Beacons up to 8-9%
  Probe Responses up to 9-10%

## Slide 4: Probe Response Problem in Congested Network
If an AP cannot successfully transmit a Probe Response in the client Off Channel Scan dwell time, a significant amount of airtime may be consumed for Probe Response management traffic by APs transmitting to a client that has changed channels.

## Slide 5: Probe Request Solution to Problem
Problem is solved by the transmission of dwell time, MaxChannelTime, in the broadcast Probe Request. AP2 will not send Probe Responses unnecessarily.