## Slide 1: LRLP potential technologies
Date: 2016-01-18
Authors:

## Slide 2: Background
LRLP Requirements
  Long range
    Approx. 10dB (20dB) improvement above existing 20MHz operation
  Ultra low power
    Average power reduction
    Peak power reduction
  Integration and backward compatibility with legacy 802.11
Potential technologies
  In most of use cases, longest range and Ultra low power may not required together
  LRLP STA and AP may apply different technologies due to different requirements.

## Slide 3: Potential technologies for longer range (1)
Signal duplication. 8x duplication can bring >10dB gain.
  Time domain duplication
  Frequency domain duplication
  Lower coding rate
  Combination of the above
    Example: ¼ rate FEC(DCM+MCS0) + 4x additional time/frequency domain duplication
    Comparing to MCS0, DCM + MCS0 can bring
      ~ 3dB gain in AWGN channel and
      ~5dB gain in D-NLOS channel (BW 20Mhz).
Data
Dup data
Data
Dup Data

## Slide 4: Potential technologies for longer range (2)
Narrow operation band to boost power density
  Reduce the operating BW can also bring SNR gain
    BW Reduce to 2MHz will bring ~ 10db SNR gain
With the combination of duplication and narrow BW, the SNR can be improved up to 20dB.
  Range and throughput will be a tradeoff
    Only ~81 Kbps throughput for 8x duplication of MCS0 signal on 2Mhz channel. This extreme case may only work for long range control usages.

## Slide 5: Potential technologies for lower power
Lower power requirement is more important at STA
  In some use case, STA may use coin battery only supporting limited peak power
  STA may have difficulty to recharge
Feasible technologies
  Lower peak power
    Narrow BW
      STA requires smaller peak power may only support smaller BW than AP to keep same range as AP.
  Lower average power
    Lower duty cycle
      Maximize the sleeping time for STA with constraint of latency requirement.

## Slide 6: Backward compatibility and coexistence
Backward compatibility
  Add spoofing preamble which is backward compatible before LRLP package
Hidden node problem might be very severe
  LRLP is coexist with legacy 802.11 devices but operation range is much larger.
  New protocol need to be designed to solve or mitigate the problem