## Slide 1: Functional Requirements for a .11az Range Measurement protocol operating 2.4/5 GHz bands
Date: 2016-01-19
Authors:
Name | Affiliation | Address | Phone | Email
Ganesh Venkatesan | Intel Corporation | 2111 NE, 25th Avenue, Hillsboro, OR 97124 | +1 503 334 6720 | Ganesh.venkatesan@intel.com
Jonathan Segev | Intel Corporation |  | +972 3 920 7038 | Jonathan.segev@intel.com

## Slide 2: Background
This document proposes a set of functional requirements for a .11az protocol operating in the 2.4 and 5 GHz bands that meets the accuracy and coverage goals established in thr PAR and CSD documents for the project

## Slide 3: Definition of Accuracy
<tbd-1>% of the set of computed estimates from uniformly distributed test locations (covering regions of interest) over a fixed test duration per test location are within <tbd-2>
  E.g. 90% of the set of computed estimates from uniformly distributed test locations over a fixed test duration per test location are within one meter
  Stated as <tbd-2>@<tbd-1> or less than <tbd-2>@<tbd_1> in the Use Case

## Slide 4: Functional Requirements (2.4/5 GHz)
The 802.11az range measurement protocol shall:
have a mechanism to obtain a range measurement that is more accurate than that obtained using legacy REVmc Fine Timing Measurement under the same conditions
support a mechanism to fallback to the legacy REVmc Fine Timing Measurement protocol
support concurrent FTM sessions in order for a STA to be able to perform range measurements with multiple APs (each operating in the same or different channels)
support range measurement in both the associated and the unassociated modes
support range measurement with an upper bound error of <TBD> m for 90% of uniformly sampled measurements.
For the purpose of simulation, 802.11az shall use 802.11n channel model D NLOS with 20MHz, 40MHz, 80MHz and 160MHz bandwidths