## Slide 1: What is the status of the ETSI BRAN work on a revised version of EN 301 893?
20 Jan 2015
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 2 84461010 +61 418 656587 | amyles@cisco.com
Notes
This presentation is an updated version of 802.11-15/1434r0 that was presented to the 802.11 WG mid session plenary in Nov 2015.
The updated presentation represents progress and status at the ETSI BRAN meeting in December 2015 in Mainz, Germany, with a focus on issues relevant to 802.11ax
That meeting was attended by a number of IEEE 802.11 WG members

## Slide 2: EN 301 893 revision is progressing in ETSI BRAN but more participation by Wi-Fi folk is encouraged
802.11 operation in Europe is based on EN 301 893 as authorised by European Directive 1999/5/EC
A revision of EN 301 893 is required by early 2016 to support a new European Directive 2014/53/EC
The work in ETSI BRAN revising EN 301 893 has been focused on a new adaptivity clause
RSC and TCAM have determined that fairness is a key requirement for adaptivity in the 5GHz band
ETSI BRAN made good progress in Oct 2015 on a new adaptivity clause but there were still important open issues … with some resolution in Dec 15
Scheduling issues make the development of new adaptivity clauses in EN 301 893 challenging!
New EN 301 893 is required
Most work is focused on fairness in adaptivity
Progress is being made but there are open issues
Companies that want to support Wi-Fi coexistence in Europe are encouraged to participate in ETSI BRAN or at least assist the effort

## Slide 3: 802.11 operation in Europe is based on EN 301 893 as authorised by European Directive 1999/5/EC
  IEEE 802.11 equipment is currently subject to requirements authorised by the European Directive 1999/5/EC
  EN 301 893 documents explicit requirements for operation in the 5GHz band in Europe, as authorised by 1999/5/EC, including:
    Frequencies
    Bandwidths
    Power
    Spurious emissions
    DFS
    Adaptivity
    …
  EN 301 893 also includes some simple tests against some of these requirements

## Slide 4: A revision of EN 301 893 is required by early 2016 to support a new European Directive 2014/53/EC
  A new EC Directive (2014/53/EC) repeals the previous EC Directive (1999/5/EC) on radio equipment
  The main objective of the new Directive is to provide:
    a high level of protection of health and safety, adequate level of electromagnetic compatibility and an effective and efficient use of radio spectrum so as to avoid harmful interference while guaranteeing the proper functioning of the internal market
  Essential requirements include requirements for effective & efficient use:
    Radio equipment shall be so constructed that it both effectively uses and supports the efficient use of radio spectrum in order to avoid harmful interference
  The new Directive comes into effect in June 2017 …
  … but EN 301 893 will need to be revised by early 2016 to allow approval and transition processes to be executed in time

## Slide 5: The work in ETSI BRAN revising EN 301 893 has been focused on a new adaptivity clause
  One key element of EN 301 893 is the adaptivity requirement
    Adaptivity is formally defined as an automatic channel access mechanism by which a device avoids transmissions in a channel in the presence of transmissions from other RLAN devices in that channel.
    There is an implicit goal of fair sharing of the channel, which is compatible with the goal of 2014/53/EC for effective channel use
  It is accepted that the current adaptivity clause in EN 301 893 needs a significant rewrite
    There is a desire to make EN 301 893 more “technology neutral”, which requires the removal of the direct reference to IEEE 802.11 in the current version
    The current version of EN 301 893 includes two “load based” and one “frame based” adaptivity mechanism that are known to not work
  ETSI BRAN has been focusing on developing a new adaptivity clause in EN 301 893 since December 2014

## Slide 6: RSC and TCAM have determined that fairness is a key requirement for adaptivity in the 5GHz band
  The requirement for fairness is implicit rather than explicit in the European Directive 2014/53/EC
  Fortunately, a meeting of two European Commission committees on 8 Oct 2015 provides clarity
    Radio Spectrum Committee (RSC)
    Telecommunications Conformity Assessment & Market Surveillance Committee (TCAM)
  In a discussion on Compliance of 5 GHz RLANs and LTE unlicensed use in the 5 GHz band (compatibility with other radio applications, coexistence between Wi-Fi and LTE unlicensed) they determined that:
    … coexistence means the fair use of the spectrum, which should ensure equal access for all technologies and applications …

## Slide 7: ETSI BRAN made good progress in Oct 2015 on a new adaptivity clause but there were still major open issues
  At the ETSI BRAN F2F meeting in Oct 2015 it was agreed to base future discussions on EN(15)150r2 (available via liaison agreement)
  This document includes some important agreements, with the most fundamental being it incorporation of LBT with exponential back using a scheme very similar to EDCA
  It also documents a variety of open issues
    Most of the issues are minor or editorial and will be resolved over time after ongoing discussions
    Three open issues can be described as “major”
  The major open issues are:
    What is the definition of the energy detect (ED) threshold?
    What is an appropriate value of max TxOP?
    What are the multi-channel requirements?

## Slide 8: ETSI BRAN came to tentative agreements in Dec 2015 on three major issues but there are still open issues
  In Dec 2015, ETSI BRAN agreed on compromises for three major issues
    ED threshold: -72dBm default with exception for 802.11a/n/ac
    Max TxOP: 6ms default with exceptions sometimes for 8ms and 10ms
    Multi-channel: two options, including one that is similar to 802.11
  However, there are still open issues that for which agreement is required
    Can devices transmit energy for the sole purpose of stopping others accessing the medium?
    Can devices send low priority traffic in high priority TxOPs?

## Slide 9: What is the definition of the ED threshold? There were two options on the table in Oct 2015 …
“Evidence based” proposal enables fair coexistence
  Proposal
    ED of -62dBm and PD of -82dBm (like Wi-Fi); OR
    ED of ~-77dBm
  Comments
    The first choice is based on status quo for billions Wi-Fi devices
    The second choice is based on 3GPP simulations that show LAA needs ED of ~-77dBm to coexist fairly with Wi-Fi
    Note: It is asserted many Wi-Fi devices do not satisfy these rules
“Alternate” proposal requires us to trust 3GPP to share fairly
  Proposal
    ED of -62dBm
  Comments
    Based on the idea that 3GPP can be trusted to define LAA in such a way that it maintains fairness …
    … and that all implementers in this band will follow 3GPP rules!

## Slide 10: … in Dec 2015 there was a compromise in relation to ED threshold but there may be questions for 802.11
Discussion on ED
  LAA folk advocated a uniform ED threshold of -72dBm
    Assuming 20MHz channels
  Wi-Fi folk advocated that LAA use ED between -77dBm and -72dBm
  Regulators did not want to provide 802.11 with a broad exception to use its usual ED/PD parameters … but agreed that an exception for existing specific dated amendments (eg 802.11ac) is acceptable
  Which all led to a compromise …

## Slide 11: … in Dec 2015 there was a compromise in relation to ED threshold …
Compromise on ED
  The ED threshold for a 20MHz channel is defined to be less than
    Min (-62 dBm, Max (-72 dBm, -72dBm + (23dBm – Pmax))),
    … where Pmax is the device’s maximum configured transmission power in dBm
    … and it is assumed that Pmax is changed only infrequently
  The ED threshold for a 20MHz channel is defined to be less than -62dBm if the device also does PD at less than -82dBm
    PD is as defined by IEEE 802.11-2012 & IEEE 802.11ac-2013
    This option is only available for use by equipment that only include 5 GHz (PHYs) defined by IEEE 802.11-2012 & IEEE 802.11ac-2013
  Part of this proposed compromise is to remove the technology specific option from the next version of this standard
    This gives time for the transition to 802.11ax

## Slide 12: … but there may be questions for 802.11 in relation to ED threshold
Questions on ED
  Is ED = -72dBm acceptable for 802.11ax?
    Would we want a different threshold if we “know” the other guy is 802.11?
  When would be want the transition to -72dBm occur for 802.11a/n/ac equipment?

## Slide 13: What is an appropriate value of max TxOP? There were at least two proposals on the table in Oct 2015
Wi-Fi based max TxOP enables proven fairness
  Proposal
    6ms
  Comments
    Value is compatible with max frame length in 802.11
    Value based on extensive 3GPP simulations that show fairness between LAA & Wi-Fi, particularly for real time QoS traffic
    Note: it is asserted many Wi-Fi devices do not satisfy this rule
LTE based max TxOP promotes efficiency over fairness
  Proposals
    10ms; OR
    6ms DL + 6ms UL; OR
    8ms (compromise?)
  Comments
    Use of larger value promotes efficiency over fairness
    Longer value allows for UL and DL in LAA, as well as LTE protocol derived delay between DL ending and UL starting

## Slide 14: … in Dec 2015 there was a compromise in relation to TxOP threshold but there is still work to be done
Discussion on max TxOP
  LAA has specified a max TxOP = 8ms
  Some Wi-Fi folk argued that this value was not justified by evidence in 3GPP TR, which showed 4ms led to fair sharing and 10-13ms probably didn’t especially for voice
  Other Wi-Fi folk noted that Wi-Fi sometimes needs very long TxOPs (~10ms) for sounding packets
  LAA folk seemed happy with 6ms for downlink only …
  … but wanted 8ms for up/downlink with a gap between the up link and the down link

## Slide 15: … in Dec 2015 there was a compromise in relation to TxOP threshold …
Compromise on max TxOP
  Max TxOP = 6ms is available for 100% of the time
    This is the default
  Max TxOP = 8 ms is available for 100% of time with a minimum pause of [TBD] µs (in order of 100’s µs) after a maximum transmission of 6 ms
    “Paused TxOP” concept for down/up link with gap in LAA
    LBT for 25us occurs before the paused TxOP restarts
  Max TxOP = 8 ms is available for [TBD1] % of the time
    May not be required
  Max TxOP = 10 ms is available for [TBD2] % of the time
    To allow some long TxOPs for 802.11 sounding

## Slide 16: … but there is still work to be done to select the max TxOP parameters
Ongoing work on max TxOP
  ETSI BRAN need to determine values of TBD, TBD1, TBD2
    Will be determined by combination of simulation and negotiation
    A Wi-Fi company is currently doing simulatsions
  Does IEEE have a view?
    Does 802.11 really need 10ms TxOPs for sounding?
      If so, how often?
    Are there other reasons for really long TxOPs?
    …

## Slide 17: What are the multi-channel requirements? There were at least two proposals on the table in Oct 2015
Wi-Fi based multi-channel promotes LAA/Wi-Fi fairness
  Proposal
    Use a primary/secondary multi-channel similar to 802.11
  Comments
    Using same mechanism as Wi-Fi guarantees fair sharing
Looser multi-channel prioritises efficiency over fairness
  Proposal
    Allow all of the multiple channels to be a primary channel and once access gained, allow the remaining channels to be a secondary channel
  Comments
    This mechanism allows LAA to make more efficient use of multiple channels …
    … but at cost of unfair access to the channel compared with Wi-Fi

## Slide 18: … in Dec 2015 there was a compromise in relation to multi-channel
Compromise on multi-channel
  All technologies will follow the same 20 MHz nominal raster for operating in the 5 GHz spectrum
    Note: a deviation from the nominal channel central frequency is allowed (200/300 kHz (to be discussed))
  Two options will be allowed
    Alternative 1: For systems that want to use multiple channels, and that will do a full LBT on each 20 MHz channel, can do any combination/grouping of 20 MHz channels.
    Alternative 2 (similar to 802.11 multi-channel): For systems that want to use multiple channels and only do a full LBT in one channel (primary channel) and do a short LBT in the secondary channel(s) shall follow a Wi-Fi like channel bonding plan

## Slide 19: There is an open issue in ESTI BRAN related to sending energy to stop others accessing the medium
  In LAA, there is delay of 0-1 ms between gaining access to the channel and the start of the sub-frame, which is a result of LAA sub-frames always being aligned to 1 ms boundaries
    The delay is 0.5 ms if partial sub-frames are used
  The only way for the LAA system to stop another system from accessing the channel during this delay is to transmit energy on the channel
  This energy represents a form of interference because its sole purpose is to stop other systems from accessing the channel
  This issue is still being discussed in ETSI BRAN; it is controversial because LAA would need major architectural changes to avoid such interference
  Does this debate have any impact on 802.11ax?

## Slide 20: There is an open issue in ESTI BRAN related to sending low priority traffic in high priority TxOPs
  In 802.11, a TxOP gained using particular priority level parameters can only be used to transmit frames of that priority or higher priorities
    There is an exception in MU-MIMO in which lower priority traffic while high priority data is being transmitted in parallel
  In contrast, it appears LAA will allow lower priority traffic to fill the remainder of a sub-frame if all higher priority traffic has been transmitted
  The argument was made during ETSI BRAN discussions on this topic was that the LAA sub-frame is of fixed length and it is better to fill the remainder of the LAA sub-frame with something rather than waste it
  The counter argument is that the LAA sub-frame should use lower priority access parameters if lower priority traffic must be transmitted when there is not enough high priority traffic
  Does this debate have any impact on 802.11ax?

## Slide 21: Scheduling issues make the development of new adaptivity clauses in EN 301 893 challenging!
  EN 301 893 needs to be finished very soon, but probably by March 2016 at the latest to allow time for approval and transition
  At the same time:
    3GPP is developing LAA with a nominal completion date of March 2016, but probably later
    … and IEEE 802.11 WG is developing 802.11ax, with a nominal completion date of ~1919
    … and billions of IEEE 802.11a/n/ac need to remain compatible with the EN 301 893 revision
  The challenge is that a revision of EN 301 893 needs to enforce fair sharing of the 5GHz band …
    between technologies that already exist
    and multiple technologies in various stages of development
  … without unduly limiting innovation

## Slide 22: There were two proposals in Oct 2015 in ETSI BRAN to address the scheduling challenge
“Two step” is based on what we know at various times
  Proposal
    Define EN 301 893 based on what we know about LAA/802.11a/n/ac coexistence today
    Once complete start a new project to revise it again once we know more about LAA and LAA/802.11ax coexistence
  Comments
    This approach is a nice balance between allowing innovation, while ensuring coexistence and not risking the immense value of Wi-Fi today
“One step” is based on trusting all to do the “right thing”
  Proposal
    Define EN 301 893 once with very broad constraints to ensure innovation is not constrained
  Comments
    This approach relies on 3GPP (and promoters of other technologies) to design their protocols to share fairly
    It also puts the ability of Wi-Fi to fulfil the promise of “anyone, anytime, anyplace can put together a network that meets their needs” at risk

## Slide 23: There was an implicit agreement for the two step approach at the ESTI BRAN meeting in Dec 2015
  Some stakeholders disagreed with a two step approach to defining the ETSI BRAN requirements
  While there was no explicit discussion of this issue in Dec 2015, it was implicitly decided that the requirements will evolve over time
  In particular, it was agreed that the “ED exception” for 802.11a/n/ac equipment would be removed at some time in the future
  It is not yet clear if this agreement will extend to revising the requirements “once we know more about LAA and LAA/802.11ax coexistence”

## Slide 24: Companies that want to support fair Wi-Fi/LAA coexistence in Europe are encouraged to participate
  The goal of todays presentation is twofold
    Inform IEEE 802.11 WG about the work being done in Europe to protect the huge socioeconomic value derived from Wi-Fi (noting this work will have an indirect impact on sharing in the US and around the world)
    Encourage IEEE 802.11 WG members to participate in the ETSI BRAN process - the companies that have supported Wi-Fi in this forum are few in number but have had a massive impact – thank you!
  If your company is an ETSI member then you can participate in a
    F2F meeting in Nice on 8-12 February 2016
  If you are not an ETSI member you can still help by contributing to the work of those companies supporting Wi-Fi in ETSI BRAN
  Contact Andrew Myles (amyles@cisco.com) for details