## Slide 1: 60GHz Functional Requirements
Date: 2015-12-15
Authors:

## Slide 2: Abstract
This document contains several functional requirements for 60GHz based on the 60GHz usage model.

## Slide 3: Remainder – 60GHz usages
Id | Name | Latency | Accuracy | Refresh | #AP/#STAs
1 | Nano Location in Store | 10ms | 1cm/10deg | 10Hz-100Hz | 
2 | Augmented Reality | 10ms | 1cm | 0.5Hz-100Hz | 3/1
3 | Determine dynamic Room Setup | 0.5sec | 20cm/20deg | 2Hz | 3/30
4 | Proximity Detection | 200ms | 5cm | 2Hz | 1/1
5 | Determine Relative Location to Docks | 200ms | 30cm/20deg | 1-10Hz | 7/12
6 | Wearable Devices | 10ms | 1cm/5deg | 0.5-100Hz | 3/8
7 | Control consoles | 100m | 1cm/100ms |  | 

## Slide 4: Functional Requirements
Id | Requirement | Usages
R13 | The 802.11az amendment shall support at least one mode of operation that enables range measurement in the 60GHz band with an accuracy of 1cm, @90%. | 1,6
R14 | The 802.11az amendment shall support at least one mode of operation that enables AOA/DOA measurement in the 60GHz band with an accuracy of 5deg, @90%. | 1,6
R15 | The 802.11az amendment shall support at least one mode of operation that enables range/AOA measurement in the 60GHz band with a latency of 10ms | 1,6
R16 | The 802.11az amendment shall support at least one mode of operation that provides location using a single link range and angle measurement | 5,1,2
R17 | The 802.11az amendment shall support at least one mode of operation at 60GHz that enables range measurement at a minimum distance of at most 5 cm | 4 (CCA)
R18 | The 802.11az amendment shall support at least one mode of operation at 60GHz that enables concurrent location measurement of 12 users and 7APs over the same 60GHz channel. | 5

## Slide 5: Straw Poll
Do you agree to add the functional requirements to the TGaz functional requirements document
Yes/No/Abstain