## Slide 1: Possible Solutions for Mobile Offloading Use Case
Date: 2016-03-11
Authors:

## Slide 2: Abstract
This submission proposes three possible solutions for blocking and short coverage which are issues for mobile offloading use case.

## Slide 3: Background
Mobile Offloading has been considered as one of TGay use cases, and ranked as the second “Main Stream” use case in WFA feedback. [1][2]
11ad/aj/ay will be very important options for mobile devices to support some Gbps throughput.
  11ay could act as the leading role in the next generation mobile communication when offloading would be more convenient at some public places (cafes, train stations, waiting spots, etc.) rather than home/enterprise use cases.
Blocking and short coverage are issues for such environment.

## Slide 4: Reflected Path
Reflector
Blocker
Reflected path compensates blocked LOS path.
Blocker
Any reflected path would compensate data communication even in case that all LOS paths with multi-Array are blocked.
Single array case
Multi array case
Reflector
AP
STA
AP
STA

## Slide 5: Proposal #1 Remote RF Head (RRH)
RRH
Blocker
RRH may be a solution for this issue.
Spatially bigger path diversity by RRH will moderate blocking issue.
Blocker
It will not be compensated even in multi-array case when there is no
effective reflected path.
AP
STA
AP
STA

## Slide 6: Fast Session Transfer (FST)
FST virtual MAC
Virtual MAC addr: MAC_virtual1
MAC 60
MAC 5
PHY 5
PHY 60
PHY 60
PHY 5
MAC 5
Physical MAC addr: MAC1
MAC 60
Physical MAC addr: MAC2
IP
AP
FST STA
FST virtual MAC
Virtual MAC addr: MAC_virtual0
Association with MAC1
Association with MAC2
Data transfer using MAC_virtual
FST
Forwarding decision
FST was defined in 11ad to compensate 60GHz unavailability due to blocking or coverage gap/shortage by prompt switching to 2.4/5GHz.
Ref: [6]

## Slide 7: Proposal #2 FST in 11ay Use Case
Backhaul NW
It could be fundamental for a 5GHz AP to compensate multiple 60GHz APs’ area gap to cover street, shopping mall, stadium, train station, etc. In such case, FST will be necessary among a 5GHz and multiple-60GHz AP.
11ay
AP
5GHz
AP
11ay
AP
11ay
AP
Blue: 5GHz range
Gray: 60GHz range
virtual MAC
virtual MAC
MAC 5
PHY 5
MAC 5
PHY 5
MAC 60 #1
PHY 60 #1
PHY 60
MAC 60
MAC 60 #2
PHY 60 #2
MAC 60 #3
PHY 60 #3
IP
AP
STA
roaming
FST among multi-11ay link

## Slide 8: Proposal #3 Link Aggregation
Link aggregation between 2.4/5GHz and 11ay will be a solution as one of FST.
virtual MAC
virtual MAC
MAC 5
PHY 5
MAC 5
PHY 5
MAC 60 #1
PHY 60 #1
PHY 60
MAC 60
MAC 60 #2
PHY 60 #2
MAC 60 #3
PHY 60 #3
IP
AP
STA
roaming
Link Aggregation in 802.11
Ref. LTE Wi-Fi Aggregation (LWA)
UE
eNB
GW
WLAN
AP
Tunneling
packet core

## Slide 9: Summary
This contribution proposed the following three possible solutions to compensate blocking and short coverage for mobile devices:
  Remote RF Head (RRH)
  Multi-Millimeter FST (Definitive name is TBD)
  Link Aggregation

## Slide 10: Straw Poll #1
Do you think RRH (Remote RF Head) will be effective to improve space diversity in mobile use case?
Y:
N:
Need more studies:

## Slide 11: Straw Poll / Motion #2 (if SP#1 was supported)
Do you agree to add the following text into the TGay functional requirements document?
11ay amendment addresses “Remote RF Head (RRH)” features as an option to improve space diversity effectiveness.

## Slide 12: Straw Poll / Motion #3
Do you agree to add the following text into the TGay functional requirements document?
11ay amendment addresses the following types of FSTs between 2.4/5GHz WLAN to compensate blocking and short coverage:
  Multi-Millimeter FST
  Link Aggregation

## Slide 13: References
[1] “IEEE 802.11 TGay Use Cases”, IEEE802.11-15/625r3
[2] “20150707 Wi-Fi Alliance feedback on 802.11 Task Group AY usage models”, IEEE802.11-15/934r0
[3] “TGay Functional Requirements”, IEEE802.11-15/1074r0
[4] “Specification Framework for TGay”, IEEE802.11-15/1358r2
[5] “A Framework for MIMO Operation over mmWave Links”, IEEE802.11-15/334r1
[6] “Fast Session Transfer”, IEEE802.11-10/491r1
[7] “