## Slide 1: Liaison from 3GPP on LWA and LWIP
Date: 2016-03-11
Authors:

## Slide 2: Abstract
The following slides are an incoming Liaison from 3GPP on LWA and LWIP for presentation to 802.11.
The 802.11 WG chair has granted permission for these slides to appear in 3GPP format along with 3GPP logos, as this is an incoming liaison to 802.11.

## Slide 3: LTE-WLAN Aggregation (LWA) and LTE WLAN Radio Level Integration with IPsec Tunnel (LWIP)
Richard Burbidge,
3GPP RAN2 WG chair

## Slide 4: Outline
Introduction
LTE-WLAN Aggregation (LWA)
LTE WLAN Radio Level Integration with IPsec Tunnel (LWIP)
Next steps
References

## Slide 5: Introduction
Unlicensed spectrum is becoming increasingly important for cellular operators
To cater to operators’ demand, in Release-13 3GPP have defined a number of WLAN interworking features:
  LTE-WLAN Aggregation (LWA)
  LTE WLAN Radio Level Integration with IPsec Tunnel (LWIP)

## Slide 6
LTE-WLAN Aggregation (LWA)

## Slide 7: LWA: Overview
Allows aggregating LTE and WLAN at RAN level
WLAN AP/AC only interacts with the LTE eNB; no interaction with LTE Core Network
Key drivers: performance, mobility, eliminating need for WLAN-specific Core Network nodes
LWA is controlled by E-UTRAN Node B(eNB), based on User Equipment (UE) measurement reporting
Formally completed at RAN#71 in March

## Slide 8: LWA: Data Plane
LWA allows a single bearer to be configured to utilize LTE and WLAN simultaneously
  Split and switched bearers are supported
In Release-13, LWA supports aggregation in downlink only, while uplink transmission is always on LTE
Packets (PDCP PDUs) belonging to LWA bearer can be sent by eNB via LTE or WLAN simultaneously
  eNB can do packet-by-packet scheduling, based on measurements (LTE and WLAN) and feedback from WLAN
PDCP PDUs sent via WLAN are encapsulated in LWA Adaptation Protocol (LWAAP) which carries bearer identity
  To allow offloading of multiple bearers to WLAN
LWA uses EtherType 0x9E65 allocated by IEEE RAC

## Slide 9: LWA: Network Architecture
LWA supports two deployment scenarios:
  Collocated – integrated eNB and WLAN Access Point (AP)/Access Controller (AC)
  Non-collocated – eNB and WLAN AP/AC connected via WLAN Termination (WT) using standardized interface Xw
Xw interface terminates in WT logical node
Deployment choice to integrate the WT into AC, APs or deploy as a standalone network node
How information is exchanged between WT and APs/ACs is out of 3GPP scope
Xw supports control and data plane

## Slide 10: LWA: Control Plane
LWA activation and deactivation are controlled by eNB
eNB configures WLAN mobility set for UE
  Based e.g. on WLAN measurements reported by UE
WLAN mobility set is a group of WLAN APs identified by SSID(s), HESSID(s) or BSSID(s)
  Mobility set is UE-specific and there is only one set configured for UE at a time
  All WLANs in mobility set are connected to the same WT
Mobility within WLAN mobility set is controlled by UE, i.e. transparent to eNB
Mobility outside of WLAN mobility set is controlled by eNB
When LWA is activated, eNB configures one or more bearers as LWA bearers

## Slide 11: LWA: WLAN Measurements
UE supporting LWA shall support WLAN measurement reporting
Measurement configuration includes: WLAN ids, WLAN band and frequency/channel
Measurement reporting is triggered by RSSI thresholds
Measurement report contains: WLAN ids, RSSI, STA count, backhaul rate, admission capacity, channel utilization and other metrics
Three WLAN measurement events are defined:
  Event W1: WLAN becomes better than a threshold;
  Event W2: All WLAN inside WLAN mobility set become worse than a threshold1 and a WLAN outside WLAN mobility set becomes better than a threshold2;
  Event W3: All WLAN inside WLAN mobility set become worse than a threshold.
WLAN measurement framework is common to LWA and LWIP
There are separate UE capability indications for LWA, LWIP and WLAN measurements

## Slide 12: LWA: WLAN security
Even though WLAN payload is encrypted (by PDCP), 3GPP decided to use WLAN security including encryption, authentication, and integrity protection
EAP/AKA 802.1x based authentication may take time, and may not be possible due to CN connectivity not being available, therefore 3GPP decided to define an optimized WLAN authentication procedure
  EAP/AKA may still be used with LWA, i.e. optimized authentication is optional
When optimized WLAN authentication is used:
  eNB derives a key (S-KWT) based on KeNB and WT Counter
  eNB sends S-KWT to WT via secure Xw interface, WT makes it available to APs/ACs which belong to UE WLAN mobility set
  UE derives the same S-KWT key autonomously (based on WT Counter received from eNB and KeNB
  S-KWT used as the Pairwise Master Key (PMK) in 4-way handshake as defined in IEEE 802.11

## Slide 13: LWA: Xw Control Plane
Xw Application Protocol (Xw-AP) is used on the Xw control plane interface
Xw-AP supports the following procedures: WT Addition Preparation, eNB or WT Initiated WT Modification, WT Status Reporting, WT Association Confirmation, eNB or WT Initiated WT Release and others
WT Addition Request is used by eNB to request preparation of resources for LWA in WT
  It carries: UE id, WLAN security key, bearer information (including QoS), WLAN mobility set and other
WT Modification Request is used by eNB to modify mobility set, security key or bearers configured for LWA for a UE
WT Status Report is used by WT to report WLAN measurements per BSS
  It carries: BSSID, bss load, WAN metrics and available channel utilization
WT Association Confirmation is used by WT to indicate that a UE successfully connected to WLAN

## Slide 14: LWA: Xw Data Plane
Xw data plane uses GPRS Tunnelling Protocol for User Plane (GTP-U) on top of UDP for data transfer from eNB to WT
Downlink stream is used for data forwarding
Uplink stream is used for feedback/flow control
Optional Downlink data delivery status procedure is used by WT to indicate its buffer status and lost PDUs to eNB
Every PDU is assigned a Xw-U sequence number

## Slide 15: LWA: UE Feedback
Provisions have been made to allow LWA deployment with limited WLAN infrastructure impact
If WT does not support feedback/flow control, eNB may trigger status reporting from UE on air interface (at PDCP layer) using either:
  PDCP status report: First Missing PDCP SN, bitmap of received PDCP SDUs
  LWA status report: First Missing SN (FMS), Number of Missing PDUs (NMP) and Highest Received SN on WLAN (HRW)
NOTE: eNB can derive information about packets lost on LTE from RLC layer, since only RLC Acknowledged Mode (AM) is allowed for LWA
If configured by the eNB, the UE reports association confirmation on air interface (at RRC layer)

## Slide 16: LWA: illustration
1,2 - UE indicates LWA support, including its MAC address (performed only once, not on every LWA activation)
3,4 – eNB configures WLAN measurements
5, 6 – UE reports WLAN meeting configured thresholds
7,8 – eNB indicates to WLAN via WT UE identity, bearer configuration including QoS and WLAN security key
9, 10 – eNB activates LWA, configuring: mobility set, LWA bearers and security key
11 – UE find suitable AP, associates, authentications using 4-way handshake
12 – WT (or UE) indicate successful connection to WLAN
13 – data is sent on LTE and WLAN
14 – if supported, WT sends feedback/flow control information
15 – if configured, UE continues measurement reporting
16 – if configured, UE sends feedback/flow control information

## Slide 17
LTE WLAN Radio Level Integration with IPsec Tunnel (LWIP)

## Slide 18: LWIP: Overview
UE uses WLAN via IPsec tunnel between eNB and UE
Key drivers: fast time to market, use of legacy WLAN infrastructure
WLAN is hidden from CN
  Except for WLAN authentication
LWIP is controlled by eNB, based on UE measurement reporting
For security reasons IPsec tunnel is terminated in LWIP-SeGW in eNB
IPsec tunnel is transparent to WLAN infrastructure
  There are no standardised network interfaces in LWIP
Single IPSec tunnel per UE for UL and DL data
Formally completed at RAN#71 in March
MME
/
S
-
GW
S
1
WLAN
eNB
UE
LWIP-SeGW
IPsec

## Slide 19: LWIP: Data Plane
Uplink and downlink data supported over WLAN
Multiple bearers can be offloaded via IPSec
In uplink, PDCP SDUs are encapsulated in Generic Routing Encapsulation (GRE) protocol
  GRE Key carries bearer identifier
Bearer differentiation is not needed in downlink
No re-ordering support: eNB in DL and UE in UL are not expected to send packets on a data radio bearer via LTE and WLAN simultaneously

## Slide 20: LWIP: Control Plane
Activation and deactivation is controlled by eNB
When LWIP is activated
  eNB sends WLAN mobility set, bearer information and LWIP-SeGW IP address
  After WLAN association and EAP/AKA authentication, UE establishes IPSec connection with LWIP-SeGW using IKE
  IPsec keys are derived (by eNB and UE) based on KeNB
Re-uses same WLAN measurement reporting framework as LWA
Re-uses same WLAN mobility concept as LWA

## Slide 21: LWIP: illustration
1,2 - UE indicates LWA support, including its MAC address (performed only once, not on every LWA activation)
3,4 – eNB configures WLAN measurements
5, 6 – UE reports WLAN meeting configured thresholds
7,8 – eNB activates LWIP, configuring: mobility set, bearers and LWIP-SeGW IP address
9 – UE find suitable AP, associates, authentications using EAP/AKA
10 – if configured, UE sends association confirmation
11 – UE acquires IP address
12 – UE establishes IPsec tunnel to LWIP-SeGW
13 – data is sent on LTE or IPsec
14 – if configured, UE sends feedback/flow control information
Notes: What do bold arrows distinguish?

## Slide 22: LWA vs. LWIP
 | eNB control | WLAN measurements | Offload granularity | Feedback/ flow control | WLAN traffic direction | Fast WLAN authentication | WLAN infrastructure impact | New network nodes
LWA | Yes | Yes | Split bearer | Yes | DL only | Yes2 | Yes4 | WT
LWIP | Yes | Yes | Bearer1 | No | DL + UL | No3 | No | LWIP-SeGW
When a bearer is configured to use IPsec, LTE DRB configuration remains, however eNB is not expected to send packets on LTE and IPsec simultaneously, as LWIP does not support re-ordering
After connecting to WLAN, LWA UE only performs 4-way handshake (if network uses the eNB based authentication)
After connecting to WLAN, LWIP UE performs 802.1x EAP/AKA authentication, IP address acquisition and IPsec tunnel establishment
Impact due to eNB based authentication mechanism, if used by network. Optional UE feedback mechanisms (as opposed to network feedback) allow to limit WLAN infrastructure impact of LWA

## Slide 23: Next steps
3GPP RAN5 will work on the definition of test cases for LWA
3GPP RAN2 and RAN3 will work on Enhanced LWA (eLWA) in Release-14
  Uplink support, enhanced mobility, optimizations for high data rate 802.11 technologies (802.11ax, 802.11ad and 802.11ay)
3GPP RAN has approved a 5G requirement on interworking with non-3GPP and will continue working on this

## Slide 24: References
LWA
  Stage-2 high level description – TS 36.300, section 22A.1
  Stage-3 data plane (PDCP) – various sections in TS 36.323
  Stage-3 data plane (LWAAP) – TS 36.360
  Stage-3 control plane (RRC) – various sections in TS 36.331
  Stage-3 control plane network interface (Xw) – TS 36.463, TS 36.462, TS 36.461
  Stage-3 data plane network interface (Xw) – TS 36.465. TS 36.464
  Stage-3 security aspects – TS 33.401, section X (section number to be allocated)
LWIP
  Stage-2 high level description – TS 36.300, section 22A.3
  Stage-3 control plane (RRC) – various sections in TS 36.331
  Stage-3 data plane – TS 36.361
  Stage-3 security aspects – TS 33.401, section Y (section number to be allocated)
Specifications are available for download here: http://www.3gpp.org/ftp/Specs/latest/Rel-13/

## Slide 25
www.3gpp.org
For more Information:
contact@3gpp.org
Search for WIDs at http://www.3gpp.org/specifications/work-plan and http://www.3gpp.org/ftp/Information/WORK_PLAN/ (See excel sheet)