## Slide 1: Further consideration for MU-RTS/CTS
Date: 2016-03-14
Authors:

## Slide 2: Background
MU-RTS/CTS operation is described in the proposed draft[1]
  Based on the RU allocation in the Per-User Info field addressed to the STA, the CTS must be transmitted on the primary 20 MHz channel, primary 40 MHz channel, primary 80 MHz channel, 160 MHz channel, or 80+80 MHz channel.
  Other indications are TBD.
  The CTS sent in response to an MU-RTS frame shall be transmitted on one or more 20 MHz channels.

## Slide 3: Background
The diagrams in the draft specification seems to indicate that the assignment of one or more 20MHz channels must be contiguous
  Example of MU-RTS/CTS/Trigger/HE trigger-based PPDU/ Multi-STA BlockAck and NAV setting[1]

## Slide 4: Background (con’t)
Additional example of MU-RTS and CTS responses on the primary 40MHz channel[1]

## Slide 5: Proposal
The AP can assign one or more 20MHz channels non-contiguously to further improve the utilization
  (Current) Based on the RU allocation in the Per-User Info field addressed to the STA, the CTS must be transmitted on the primary 20 MHz channel, primary 40 MHz channel, primary 80 MHz channel, 160 MHz channel, or 80+80 MHz channel.
  (Current) The CTS sent in response to an MU-RTS frame shall be transmitted on one or more 20 MHz channels.
  Other indication is TBD -> Proposal:
    For an STA, the secondary 20 MHz channel, secondary 40 MHz channel needs not be contiguous to the primary 20.

## Slide 6: Proposal (con’t)
  For an STA, the secondary 20 MHz channel, secondary 40 MHz channel needs not be contiguous to the primary 20.
E.g.
For STA 2:

## Slide 7: Conclusions
In this contribution, we suggested that the AP can assign one or more 20MHz channels non-contiguously to further improve the utilization

## Slide 8: SP
Do you agree to add the following to the 4.4.z of 11ax TG SFD:
  For an STA, the secondary 20 MHz channel, secondary 40 MHz channel needs not be contiguous to the primary 20.

## Slide 9: References
11-16/0024r1, Draft Specifications, March 2016
11-15/0132r15, Specification Framework for TGax, Jan 2016
Notes: As I mentioned the motivation is to further improve