## Slide 1: Considerations on Phase Noise Model for 802.11ay
Date: 2016-03-17
Authors:

## Slide 2: Motivation
Phase noise (PN) is one of the critical impairments in 60GHz band. It may significantly impact on the bit error rate, and yield synchronization problems.
In IEEE 802.11ad [1], PN characteristic is modeled as a one-pole-one- zero model, and applied in SYS/PHY simulations.
802.11ay introduces new use cases (e.g., wireless backhauling) and new features (e.g., MIMO), which will generate additional requirements on PN modeling.
This submission addresses this problem and proposes a new complementary PN model which may be better suitable for the 802.11ay simulation for these new cases or features.
Mar. 2016

## Slide 3: Phase Noise and its Effects
PN is a critical RF impairment, mainly occurred in oscillator.
  Even small amount of noise caused by an oscillator will lead to significant changes in its frequency spectrum and timing properties (timing jitter).
It may significantly affect system performance.
BPF
LNA
VGA
PA
PA drive
PLL (Osc.)
0
90
ADC
BPF
VGA
I/Q mod.
I/Q demod.
0
90
ADC
DAC
DAC
Phase-noise from VCO/PLL
BPF
VGA
Mar. 2016

## Slide 4: PLL Output Phase Noise Model
PLL (Phase-Locked-Loop) output model [2] is a typical PN model, and widely applied for carrier synchronization in communication system.
Its PN output is the synthesis of the noise in each building block.
Phase noise contributions for a normal PLL (termed Single Local Oscillator Structure)
Ref. Oscillator
Phase Detection
LPF
VCO
x N
Dominated Noise
Freq. Multiplier
(Optional)
1/N
Freq. Divider
noise
noise
noise
noise
noise
Phase noise characteristics for VCO and PLL [3]
Mar. 2016

## Slide 5: 802.11ad Phase Noise Model [1]
PN model in 802.11ad is a typical PLL output model that,
      PSD(0) = -90 dBc/Hz
      Pole frequency fp = 1 MHz
      Zero frequency fz = 100 MHz
      PSD (infinity) = -130 dBc/Hz
11ad theoretical result
pole freq.
zero freq.
Mar. 2016

## Slide 6: New Requirements on PN model for 802.11ay
Outdoor scenario and MIMO transmission in 11ay, which will pose changes on current Single LO Structure of 11ad.
      Wireless Backhauling: To compensate significant propagation losses, a feasible and economical approach is by composing a larger array with higher antenna gain based on several small arrays (left-handed figure);
      MIMO: Multi-stream is supported by multiple RF paths (right-handed figure);
It is necessary to implement Multiple LOs Structure in 802.11ay.
Mar. 2016

## Slide 7: Possible Multiple LOs Structures
Option A
Option B
Option C
A | Independent LO for each path/ no freq. multiplier
B | Independent LO & freq. multiplier for each path
C | Common oscillator/no freq. multiplier
D | Common oscillator & independent freq. multiplier for each path
Option D
Mar. 2016

## Slide 8: Partially Coherent Common LO Structure (1/2)
Among these multiple LOs structures, we prefer Option D “partially coherent common LO structure” for its advantages,
      Compared with Option A & B, less oscillators are used, which will reduce RF circuit cost;
      In addition, for MIMO transmission, maintaining some correlation characteristic of PN between each path will be helpful in MIMO detection (since advanced PN compensation/ immunity schemes are feasible);
PNs between these paths are partially correlated
Mar. 2016

## Slide 9: Partially Coherent Common LO Structure (2/2)
Among these multiple LOs structures, we prefer Option D “partially coherent common LO structure” for its advantages,
      Compared with Option A & C, reference source is first carried on fundamental frequency via common LO, and then carried to harmonical frequency. This procedure will reduce the feeder loss (since the feeder loss for the lower frequency signals is less);
Lower fundamental frequency signal
1.4 dB/in. @60GHz
2.2 dB/in. @60GHz
Measurements by Rogers Corp. [4]
Mar. 2016
Notes: Harmonical
Fundamental

## Slide 10: Proposed Phase Noise Model for 802.11ay
In this submission, we propose the following model for this partially coherent common LO structure, which is complementary to the PN model in 802.11ad
(treated as a Behavior Model)
Shared LO0
Ref. Oscillator
Ideal Freq. Multiplier
LO 1
x N
Freq. Multiplier Noise
LO 2
x N
Freq. Multiplier Noise
LO M
x N
Freq. Multiplier Noise
…
…
…
    where,
    PN(m) the output of phase noise in mth path LO, LOm
    PN0 the output of LO signal after ideal frequency multiplier, i.e.,
    the independent noise caused by frequency multiplier, and can be simplified as white noise which PSD = - 130 dBc/Hz
Mar. 2016

## Slide 11: How to Generate the Proposed Phase Noise for 802.11ay
AWGN
time
FFT
IFFT
freq.
freq.
(N-point)
PSD
fp
fz
p0
11ad Phase-noise characteristics
(red: original ; blue : omit background noise)
(N-point)
time
WGN1
Phase-noise @ path 1
WGN2
Phase-noise @ path 2
WGNM
Phase-noise @ path M
…
      In the figure above, WGNi is the independent white noise with PSD p0 = - 130 dBc/Hz
Mar. 2016

## Slide 12: Summary
New use cases and features in 802.11ay suggest new requirements on PN modeling.
For better performance evaluations, in this submission, possible multiple LOs structures are presented.
Partially coherent common LO structure is suggested for 802.11ay, and a complementary PN model is proposed accordingly .
Mar. 2016

## Slide 13: Backup: the relationship between the proposed model and 11ad PN model
Shared LO0
Ref. Oscillator
Ideal Freq. Multiplier
LO 1
x N
Freq. Multiplier Noise
LO 2
x N
Freq. Multiplier Noise
LO M
x N
Freq. Multiplier Noise
…
…
…
Ref. Oscillator
Phase Detection
LPF
VCO
x N
Freq. Multiplier
1/N
Freq. Divider
noise
noise
noise
noise
noise
noise
LO0
Each path in the partially coherent common LO can be equivalent to a single LO in11ad, with independent frequency multiplier noise.
Ideal Freq. Multiplier + Noise
PN0
Mar. 2016

## Slide 14: Backup: how to generate phase noise for 802.11ad
Source: IEEE802.15-06-0477-01-003c, “RF Impairment models for 60GHz-band SYS/PHY simulation”
Mar. 2016

## Slide 15: References
[1] IEEE802.11-09/1213r1, “60 GHz Impairments Modeling”
[2] W. Rosenkranz, “Phase-Locked Loops with Limiter Phase Detectors in the Presence of Noise”, IEEE Tran. Communications, vol.30, no.10, Oct. 1982
[3] IEEE802.15-06-0477-01-003c, “RF Impairment models for 60GHz-band SYS/PHY simulation”
[4] Rogers Corporation, “RO4000® Series High Frequency Circuit Materials”
Mar. 2016

## Slide 16: Motion
Would you agree to consider partially coherent common LO model shown on Slide 10 as a complementary PN model in 11ay performance evaluation and to be included in the 802.11ay Evaluation Methodology Document?
Y-N-A
Mar. 2016