## Slide 1: HE-SIG-B Signaling Discussions
Date: 2016-03-14
Authors:

## Slide 2: Introduction
In HE MU PPDU, HE-SIG-B field delivers multi user signaling information [1].
Also, TGax adopted non-contiguous channel bonding [2][3]
  The non-contiguous channel bonding will be supported in 802.11ax by:
    Transmitting using OFDMA PPDU format by nulling the tones of one or more secondary channels in 80 MHz and 160 (80+80) MHz;
    Modes for non-contiguous channel bonding are TBD;
    Non-contiguous channels within primary or secondary 80 MHz only exists at AP side.
In this submission, we discuss HE-SIG-B signaling details for the non-contiguous channel bonding

## Slide 3: Recap: HE-SIG-B
Two HE-SIG-B content channels are parallel-decoded at receiving STAs
RU allocation subfield signals RU arrangements in frequency domain and the number of User specific subfields
Signaling for the center 26 RU in 80MHz is TBD
S40 MHz
(C)
(D)
(A)
(B)
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-SIG-B
(A,C)
HE-
STF/LTF
L-Part
HE-
SIG-A
HE-SIG-B
(A,C)
Dup.
L-LTF
Dup.
HE-
SIG-A
HE-SIG-B
(B,D)
RU (C1)
RU (A1)
...
...
RU (Cn)
RU (B1)
...
RU (Bn)
RU (An)
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-SIG-B
(B,D)
RU (X)
RU (Dn)
...
RU (Dn)
P20 MHz
S20 MHz
C/T
STA
B1
STA
Bn
C/T
...
RA
B
C/T
HE-SIG-B
(A,C)
RA
C
RA
A
C/T
C/T
STA
A1
...
STA
An
C/T
C/T
STA
C1
STA
Cn
...
HE-SIG-B
(B,D)
RA
D
STA
D1
...
STA
Dn
STA
X
C/T
*C/T: CRC/Tail
1st content
channel
2nd content
channel
RU allocation
User specific subfield
TBD

## Slide 4: Signaling of non-contiguous channel-bonding
For DL OFDMA PPDU, tones of one or more secondary channels in 80MHz and 160(80+80) MHz can be nulled [2][3]
AP can signal non-contiguous channel based PPDU constructions by
  (A) Using SIG-A’s BW subfield
  (B) Using SIG-B’s RU allocation subfield
S40MHz
(C)
(D)
P20MHz
(A)
S20MHz
(B)
CCA
(idle)
CCA
(idle)
CCA
(busy)
CCA
(idle)
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-SIG-B
HE-
STF/LTF
L-Part
HE-
SIG-A
HE-SIG-B
Dup.
L-LTF
Dup.
HE-
SIG-A
HE-SIG-B
RU (C1)
RU (A1)
...
...
RU (Cn)
RU (B1)
...
RU (Bn)
RU (An)
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-SIG-B
RU (D1)
...
RU (Dn)
nulled channel
RU (X)
(A) BW
(B) RU allocation

## Slide 5: Signaling of non-contiguous channel-bonding
(A) Using SIG-A’s BW subfield
  In SU PPDU, SIG-A’s BW subfield signals 20/40/80/160(80+80) MHz bandwidths only
  In MU PPDU, SIG-A’s BW subfield is TBD that may accommodate more bandwidth options than in SU case
  11ax may extend SIG-A’s BW subfield in DL MU to explicitly signal multiple TBD non-contiguous bandwidth options (e.g. P20+S40)
  According to [2], BW subfield may require 3~7 bits according to channel bonding rules

## Slide 6: Signaling of non-contiguous channel-bonding
(B) Using SIG-B’s RU allocation subfield
  Add additional Null RU indices to the current RU allocation definition (currently there are many TBD index ranges)
  RU allocation subfield signals “242/484/996 Null” to indicate nulled secondary channels
  No user specific subfields are sent corresponding to the Null RUs
  No additional signaling overheads on SIG-A/B bit fields compared to the current design
  The Null RU indices can be reused in MU-MIMO signaling load balancing scenarios [4]
RA
D
C/T
STA
B1
STA
Bn
C/T
...
indices | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | # of Entries
... | ... |  |  |  |  |  |  |  |  | ...
TBD | 242 Null |  |  |  |  |  |  |  |  | 1
TBD | 484 Null |  |  |  |  |  |  |  |  | 1
TBD | 996 Null |  |  |  |  |  |  |  |  | 1
 | ... |  |  |  |  |  |  |  |  | 
RU allocation
S40MHz
(C)
(D)
P20MHz
(A)
S20MHz
(B)
CCA
(idle)
CCA
(idle)
CCA
(busy)
CCA
(idle)
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-SIG-B
(A,C)
HE-
STF/LTF
L-Part
HE-
SIG-A
HE-SIG-B
(A,C)
Dup.
L-LTF
Dup.
HE-
SIG-A
HE-SIG-B
(B,D)
RU (C1)
RU (A1)
...
...
RU (Cn)
RU (B1)
...
RU (Bn)
RU (An)
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-SIG-B
(B,D)
RU (X)
RA
B
C/T
STA
D1
STA
Dn
...
HE-SIG-B
(A,C)
RA
C
RA
A
C/T
C/T
STA
A1
...
STA
An
C/T
C/T
STA
C1
STA
Cn
...
HE-SIG-B
(B,D)
RU (D1)
...
RU (Dn)
nulled channel

## Slide 7: Signaling of non-contiguous channel-bonding
In 80MHz OFDMA there is the center 26 RU, and its signaling within HE-SIG-B content channels is TBD (e.g. 1st or 2nd, fixed or dynamic)
In non-contiguous channel PPDU, when a secondary channel adjacent to the center 26 RU is nulled, the center 26 RU also should be nulled
The proposed option (B) signaling can explicitly identify the existence of the center 26 RU even with the decoding failure of one SIG-B content channel
HE-SIG-B (A, C)
RA
242
(Null)
STA
A1
RA
A
C/T
...
STA
An
C/T
HE-SIG-B (B, D)
RA
D
STA
B1
RA
B
C/T
...
STA
Bn
C/T
STA
D1
...
STA
Dn
C/T
STA
X
C/T
HE-SIG-B (A, C)
RA
484
Null
STA
A1
RA
A
C/T
...
STA
An
C/T
HE-SIG-B (B, D)
RA
484
Null
STA
B1
RA
B
C/T
...
STA
Bn
C/T
STA
X
C/T
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-SIG-B
(A,C)
HE-
STF/LTF
L-Part
HE-
SIG-A
HE-SIG-B
(A,C)
Dup.
L-LTF
Dup.
HE-
SIG-A
HE-SIG-B
(B,D)
RU (C1)
RU (A1)
...
...
RU (Cn)
RU (B1)
...
RU (Bn)
RU (An)
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-SIG-B
(B,D)
RU (X)
RU (Dn)
...
RU (Dn)
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-SIG-B
(A,C)
HE-
STF/LTF
L-Part
HE-
SIG-A
HE-SIG-B
(A,C)
Dup.
L-LTF
Dup.
HE-
SIG-A
HE-SIG-B
(B,D)
RU (C1)
RU (A1)
...
...
RU (Cn)
RU (B1)
...
RU (Bn)
RU (An)
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-SIG-B
(B,D)
RU (X)
RU (D1)
...
RU (Dn)
nulled
channel

## Slide 8: Signaling of non-contiguous channel-bonding
We prefer option (B) using SIG-B’s RU allocation subfield to signal non-contiguous channel-bonding
HE-SIG-B transmission in secondary 20MHz
  With option (B), SIG-A’s BW subfield signals only 20/40/80/160(80+80) MHz BW
  Thus receiving STAs do not know the nulled secondary channels before SIG-B
  Therefore, 1/2 SIG-B content channels should be transmitted at least for Primary 40MHz to signal nulled secondary channels (unless there is no RUs to be signaled by 2nd SIG-B content channel)
  Possible ways
    Limit non-contiguous channel bonding rule to always occupy P40
    Transmit preamble parts even in nulled secondary channels (at least in S20)

## Slide 9: Conclusions
In this submission, we discussed signaling for non-contiguous channel-based PPDU
We propose 11ax to adopt the method that signals nulled secondary channels using SIG-B’s RU allocation subfields
  No additional signaling overhead increases
  Can explicitly identify the existence of the center 26 RU even with the decoding failure of one SIG-B content channel
  Added Null RU indices can be reused for the No user allocation signaling cases for MU-MIMO signaling load balancing scenarios

## Slide 10: References
  [1] 11-15/0132r15, Spec Framework Doc
  [2] 11-16/0045r1, Flexible Wider Bandwidth Transmission
  [3] 11-16/0059r1, Non-contiguous Channel Bonding in 11ax
  [4] 11-16/0039r1, RU Allocation in SIG-B

## Slide 11: Straw poll - 1
Do you agree to add the following text into 11ax SFD?
  3.2.5 The following indices shall be included in RU allocation subfield table in HE-SIG-B
    242 Null
    484 Null
    996 Null
  Y/N/A

## Slide 12: Straw poll - 2
Do you agree to add the following text into 11ax SFD?
  3.2.5 For DL MU PPDU of 80/160(80+80) MHz, HE-SIG-B shall be included at least in Primary 40MHz when there is a non-null RU that needs to be signaled by 2nd HE-SIG-B content channel.
  Y/N/A