## Slide 1: Spatial Re-Use Adaptive CCA Simulation Results
Date: 2016-03-15
Authors:

## Slide 2: Open Loop Methods
When packets are detected from OBSS, the carrier sense (CS) CCA level, OBSS_PD, of OBSS packets should be adjusted and suitable transmit power control (TPC) should be considered as well
Among these IEEE contributions, there are mainly three types of open loop methods
  Static OBSS_PD , No TPC
  Static Balanced OBSS_PD + TPC
  RSSI-Based Balanced OBSS_PD + TPC

## Slide 3
BSS 1
BSS 2
Legacy PD
Range
OBSS PD
Range
Static Balanced OBSS_PD + TPC
- considerate
Method Summary
Static OBSS_PD , No TPC - not considerate at all
RSSI-Based Balanced OBSS_PD + TPC - very considerate
Increase CCA = Reduction PWR = fixed
Increase CCA = Reduction PWR = min(DynamicValue, RaiesdCCAmax)
Increase CCA = fixed
RaiesdCCAmax
DynamicValue

## Slide 4: Simulation Parameters
Use simplified 11ax simulation Scenario 1
  2 x 5 x 10 = 100 apt. in a building
  One pair of AP/STA in each apt.
Random factor
  Location of AP/STA in each apartment
  Use one channel out of three (0, 1, 2)
  Shadowing effect
Power setting
  TX Power: AP: 20dBm, STA: 15dBm
  Standard CCA in 20MHz: -82dBm
  BW 20 MHz
Other simplification
  Link adaptation: assign best MCS that can sustain 10% PER by looking up SINR-PER table
  No MAC overhead
  No collision
* Follow 11ax-evaluation-methodology in Box2TestCase3

## Slide 5: Scenario
Initially:
  Whole building is empty.
Procedure:
  try to deploy 11ax and legacy devices one by one with specified selection probability p and 1-p at apartments using ch0
  Successfully deployed if interference from all other deployed BSS is less than OBSS_PD
  In the end there are 33 AP/STA pairs in ch0
Evaluation Metrics:
  Total system throughput
  System gain
Legacy or 11ax
1st TX
Ch0
Ch0
Ch0
Ch0
Ch2
Ch2
Ch1
Ch1
Ch2
Ch2
TX
RX
1st RX
1st TX
1st TX
Legacy or 11ax
Legacy or 11ax
Follow procedure

## Slide 6: Total System Throughput (mcs0: 1, mcs1: 2, … mcs9: 13.3, PHY rate relative ratio to MCS0)
Chart: 
| 0 | 2.5 | 5 | 7.5 | 10 | 12.5 | 15 | 17.5 | 20 | 22.5 | 25 | 27.5 | 30
CCA: nAx 100% | 145.8 | 157.4 | 169.6 | 181.8 | 190.7 | 200.5 | 207 | 211.3 | 214 | 215.3 | 214.3 | 208.4 | 208.1
CCA: nAx 75% | 147.3 | 155.5 | 163.9 | 173 | 180 | 187.5 | 192.3 | 194 | 195.3 | 195.5 | 194 | 190.4 | 187.4
CCA: nAx 50% | 145.3 | 151.6 | 158.2 | 164.4 | 170.5 | 172 | 175.8 | 177.6 | 177.7 | 175.9 | 175.5 | 172.7 | 169.5
CCA: nAx 25% | 146.2 | 147.8 | 152.3 | 154.5 | 156.5 | 161.1 | 160.7 | 159.1 | 160.3 | 158.2 | 157.7 | 156.7 | 154.3
CCA+TPC: nAx 100% | 145.2 | 169.7 | 192.5 | 205.7 | 214.3 | 213.2 | 206.3 | 201.3 | 199.8 | 198.7 | 199 | 199 | 199
CCA+TPC: nAx 75% | 145.4 | 163.5 | 179.2 | 190.2 | 195.7 | 192.6 | 187.3 | 180.5 | 172.3 | 163.6 | 154.5 | 144.1 | 135.1
CCA+TPC: nAx 50% | 144.3 | 157.9 | 168.3 | 174.2 | 178 | 176.7 | 171.2 | 166.4 | 159.5 | 150.9 | 144.3 | 138.9 | 132.7
CCA+TPC: nAx 25% | 145.6 | 151.4 | 157.4 | 160.3 | 161.3 | 160 | 158.1 | 154.5 | 149.7 | 148.3 | 143.8 | 141.1 | 138.6
RSSI Based CCA+TPC: nAx 100% | 146 | 169.3 | 192 | 206.9 | 214 | 215.1 | 206.2 | 200.8 | 199.3 | 198.1 | 197.8 | 197 | 195.1
RSSI Based CCA+TPC: nAx 75% | 145.9 | 164.1 | 180.2 | 190.9 | 195.2 | 194.6 | 187.5 | 178.1 | 172.6 | 164.5 | 153.9 | 144.1 | 134.9
RSSI Based CCA+TPC: nAx 50% | 145.7 | 157.1 | 168.5 | 175.2 | 177.7 | 177.7 | 171.3 | 166.5 | 158.2 | 151.2 | 144 | 137.7 | 132.8
RSSI Based CCA+TPC: nAx 25% | 145.7 | 151.3 | 157.1 | 160.1 | 160.2 | 160.5 | 157.8 | 154.4 | 150.2 | 146.6 | 143.1 | 142.1 | 139.3
CCA: Raisd CCA
CCA+TPC: Raised CCA = Reduced TPC RSSI Based CCA+TPC: RaisedCCAmax
Relative PHY rate

## Slide 7: System Gain
“CCA”, “CCA+TPC”, “RSSI-based”:
  The higher chance you deploy 11ax devices instead of legacy ones, the higher system throughput you can get  incentives to use 11ax
  Each method can achieve same optimal (peak) system throughput (like system capacity) at different raised CCA level  does it mean simple “CCA” with suitable raised level is good enough?
“CCA+TPC” behaves like “RSSI-based”
  At most of the time, the raised CCA (or reduced TX power) of RSSI-based method is capped at its RaisedCCAmax instead of the true dynamically determined value
CCA+TPC
RSSI-based
11ax dev. deploy prob. | 25% | 50% | 75% | 100%
Maximum System Gain | 10% | 22% | 33% | 48%
RaiesdCCAmax

## Slide 8: Conclusion
We have summarized several open loop SR methods/algorithms from IEEE contributions and done a high level system simulation to understand the limitation and potential gain, and also summarized some potential HW related parameters
Simulation results
  Using more 11ax devices can provide some significant system gain
11ax dev. deploy prob. | 25% | 50% | 75% | 100%
Maximum System Gain | 10% | 22% | 33% | 48%