## Slide 1: BF Training for SU MIMO
Date: 2016-03-14
Authors:

## Slide 2: Background
Many BF features were agreed in 11ay SFD:
  The 11ay BF protocol shall provide means to enable TX sector down selection as part of BF training.
  The 11ay BF protocol shall support RX sector down selection as part of BF training.
  The 11ay SLS BF protocol shall enable feedback of one or more sectors per TX and RX antenna.
  etc.
  This contribution intends to address the flow of BF for SU MIMO.

## Slide 3: BF Flow for SU-MIMO
  Assumption: Control PHY connection established between Initiator and Responder.
  BF for SU MIMO can mainly be performed in the following phases:
  SLS: Coarse BF training to allow TX sector down selection for Initiator and Responder
    Can be skipped if the previous I-TXSS and R-TXSS are still valid.
  Setup (TBD): Message exchange between Initiator and Responder for specifying how the TX-RX pairing phase is performed.
    Our preference is to eliminate or reduce the amount of negotiation between Initiator and Responder per BF Training to simplify the BF training flow
    For example, to have capability exchange during association. If a Device’s capability supports a certain feature, no negotiation is needed.
  TX-RX sector/antenna mapping (name: TBD): BF training of RX sectors/antennas/RF chains for each of the candidate TX sectors to determine best TX-RX configuration for SU MIMO.

## Slide 4: SLS
I-TXSS to allow TX sector down selection for Initiator by collecting feedback of multiple TX sectors from Responder.
    Each TX antenna should have the same number of selected sectors. The intention is to avoid the case that the selected sectors bias a TX antenna.
R-TXSS to allow TX sector down selection for Responder by collecting multiple TX sector feedback from Initiator.
  If Responder has antenna pattern reciprocity, RX sector down selection for Initiator can be performed in the same manner as TX sector down selection for Responder.
  Should be used only when the number of TX sector/RX sector pairing is large.
Feedback selected sectors per TX antenna for Responder,
Setup for TX-RX pairing
Allow TX sector sweep using a single BRP frame;
Feedback selected sectors per TX antenna for initiator
Allow TX sector sweep using a single BRP frame

## Slide 5: Setup
  What can be done during Setup:
  Perform TX sector down selection based on the previous I-TXSS and R-TXSS if necessary. For example,
    SLS phase is skipped and the previous I-TXSS and R-TXSS do not include feedback of multiple sectors.
    may be included into the TX-RX pairing phase
  Determine whether TX-RX pairing is performed for Responder link besides for Initiator link.
    may be unnecessary if it is done during SLS phase
  Determine whether TX or RX makes TX/RX sector/antenna pairing decision based on the TX/RX capability
    may be unnecessary if it is done via capability exchange during association
  etc.
Our preference is to eliminate or reduce the amount of negotiation between Initiator and Responder per BF Training to simplify the BF training flow.

## Slide 6: TX-RX Sector/Antenna Pairing (MID)
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Selected TX sectors/antennas for Initiator

## Slide 7: TX-RX Sector/Antenna Pairing (MID)
CSI Feedback for Initiator link
Selected RX sectors/antennas for Initiator
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms

## Slide 8: TX-RX Sector/Antenna Pairing (MID)
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Selected TX sectors/antennas for Initiator
Selected TX sectors/antennas for Responder
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms

## Slide 9: TX-RX Sector/Antenna Pairing (MID)
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
CSI feedback for Initiator link
Selected RX sectors/antennas for Responder
CSI feedback for Responder link
Selected RX sectors/antennas for Initiator
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms

## Slide 10: TX-RX Sector/Antenna Pairing (MID)
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Selected TX sectors/antennas for Initiator
Selected RX sectors/antennas for Initiator
CSI feedback for Responder link
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms

## Slide 11: TX-RX Sector/Antenna Pairing (MID)
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
CSI feedback for Initiator link
Selected RX sectors/antennas for Responder
Selected TX sectors/antennas for Responder

## Slide 12
Straw Poll
Do you agree to insert the following text into 11ay SFD?
  BF for SU MIMO comprises the following phases:
    SLS: Coarse BF training to allow TX sector down selection for Initiator and Responder including feedback with candidate sectors.
    TX-RX Sector/Antenna Mapping (name: TBD): BF training of RX sectors/antennas/RF chains for each of the candidate TX sectors to determine best TX-RX configuration for SU MIMO.
    others: TBD
  Yes:
  No:
  Abstain: