## Slide 1: Functional requirements for scalability operation
Date: 2016-03-14
Authors:
Name | Affiliation | Address | Phone | Email
Chao-Chun Wang | MediaTek Inc |  |  | Chao-chun.wang@mediatek.com
James Yee | MediaTek Inc |  |  | James.yee@mediatek.com
Thomas Handte | SONY Corp. |  |  | thomas.handte@ eu.sony.com
Kåre Agardh | SONY mobile |  |  | kare.agardh@ sonymobile.com
Chao-Chun Wang (MediaTek Inc)

## Slide 2: Background
This document proposes a set of functional requirements for a scalable .11az protocol to support a large number of STAs (> 200) in performing locationing operation concurrently.

## Slide 3: Definition of Scalability
11-16-0134-03-00az-accuracy-and-coverage-functional-requirements details the functional requirement for accuracy and coverage
The objectives of the accuracy and coverage are also applicable to scalability, except the consideration of the performance threshold needs to be updated for > 200 STAs rather than for a single STA

## Slide 4: Objectives
Optimize the time it takes to get a first location fix with the required accuracy
Determine the Refresh rate of the location information vs. accuracy
Minimize Power (i.e., minimize Idle Rx, Active Rx and Active Tx)
Minimize Medium Usage
Optimize the duration a device has to operate off-channel

## Slide 5: Functional Requirements - 1(Scalability)
The scalable mode of the 802.11az range measurement protocol shall:
Support at least one mode which allows for scalable positioning, meeting the following scalability mode requirements
  Support at least 200 unassociated and associated STAs, per AP performing locationing operation concurrently
  Achieve improved accuracy of 1st fixed time of a STA with greater number of APs involved
  Utilize less than 10% of the channel capacity of an AP
  Operate with a maximum refresh rate of .5Hz
  Maintain stability with up to 5% STAs joining and leaving the coverage of the AP
March 2016

## Slide 6: Motion
Move to adopt the set of functional requirements listed in slide #5 and include them in the TGaz Functional Requirements Document under the sub-section focused on Scalability for the .11az protocol
Moved:
Seconded:
Result:

## Slide 7: Back UP

## Slide 8: Functional Requirements for scalable positioning protocol
Parameter | Value | Assumptions | comments
Number of locating STAs | STAs | STA may be unassociated STA. Number is per AP. | 
Number of APs used to accomplish the task dependent? | Yes. |  | e.g. If to support the technique more than 1 AP is required multiply the number of loc. STAs by number of APs required to accomplish the task.
Medium usage | 10% |  | Dedicated to location determination purposes for the scalable operational mode.
Refresh rate | 0.5Hz | Rate of location fixes required by the Application layer. | e.g. might be that multiple measurements are required for a single fix to be generated.
Mobility factor? | 5% | Percentage of STAs joining the service and leaving the service out of the STAs under coverage of 1 AP. Out of refresh rate. STA stays for 20 cycles @ 0.5Hz giving 5% of total locating STAs. | e.g. ability to account for variability in STA’s mobility
Support for unassociated STAs required. | Yes. |  |