## Slide 1: 802.11ak/802.1AC/STAs/APs/DSes and Convergence Functions
Date: 2016-03-15
Authors:

## Slide 2: Abstract
Building upon a model being proposed for the IEEE 802.11 Portal Convergence Function, this presentation carries that concept into the 802.11ak concepts, and 802.1AC considerations for these extended concepts.

## Slide 3
Following are several slides from the 802.11 portal presentation (being considered in ARC, and 802.1AC) – 11-14/497 …

## Slide 4: This is an example of a physical network
802.3
Two physical boxes, commonly (but inaccurately) called “APs,” connected by an IEEE 802.3 link.
Two clients of “AP 1” shown, two wireless and one wired clients of “AP 2” not shown.
No VLANs.
“AP” 1
“AP” 2
802.3

## Slide 5: Layering
In the ISO layering model, a DATA.request is presented by a higher layer to a lower layer, and a DATA.indication is presented by a lower layer to a higher layer.
In all further diagrams in this deck, the “higher” layer is closer to the top of the slide, and the “lower” layer closer to the bottom.

## Slide 6: A standard view of that same network in 802.11 today
Distribution System (DS)
MAC
PHY
MAC
PHY
MAC
PHY
AP STA 1
Non-AP STAs
MAC
PHY
AP STA 2
unspecified
portal
AP
AP
MAC
PHY
802.3
This is similar to IEEE 802.11-2012, Figure R-1, but drawn with “request down indication up” rigorously applied.
The DS has three users, two APs and a portal, so is shown passing behind a MAC.

## Slide 7: One possible 802.1AC-to-portal architecture
A connecting link is required, because the portal uses a SAP; it does not provide one.
Therefore an 802.1AC convergence layer specific to 802.11 is not necessary.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
portal
AP
MAC
PHY
MAC
PHY
anything, e.g. 802.3
802.3
MAC
PHY
802.1Q bridge relay
MAC
PHY
MAC
PHY
Non-AP station
end station

## Slide 8: But, there is an alternate approach.
This interface is defined.
It is the DS_SAP, illustrated in IEEE Std 802.11-2011 Figure R-1.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
portal
AP
MAC
PHY
MAC
PHY
anything, e.g. 802.3
802.3
MAC
PHY
802.1Q bridge relay
MAC
PHY
MAC
PHY
Non-AP station
end station

## Slide 9: So, another representation could be …
That is, the 802.1AC Clause 12.2.1 “portal convergence function” is not an interface to a portal; .1AC 12.2.1, plus a bridge relay function, is an example of a portal.
.1AC 12.2.1 connects the ISS to the DS_SAP.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
AP
802.1Q bridge relay
MAC
PHY
Non-AP station
MAC
MAC
802.3
PHY
PHY
end station
.1AC
One example (of many) of a portal

## Slide 10
New for 802.11ak consideration…

## Slide 11
MAC
PHY
MAC
PHY
PHY
MAC
AP STA 2
PHY
MAC
AP STA 1
Non-AP STAs
802.3
Extending this to P802.11ak + P802.1Qbz
MAC
PHY
802.1Q bridge relay
AP
AP
Conv.
Funct
.1AC CF
SAP[ ]
SAP
SAP
.1AC CF
SAP[ ]
SAP
SAP
That is, 802.1AC/802.11ak are defining a SAP and a convergence function that supports multiple, logical links as seen by the Bridge, to each of the 11ak-aware non-AP endpoints.
CHANGED

## Slide 12: P802.11ak and non-11ak STNs on one AP.
DS
AP w/Bridge and
non-11ak (legacy) access
11ak STAs
MAC
PHY
MAC
PHY
Non-11ak STAs
MAC
PHY
MAC
PHY
AP
Bridge
.1AC
MAC
PHY
.1AC
CHANGED

## Slide 13: P802.11ak and non-11ak STNs on two APs.
Non-
11ak
STA(s)
11ak
STA(s)
Non-
11ak
STA(s)
11ak
STA(s)
11ak AP w/Bridge and
non-11ak (legacy) access
11ak AP w/Bridge,
uses DS
for non-11ak access
.1AC
.1AC
DS
MAC
PHY
MAC
PHY
MAC
PHY
MAC
PHY
AP
Bridge
.1AC
MAC
PHY
MAC
PHY
AP
Bridge
Note that connectivity between this 11ak STN and the other stations depends on some connection between the Bridges not shown.
isolated
CHANGED

## Slide 14: P802.11ak and non-11ak STNs on two APs.
Non-
11ak
STA(s)
11ak
STA(s)
Non-
11ak
STA(s)
11ak
STA(s)
AP w/Bridge and
non-11ak (legacy) access
AP w/Bridge,
uses DS
for non-11ak access
.1AC
DS
.1AC
DS
MAC
PHY
MAC
PHY
MAC
PHY
MAC
PHY
AP
Bridge
.1AC
MAC
PHY
MAC
PHY
AP
Bridge
Now, all stations are fully connected, but the DS appears to be split.
.1AC
CHANGED

## Slide 15: P802.11ak and non-11ak STNs on two APs.
Non-
11ak
STA(s)
11ak
STA(s)
Non-
11ak
STA(s)
11ak
STA(s)
AP w/Bridge and
non-11ak (legacy) access
AP w/Bridge,
uses DS
for non-11ak access
.1AC
DS
.1AC
DS
MAC
PHY
MAC
PHY
MAC
PHY
MAC
PHY
AP
Bridge
.1AC
MAC
PHY
MAC
PHY
AP
Bridge
In fact, the DS is not split; it is perfectly free to use the link provided by the bridges in order to accomplish its purposes. PROVIDED …
.1AC
CHANGED

## Slide 16: P802.11ak and non-11ak STNs on two APs.
Non-
11ak
STA(s)
11ak
STA(s)
Non-
11ak
STA(s)
11ak
STA(s)
AP w/Bridge and
non-11ak (legacy) access
AP w/Bridge,
uses DS
for non-11ak access
.1AC
DS
.1AC
DS
MAC
PHY
MAC
PHY
MAC
PHY
MAC
PHY
AP
Bridge
.1AC
MAC
PHY
MAC
PHY
AP
Bridge
The DS must not pass user data in parallel to the bridges’ data. (DS “control” data is fine. This is nothing new: hence the “one portal” rule, which we are purposely violating, here for optimal connectivity.
.1AC
CHANGED

## Slide 17: Tasks for 802.1AC
Rewrite 802.1AC Draft 0.2 Clause 12.2.1 to provide a convergence function that maps multiple, logical ports visible to the bridge, to the vector-of-endpoints SAP provided by an 11ak AP.

## Slide 18: Tasks for 802.11ak
Define the SAP presented by an 11ak AP to include the vector-of-endpoints parameter, which identifies links to each of the 11ak-aware non-AP STAs.

## Slide 19: P802.11ak and non-11ak STNs on one AP.
DS
AP w/Bridge and
non-11ak (legacy) access
11ak Non-AP STAs
MAC
PHY
MAC
PHY
Non-11ak Non-AP STAs
MAC
PHY
MAC
PHY
Bridge
.1AC
MAC
PHY
SAP[ ]
SAP
SAP
Bridge
SAP
11ak DSAF
Portal
.1AC
One-to-one
mapping, 11ak
non-AP STA
to SAP
SAP
SAP

## Slide 20: P802.11ak and non-11ak STNs on one AP.
DS
AP w/Bridge and
non-11ak (legacy) access
11ak Non-AP STAs
MAC
PHY
MAC
PHY
Non-11ak Non-AP STAs
MAC
PHY
MAC
PHY
Bridge
MAC
PHY
SAP[ ]
SAP
SAP
Portal
SAP
11ak DSAF
Portal
.1AC
One-to-one
mapping, 11ak
non-AP STA
to SAP
SAP
Bridge
Bridge
With Portal still generic (not necessarily a bridge)
And, MACs, Portal, Bridges height aligned to LLC layer
SAP

## Slide 21: P802.11ak and non-11ak STNs on one AP.
DS
AP w/Bridge and
non-11ak (legacy) access
11ak Non-AP STAs
MAC
PHY
MAC
PHY
Non-11ak Non-AP STAs
MAC
PHY
MAC
PHY
Bridge
MAC
PHY
SAP[ ]
SAP
SAP
Portal
SAP
11ak DSAF
Portal
.1AC
One-to-one
mapping, 11ak
non-AP STA
to SAP
SAP
Bridge
Bridge
SAP
SAP
TBC: add a SAP to the AP bridge that allows MSDUs to get from the Bridge to the DS via the 11ak switching function.

## Slide 22: There is an obvious problem!
Q: How can such a simple idea (a layer 2 distribution service) require such complicated architectural diagrams, especially when the implementations are simple?
A: It could be that the thinking about the architecture behind what constitutes an AP, a portal, and a DS is not correct!

## Slide 23: Some Fundamentals
A STA is an IEEE 802.11 two-layer (one and a sublayer) entity that (to date) has a single wireless interface “on the bottom” and a single MAC-SAP “on the top” (a MAC-to-LLC-sublayer-SAP, or ML-SAP for short). (.11ak is changing this!)
Currently, from the IEEE 802 (and 802.11) perspective, the LLC sublayer (“above” the MAC sublayer) consists of either:
  legacy (and disappearing) IEEE 802.2 LLC sublayer services (LPD) in a sublayer with NO addressing, or
  no addressing AND no services (EPD – the ONLY content of the LPDU header is the two-octet ethertype (aka network layer address)).

## Slide 24: Some More Fundamentals
An AP is (currently) a STA with:
  NO ML-SAP (why not???)
  OPTIONAL access to a layer 2 (MAC sublayer) distribution service (DS) which implies a second egress interface!
  additional functionality (beacons, point-coordination, authentication/association, etc.), and it is (or soon will be) this functionality that ultimately distinguishes an AP from a STA!

## Slide 25: Some More Fundamentals
An IEEE 802.11 DS is a layer 2 service that uses layer 2 (MAC) addresses to exchange MPDUs between peer layer 2 entities in STAs as well as other nodes in the local area network (LAN)
  The service offered by an IEEE 802.1Q bridged LAN is an example of such a service (NF)!
A DS is analogous to (BUT NOT THE SAME AS) a layer 3 IPv6 forwarding service, where NPDUs not addressed to the receiving entity are forwarded (if possible).

## Slide 26: Some More Fundamentals
Nodes connected at layer 2 use layer 2 addressing and services to form Local Area Networks (LANs) which are in turn connected at layer 2 using switches in special layer 2 nodes called bridges.
Nodes connected at layer 3 use layer 3 addressing and services to form (inter-)networks which use special layer 3 functionality in routers to create and maintain connectivity between peer layer 3 entities.
All layer 3 functionality is unobservable to and unreachable by any layer 2 entity. Thus, layer 3 functionality is invisible to IEEE 802.11 STAs/APs.

## Slide 27: Some More Fundamentals
The IEEE 802.11 DS was purposefully left “unspecified” so vendors could implement AP connectivity however they chose.
This does NOT imply that ANY means for connecting APs qualifies as an IEEE 802.11 DS.
It would be, and still is, out-of-scope for IEEE 802.11 to specify ANYTHING above the MAC sublayer, so to state that a DS could include functionality above the MAC sublayer is out-of-scope.
Can devices that have layer 2 APs communicate above the MAC sublayer to form ESSes? … YES! Is that communication “through an IEEE 802.11 DS”? … NO!

## Slide 28: Some More Fundamentals
To form ESSes, devices that have IEEE 802.11 APs can be connected (and communicate) using:
  IEEE 802.11 DS services (layer 2 (MAC sublayer)),
  network layer services (layer 3),
  “gateway” services (above layer 4), and
  any combination of the above.
How devices with APs communicate to form ESSes is outside the scope of IEEE 802.11, UNLESS the “first-hop” of such communication involves only MAC sublayer services, access to which through the MD-SAP is “in scope”.

## Slide 29: The Impact
The “AP box” in all these .11ak/.1AC diagrams disappears.
It is “replaced” by:
  the “normal” functionality in any layered communication architecture which at each layer inspects addresses in received PDUs to ascertain what to do with those PDUs, and
  a label put on a STA with the added “AP functionality”.

## Slide 30: The Impact
A DS and a STA’s MAC sublayer entity are connected using a “DS convergence function”, the details of which depend on the DS.
A DS implemented using .1Q bridging is connected to STAs using the “.1AC convergence function”.
A DS convergence function communicates with the DS using a SAP between the DS convergence function in the MAC sublayer and the DS (the “MD-SAP”) and it’s “sideways”!

## Slide 31: Legend
MAC
PHY
STA with no AP functionality and no access to a DS
MAC
PHY
MAC
PHY
STA with no AP functionality and access to one or more DSes
STA with AP functionality and access to one or more DSes
DSCF

## Slide 32: APs STAs and a DS
Distribution System (DS)
Non-AP STAs
unspecified
MAC
PHY
802.3
MAC
PHY
MAC
PHY
MAC
PHY
DSCF
DSCF