## Slide 1: QoS Handling of Trigger Frame
Date: 2016-05-04
Authors:

## Slide 2: Abstract
The submission discusses the TF (Trigger Frame) transmission handling in a QoS STA
We identify two options to configure EDCA (Enhanced Distributed Channel Access) parameters for the TF
We identify two options to handle backoff for TF transmission respect to the 802.11e framework

## Slide 3: Transmission Priority of TF
When an AP transmit a TF that elicits an HE trigger-based PPDU, the TF competes for channel access with other STAs
If the TF is mapped to an AC in a QoS STA, it competes for channel access with the traffic of other ACs in the same STA
The transmission priority of the TF is decided by the EDCA parameters, e.g. IFS (Inter-Frame Spacing) and CW (Contention Window) size

## Slide 4: EDCA Transmission Prioritization
With EDCA, ACs have been specified in IEEE 802.11e with four priorities realized by different sensing duration before transmission
QoS STAs certified with Wi-Fi Multimedia (WMM) support EDCA
AC | CWmin | CWmax | AIFSN
AC_BK | aCWmin | aCWmax | 7
AC_BE | aCWmin | aCWmax | 3
AC_VI | (aCWmin+1)/2-1 | aCWmin | 2
AC_VO | (aCWmin+1)/4-1 | (aCWmin+1)/2-1 | 2

## Slide 5: EDCA Parameters for TF
Two options to configure EDCA parameters for the TF
Option 1: fixed EDCA parameters
  It’s suggested to apply AC_VI parameters to prioritize TF for scheduled transmissions
Option 2: variable EDCA parameters
  TF may have the same priority as the traffic it solicits from one or multiple STAs
  When the multiple STAs have different priorities, the TF should apply the parameters of the highest one
  It’s TBD how an AP obtain the traffic priority knowledge from the STAs, e.g. by including such info in BSR (Buffer Status Report)

## Slide 6: 802.11e Framework of Backoff Processes in One QoS STA
In a QoS STA, each AC maintains an independent backoff process
Different ACs compete for channel access with the independent processes
Figure source: [1]

## Slide 7: TF and AC Backoff Processes in a STA
Two options to handle backoff for TF transmission
Option 1: TF backoff in the 802.11e framework
  By placing TF in one of the AC queues and follow the backoff procedures specified in 802.11e
Option 2: TF backoff out of the 802.11e framework
  Once a STA decides to transmit a TF, it starts a dedicated backoff process with certain EDCA parameters
  The backoff processes specified in 802.11e halt until the TF is sent

## Slide 8: Conclusion
Two options are identified to configure EDCA parameters for TF
  Fixed or variable EDCA parameters
Two options are identified to handle backoff for TF transmission
  In or out of the 802.11e framework

## Slide 9: Straw Poll
TGax should decide whether fixed or variable EDCA parameters are applied to the TF
TGax should decide whether TF backoff process in a QoS STA is in or out of the 802.11e framework

## Slide 10: References
[1] S. Mangold et al., “Analysis of IEEE 802.11 for QoS Support in Wireless LANs,” Dec. 2003. IEEE Wireless Communications