## Slide 1: Impact of transmission power control on Clear Channel Assessment Threshold adjustment
Date: 2016-05-11
Authors:

## Slide 2: Abstract
The document presents results on the impact of transmission power control (TPC) together with dynamic sensitivity control (DSC).
Recommendations for the usage of TPC are also presented.

## Slide 3: Background and objectives
Gain using dynamic sensitivity control (DSC) has been observed in previous work [1].
Evaluate the impact of two TPC algorithms used together with DSC.
  TPC is supposed to reduce the power of the transmitting node in order to reduce its interference on neighbouring nodes.

## Slide 4: The algorithm structure
The following flow chart is used for the power control algorithm:
The power control algorithm: powerControl(CCAT_DSC,max(interference)) is varied as described in the following page.
No
powerControl(CCAT_DSC,max(interference))
OBSS transmission?
Any
Interference > -82dBm
Yes
Yes
No
No power change
No power change

## Slide 5: TPC algorithm
Two different TPC algorithms are evaluated:
Algorithm a:
A path loss compensating algorithm where the transmission power is adjusted based on the difference of the default CCAT value and the CCAT set by DSC.
Tx_power = power-(DSC_CCAT-CCAT_default)×controlValue
The controlValue is a value between [0-1] to dimension the reduction.
Algorithm b:
An algorithm were the transmission power is based on the percentage of the increased CCAT value based on the DSC CCAT and the default CCAT value:
Tx_power = (1-(DSC_CCAT/CCAT_default))×power.

## Slide 6: TPC algorithms (cont.)
Algorithm a:
  Linear power reduction.
  The controlValue defines the aggressiveness of the algorithm.
Algorithm b:
  Non-linear power reduction.
  Low power change for lower CCAT and more aggressive for high CCAT value.
The goal is to see how these two algorithms affect the results of the TPC.

## Slide 7: Simulations
Simulations are performed with the following simulation assumptions:
  80 MHz in 5 GHz band.
  2×2 MIMO.
  Equal DL and UL traffic.
  Equal buffer with Poisson arrival, 1 MB file download.
  Minstrel Link Adaptation.
  Max AMPDU size 64 kB.
The simulations are done for the enterprise scenario in the IEEE scenario document [2].

## Slide 8: Results – algorithm a
Sweep of the controlValue show that an increased controlValue decreases the SINR and user performance. None of the controlValues improve the results of DSC.
SINR is reduced for TPC, even though interference (I) might be reduced due to PC, the lower signal power (S), reduces the SINR.

## Slide 9: Results - algorithm comparison
The two above algorithms are compared to each other.
None of the algorithms provide significant improvements for scenario 2. The DSC algorithm outperform the DSC +TPC algorithms.
The chosen controlValue for algorithm a is 0.125 which provides the best performance.

## Slide 10: Interference reduction
For the TPC algorithm to trigger, the nearby nodes are within a certain interference threshold (-82 dBm), i.e. transmitting with a certain power causing interference for the other nodes.
The CDF of the interference, at 150 Mbps traffic load, heard by the nodes ranges between -150 dBm and -50 dBm.
The interference level is not significantly reduced using TPC, explaining the lack of observed gain.
Interference [dBm]

## Slide 11: Conclusions
Simulation results
    No gain is observed using TPC together with any of the DSC algorithms for the enterprise scenario.
    A linear and non-linear TPC algorithm were compared with each other to analyse the impact of DSC + TPC.
    The results indicate that TPC might degrade user throughput in the studied scenario. The algorithm can be too aggressive and decrease user throughput.
Recommendations
  Based on the results, TPC is not recommended and should not be mandated.

## Slide 12: References
[1] - IEEE 802.11-14/1427r1 DSC performance.
[2] - IEEE 802.11-14/0980r7 TGax Simulation scenarios.