## Slide 1: Random Access RU Allocation in the Trigger Frame
Date: 2016-05-16
Authors:
Name | Affiliation | Address | Phone | Email
Evgeny Khorov | IITP |  |  | khorov@frtk.ru
Anton Kiryanov | IITP |  |  | ant456@ya.ru
Sigurd Schelstraete | Quantenna |  |  | sigurd@quantenna.com
Huizhao Wang | Quantenna |  |  | hwang@quantenna.com

## Slide 2: Background
The Trigger frame is used to allocate resource for UL MU transmission and to solicit an UL MU transmission. The Trigger frame also carries other information required by the responding STA to send UL MU.
The spec shall define a Trigger frame that allocates resources for random access. [MU Motion 8, July 16, 2015]
In [1] the RU allocation signaling for each STA carried in per user info field of the Trigger frame was proposed.
However, current SFD and Draft revisions do not describe how RUs for UL MU random access are signaled.

## Slide 3: Trigger Frame for Random Access or Random Access RUs
The Draft describes the following Trigger types
One way is to have an additional Trigger type, i.e. Trigger Frame Random (TF-R), which allocates resource in UL for random access only.
Another way is to allow Basic Trigger allocating RUs for random access also.
Trigger Type value | Trigger Type description
0 | Basic Trigger
1 | Beamforming Report Poll Trigger
2 | MU-BAR
3 | MU-RTS
4-TBD | Reserved

## Slide 4: Random Access RUs
Currently the User Identifier subfield of the Per User Info field of Trigger Frame indicates the AID of the STA to which an RU described in RU Allocation subfield is allocated.
Following the allocation signaling adopted from [1], it is possible
to introduce Random Access User ID (the exact value is TBD) which is placed to User Identifier subfield of the Per User Info field to let an RU be the Random Access RU.
 | User Identifier | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
Figure 9‑1 - Per User Info field

## Slide 5: Multiple Random Access RUs Allocation
Redundant information
  To allocate several RUs with the same transmission parameters, we need to repeat Per User Info field many times explicitly.
 | User ID STA1 | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
RU for STA1
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for STA2
RU for RA
(26-tome)
…
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID STA2 | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
Huge overhead!
Overhead can be reduced in several ways with no changes or very small changes to current signaling

## Slide 6: Multiple Random Access RUs
If an HE AP wants to allocate multiple RUs for random access with the same parameters (Coding Type, MCS, DCM, SS Allocation), it is better to describe all of them once instead of creating individual entry for each RU. In such a way signaling overhead is reduced.
We propose several ways how to signal multiple random access RUs and reduce overhead.
For that case, we extend signaling adopted from [1].

## Slide 7: Recall: RU Allocation info for each STA [1]
  Proposed to use 8 bits RU allocation signalling to cover all the different BW cases (e.g. 20/40/80/160MHz).
    The 8 bits RU allocation signalling consists of 1 bit for RU location and 7 bits RU indices.
    The first bit for RU location indicates the allocated RU is located at the primary or non-primary 80MHz.
    The subsequent 7 bits indices indicate 69 possible RU allocation cases based on 80MHz tone plan. The mapping of the 7 bits to the RU allocation is defined in the table below. The last entry means RU allocation with the whole 160/80+80MHz.
primary 80MHz
non-primary 80MHz
“0 xxxxxxx”
“1 xxxxxxx”
160MHz/80+80MHz -> “x 1000100”
1 bit for RU location
20MHz
26
52
106
242
484
996
7 bits indices | Message | Number of entries
0000000 ~ 0100100 | Possible 26 RU cases in 80MHz | 37*
0100101 ~ 0110100 | Possible 52 RU cases in 80MHz | 16
0110101 ~ 0111100 | Possible 106 RU cases in 80MHz | 8
0111101 ~ 1000000 | Possible 242 RU cases in 80MHz | 4
1000001 ~ 1000010 | Possible 484 RU cases in 80MHz | 2
1000011 | Possible 996 RU cases in 80MHz | 1
1000100 | 160MHz/80+80MHz case | 1
Total |  | 69
  * Note: Signaling for the center 26 unit in 80 MHz is also included.

## Slide 8: 1. Interval RUs Allocation for RA
  To allocate an interval of RUs with the same transmission parameters, we specify only the first and the last RUs of the interval.
  In TF, the Per User Info field describing the last RU of the interval goes right after Per User Info field describing the first RU of the interval.
 | User ID STA1 | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
RU for STA1
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for STA2
RU for RA
(26-tome)
…
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID STA2 | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
Instead of N RUs for RA, advertise only 2 RUs
Implicitly defined RUs for RA
The first RU
of the interval
The last RU
of the interval
the same values

## Slide 9: 1. Example of Interval RUs Allocation for RA
  What happens if the interval of 52-tone RUs includes a 26-tone RU which is not a part of any 52-tone RUs?
  26-tone RU is excluded from the interval, but it can be explicitly allocated for deterministic or random access.
RU for RA
(52-tome)
RU for RA
(52-tome)
RU for STA1
(26-tome)
RU for RA
(52-tome)
RU for RA
(52-tome)
 | User ID STA1 | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info

## Slide 10: 2. Explicit Multiple RUs Allocation for RA
  To allocate multiple RUs with the same transmission parameters, we specify only the first RU and the number of consequent RUs (N).
  In TF for RA, the Per User Info field contains additional field (N).
 | User ID STA1 | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info (0 or no field)
RU for STA1
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for STA2
RU for RA
(26-tome)
…
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | N
 | User ID STA2 | RU Allocation | Coding Type | MCS | DCM | SS Allocation | 0 or no field
Instead of N+1 RUs for RA, advertise only 1 RU, however we extend Per User Info field for RA
N RUs for RA
The first RU
of the interval

## Slide 11: 3. Implicit Multiple RUs Allocation for RA
  To allocate multiple RUs with the same transmission parameters, we specify only the first RU. The interval ends when the RU defined in the next Per User Info field starts.
RU for STA1
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for STA2
RU for RA
(26-tome)
…
Instead of N RUs for RA, advertise only 1 RU
The first RU
of the interval
 | User ID STA1 | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID STA2 | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
Implicitly defined RUs for RA
The next
Per User Info
or the end
of TF

## Slide 12: 3. Implicit Multiple RUs Allocation for RA
  Special case: Do not use a part of bandwidth
RU for STA1
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for RA
(26-tome)
RU for RA
(26-tome)
Empty RU
RU for RA
(26-tome)
…
We need to define User ID corresponding to No STA
The first RU
of the interval
 | User ID STA1 | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | User ID RA | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
 | NONE | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Trigger dependent Per User Info
Implicitly defined RUs for RA
Ends the
interval of
RUs

## Slide 13: Per 20MHz Random Access RUs Allocation
  Another approach – signalling on per 20 MHz basis
    Bit B0 indicates whether the described RUs for random access is located at the primary or non-primary 80MHz
    Bits B1=1, B2=1, B3=1 to distinguish from signalling allocation described in [1]
    Bits B4 and B5 defines a particular 20 MHz channel within the primary or non-primary 80MHz.
    Bits B6 and B7 defines how the 20 MHz channel is split into RUs (partition pattern)
20MHz
B6 B7 | Partition pattern
00 | 9 x 26-RUs
01 | 4 x 56-RUs
10 | 2 x 106-RUs
11 | Reserved (242-RU)
B1 B2 B3
1 1 1
B4 B5 | 20 MHz channel
00 | Fist
01 | Second
10 | Third
11 | Fourth
First
Second
Third
Fourth
80 MHz
Primary 80
non-primary 80
B0=0
B0=1
Signaling on per 20 MHz basis can be useful because interference conditions within 20 MHz channel are often similar
  In addition to 69 combinations used in [1], we propose additional 12 combinations. Thus, 128-69-12=47 combinations are still available for future use.

## Slide 14: Comparison of the Proposed Methods
 | Overhead | Modification of the Frame Format | Flexibility of RU selection | Implementation
Interval (First and Last RU) | Medium | No | Good | Easy
Explicit (First RU, Number of RUs) | Small | Yes | Good | Easy
Implicit (First RU, the Last RU is defined by the next Per User Info field) | Small | No | Good | Medium
Per-20MHz | Small | No | Bad | Easy

## Slide 15: Summary
In this presentation, we propose to allocate RUs for RA in the same way as they are allocated for deterministic access
In addition, we propose several ways to allocate multiple RUs for random access with the same parameters (RU size, Coding Type, MCS, DCM, SS Allocation) without creating individual entry for each RU
  In such a way, signaling overhead is significantly reduced
The first 3 approaches slightly modify the existing signaling mechanism
  Signal the first and the last RUs for RA
  Signal the first RU for RA and the number N of RUs for RA
  Signal only the first RU for RA. The Last RU is defined by the next Per User Info field
The last approach is an extension of the existing signaling. It is designed for signaling on per 20 MHz basis because interference conditions within 20 MHz channel are often similar
  In addition to 69 combinations used in [1], we propose to use another 12 combinations. Thus, 47 combinations are still available for future use.

## Slide 16: Straw Poll #1
Do you agree to add the following text in SFD:
  x.y.z The spec shall define Random Access User ID (the value is TBD). When User Identifier subfield of the Per User Info field of the Trigger Frame equals Random Access User ID, the Per User Info field describes Random Access RU(s).
  Y
  N
  A

## Slide 17: Straw Poll #2
Do you agree to add the following text in SFD:
  x.y.z The spec shall provide a way to allocate multiple RUs for random access with the same RU size and other transmission parameters (Coding Type, MCS, DCM, SS Allocation) without creating an individual entry for each RU.
  Y
  N
  A

## Slide 18: Straw Poll #3
Do you agree to add the following text in SFD:
  x.y.z Multiple RUs for random access with the same RU size and other transmission parameters (Coding Type, MCS, DCM, SS Allocation) can be allocated as follows
    A pair of consecutive Per User Info fields with User Identifier = Random Access User ID and with the same RU size and other transmission parameters defines an interval of RUs for RA. All RUs from the interval have the same size and other transmission parameters.
  Y
  N
  A

## Slide 19: Straw Poll #4
Do you agree to add the following text in SFD:
  x.y.z Multiple RUs for random access with the same RU size and other transmission parameters (Coding Type, MCS, DCM, SS Allocation) can be allocated as follows
    If a Per User Info field has User Identifier = Random Access User ID, the Trigger Dependent Per User info contains the number of RUs (N) for random access which follow the defined RU and have the same RU size and other transmission parameters as the defined RU.
  Y
  N
  A

## Slide 20: Straw Poll #5
Do you agree to add the following text in SFD:
  x.y.z Multiple RUs for random access with the same RU size and other transmission parameters (Coding Type, MCS, DCM, SS Allocation) can be allocated as follows
    When a Per User Info field has User Identifier = Random Access User ID, the field defines a series of RUs for random access with the same RU size and other transmission parameters. The series includes all RUs up to but not including the RU, defined in the next Per User Info field, if any.
  Y
  N
  A

## Slide 21: Straw Poll #6
Do you agree to add the following to SFD:
  x.y.z Multiple RUs for random access with the same RU size and other transmission parameters (Coding Type, MCS, DCM, SS Allocation) can be allocated as follows
  When a Per User Info field has User Identifier = Random Access User ID, the RU allocation subfield content is as follows.
    Bit B0 indicates whether the described RUs for random access is located at the primary or non-primary 80MHz
    Bits B1, B2, B3 are set to 1,1,1.
    Bits B4-B7 are defined as follows
  Y
  N
  A
B6 B7 | Partition pattern
00 | 9 x 26-RUs
01 | 4 x 56-RUs
10 | 2 x 106-RUs
11 | Reserved
B4 B5 | 20 MHz channel
00 | Fist
01 | Second
10 | Third
11 | Fourth

## Slide 22: Reference
  [1] Yunbo Li (Huawei), “0386r0 RU Signaling in Trigger Frame”
  IEEE P802.11-REVmcTM/D4.3