## Slide 1: HE NDPA frame format
Date: 2016-05-13
Authors:
Name | Affiliation | Address | Phone | Email
Ross Jian Yu | Huawei | F1-17, Huawei Base, Bantian, Shenzhen | +86 18126392367 | ross.yujian@huawei.com
Jason Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com

## Slide 2
Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com
Narendar Madhavan | Toshiba |  |  | narendar.madhavan@toshiba.co.jp
Masahiro Sekiya |  |  |  | 
Toshihisa Nabetani |  |  |  | 
Tsuguhide Aoki |  |  |  | 
Tomoko Adachi |  |  |  | 
Kentaro Taniguchi |  |  |  | 
Daisuke Taki |  |  |  | 
Koji Horisaki |  |  |  | 
David Halls |  |  |  | 
Filippo Tosato |  |  |  | 
Zubeir Bocus |  |  |  | 

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Lochan Verma |  | 5775 Morehouse Dr. San Diego, CA USA |  | lverma@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 6: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Feng Jiang |  |  |  | feng1.jiang@intel.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 8: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jayh hyunhee Park |  |  |  | hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 11: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Minho Cheong | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com
Sigurd Schelstraete | Quantenna | 3450 W. Warren Ave, Fremont, CA 94538 |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quanetnna.com

## Slide 12: Background
Following has been decided in previous 11ax meetings:
  AP can request beamforming feedback over partial BW which is less than the NDP BW. The indication of the feedback BW goes in NDPA.
    [PHY Motion 148, March 2016, see 16/389]
  The granularity of channel feedback requested by the AP is a 26 tone RU. The AP signals start and end 26 tone RUs requested for feedback.
    [PHY Motion 149, March 2016, see 16/389]
  802.11ax spec shall not support Ng = 1 for sounding feedback.
    NOTE—The tone grouping factor, Ng is defined with respect to data tones of the HE PPDU.
    [PHY Motion 38, September 17, 2015, see [138]]
  802.11ax spec shall support Ng = 4 and 16 for sounding feedback with SU/MU-MIMO-OFDM(A).
    NOTE—The tone grouping factor, Ng is defined with respect to data tones of the HE PPDU.
    [PHY Motion 101, January 2016, see [139]]
  AP shall control the Ng, quantization, and Nc of the sounding FB in NDPA except in the special case of a NDPA addressed to a single STA which requests SU type feedback. In the aforementioned special case, the STA controls these quantities.
    [PHY Motion 151, March 2016, see 16/389]
  This proposal addresses the HE NDPA frame format

## Slide 13: VHT NDPA frame format Recap
VHT NDPA includes AID12, SU/MU feedback type and number of columns
Frame
Control
Duration
RA
TA
Sounding
Token
STA Info 1
STA Info 2
….
STA Info n
FCS
Bytes:
2
2
6
6
1
2
2
2
4
Reserved
Sounding
Token Number
Bits:
2
6
Bits:
Nc
Feedback
Type
12
3
1
AID12
B0
B11
B12
B13
B15
Bits:
Nc
Feedback
Type
12
3
1
AID12
B0
B11
B12
B13
B15

## Slide 14: HE NDPA frame format
In HE NDPA we need 4 Byte for per STA Info:
  AID per STA = 11bit
  Feedback type per STA: SU/MU/CQI per-STA = 2bits
  Ng per-STA = 1bit (Ng = {4,16})
  Codebook size per-STA = 1bit (quantization resolution = {(2,4),(4,6)} when feedback type = SU, quantization resolution = {(5,7),(7,9)} when feedback type = MU)
  Nc per-STA = 3bits (Nc = 1…8)
  Partial BW Info per-STA of feedback report = 14 bits
We suggest to reuse the frame type/subtype of VHT NDPA
  HE NDPA and VHT NDPA serve similar function
  Only 3 reserved subtype for control type, need to reserve subtype values for future use

## Slide 15: HE NDPA frame format
The proposed HE NDPA frame format reusing the type/subtype of VHT NDPA is shown as below:
  Only for HE NDPA aimed at more than one STAs
Frame Control | Duration | RA | TA | Sounding Dialog Token | STA Info 1 | … | STA Info n | FCS
Octets: 2 | 2 | 6 | 6 | 1 | 4 |  | 4 | 4
AID11 | Partial BW Info | Feedback type + Ng | Disambiguation bit | Codebook size | Nc
11 | 14 | 2 | 1 | 1 | 3
 | Reserved | VHT/HE | Sounding Dialog Token Number
Bits | 1 | 1 | 6
 | Start RU | End RU
Bits: | 7 | 7
B0
B10
B11
B24
B25
B26
B27
B28
B29
B0
B1
B2
B7
B31

## Slide 16: Changes Compared with VHT NDPA
VHT/HE (B1 of sounding dialog token) : to help all HE STAs to differentiate between VHT NDPA and HE NDPA.
Per STA Info extends from 2 Byte to 4 Byte to include more info:
  AID11: 11 LSB of the AID of an HE STA expected to process the following HE NDP and prepare the sounding feedback.
  Partial BW Info: signals the start index and the end index 26 tone RUs requested for feedback (7 bit is needed for maximum 74 RUs for start/end RUs).
  Disambiguation bit (B27): set to 1 to prevent VHT STA from parsing B16-B27 as his own AID
  Feedback + Ng + codebook size (2+1 bits) jointly indicate:
Feedback type + Ng + codebook size | Description
000 | SU, Ng4, quantization resolution = {2,4}
001 | SU, Ng4, quantization resolution = {4,6}
010 | SU, Ng16, quantization resolution = {2,4}
011 | SU, Ng16 quantization resolution = {4,6}
100 | MU+Ng4, quantization resolution = {5,7}
101 | MU+Ng4, quantization resolution = {7,9}
110 | CQI only feedback
111 | MU+Ng16, quantization resolution = {7,9}

## Slide 17: Further Explanation Regarding VHT STAs Behavior
Some further explanations regarding VHT STAs behavior:
  AID11 in STA info 1 of HE NDPA is the AID of an HE STA, hence VHT STA will not parse B0-B11 as its own AID.
  Disambiguation bit corresponds to the MSB of AID12 of the 2nd STA in VHT NDPA, and is set to 1, making AID12 > 2048 , never match the AID of a VHT STA.
Bits:
Nc
Feedback
Type
12
3
1
AID12
B0
B11
B12
B13
B15
Nc
Feedback
Type
12
3
1
AID12
B16
B27
B28
B29
B31
VHT NDPA: STA info 1 + STA info 2
AID11 | Partial BW Info | Feedback type + Ng | Disambiguation bit | Codebook size | Nc
11 | 14 | 2 | 1 | 1 | 3
B0
B10
B11
B24
B25
B26
B27
B28
B29
B31
Bits:
HE NDPA: STA info 1
MSB of AID 12 of VHT STA 2

## Slide 18: Summary
HE NDPA frame format reusing the type/subtype of VHT NDPA is proposed.

## Slide 19: Straw Poll
Do you agree to add to the SFD the HE NDPA frame format as shown in slide 15 and 16?
  Y
  N
  A