## Slide 1: ROM Recovery Rules
Date: 2016-05-16
Authors:
Name | Affiliation | Address | Phone | Email
Jayh hyunhee Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hyunh.park@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2
Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Thomas Derham |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 3
Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Feng Jiang |  |  |  | feng1.jiang@intel.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Jie Huang |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 5
Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Lochan Verma |  | 5775 Morehouse Dr. San Diego, CA USA |  | lverma@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 6
Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 7
Authors (continued)
Joonsuk Kim | Apple |  |  | joonuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 8
Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Yuichi Morioka | Sony Corporation | 1-7-1 Konan Minato-ku, Tokyo 108-0075, Japan |  | yuichi.Morioka@jp.sony.com
Masahito Mori |  |  |  | masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | yusukeC.Tanaka@jp.sony.com
Kazuyuki Sakoda |  |  |  | kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | william.Carney@am.sony.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com

## Slide 11
Authors (continued)
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com
Minho Cheong | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com

## Slide 12
Authors (continued)

## Slide 13: Introduction
An HE STA may request to change of its Rx Operating mode values (i.e., Rx NSS and Rx BW) by using ROMI parameters in the HT control field of the MAC Header of the MPDU
The HE STA can changes its ROM after receiving ACK/BA to frame containing new ROMI parameters
If the HE STA fails to receive the corresponding ACK/BA from the AP, it could not change its ROM even if the AP sent the ACK/BA
The Contribution addresses the failure of acknowledgement reception when new ROMI parameters are signaled

## Slide 14: Recap, Receiving Operating Mode
  In 11ax SFD [1]:
  The spec shall define a mechanism for a transmitting STA to indicate its RX operating mode, (i.e., Rx NSS, Rx channel width) in a transmitted DATA type MAC header, so that the responding STA shall not transmit a subsequent PPDU using an NSS or channel width value not indicated as supported in the RX operating mode of the transmitting STA. The responding STA shall not adopt the new NSS and BW until a time TBD.
DATA
BA
AP
STA
Outage Delay
NSS=2, BW=40MHz
DL DATA
BA
AP shall not start any PPDU transmissions to this STA
STA receives Data with Rx NSS=1, Rx BW=20MHz from AP
STA receives
Rx NSS=1, Rx BW=20MHz
STA requests new Rx NSS=2, Rx BW=40MHz
AP sends DL Data with new changed Rx values (Rx NSS=2, Rx BW=40MHz)
Accept
TX
RX
RX
RX
ROM request

## Slide 15: Problem Statement
If reception of acknowledgement from the AP is failed when the HE STA requests ROMI change:
  STA side: HE STA can not change its ROM due to not receiving an acknowledgement for ROMI
  AP side: AP will change ROM for requested STA after sending an acknowledgement for ROMI
DATA
BA
AP
STA
STA does not receive
an ACK for ROM acceptance
STA requests new Rx values
TX
RX
ROM request
x
AP: new Rx values
STA: old Rx values
“inconsistent state problem”

## Slide 16: Two cases of ROM change
Two cases to request the ROM change:
CASE 1) Requested Rx values are smaller Rx NSS and/or lower Rx Bw than currently in use
  when the HE STA changes a parameter from higher to lower, it should make the change for that parameter only after receiving the ACK for the ROMI packet
    Details in slide 17 and 18
CASE 2) Requested Rx values are larger Rx NSS and/or high Rx BW than currently in use
  when the HE STA changes a parameter from lower to higher, it should make the change for that parameter right after the ACK timeout or receiving the ACK for the ROMI packet
    Details in slide 19 and 20

## Slide 17: Problem statement for CASE 1
CASE 1) Requested Rx values are smaller Rx NSS and/or lower Rx BW than currently in use
After the reception of acknowledgement is failed from the AP:
  Even though the transmission of acknowledgement is failed, the AP will use the requested RX NSS and RX Channel width to the STA
  The STA can not change ROM because it doesn’t receive the acknowledgement and it does not know does the AP use the larger or the smaller NSS and BW for its transmission
  In this case, the STA can receive DL Data even if the AP sends DL Data with new Rx values because new Rx values of AP is lower than old Rx values of STA
DATA
BA
AP
STA
STA does not receive
an ACK for ROM acceptance
STA requests new Rx values
(2 Rx NSS, 20MHz Rx BW)
TX
RX
ROM request
x
AP: new Rx values (2 Rx NSS, 20MHz Rx BW)
STA: old Rx values (4 Rx NSS, 80MHz Rx BW)
4 Rx NSS, 80MHz Rx BW
DL DATA
AP sends DL Data with new changed Rx values (Rx NSS=2, Rx BW=20MHz)
STA can receive DL Data
due to small Rx NSS and low BW
BA

## Slide 18: Proposal for CASE 1
When the HE STA transmits a frame with ROMI field indicating smaller Rx NSS and/or lower Rx BW than currently in use
  Step 1) HE STA sends a ROM change request to the AP
  Step 2) When the AP receives the ROM request, it takes the received RX BW or RX NSS into use, if they are smaller than the current ROMI values and the AP sends an ACK to the STA
  The HE should make the change for that parameter only after receiving the ACK for the ROMI packet
Note: In this case, the operation can be followed in the Receive operating mode of 11ax Spec Draft
ROMI packet
ACK
AP
STA
Accept
Change to new ROM parameter

## Slide 19: Problem statement for CASE 2
CASE 2) Requested Rx values are larger Rx NSS and/or high Rx BW than currently in use
After the transmission of acknowledgement is failed from the AP:
  Even though the transmission of acknowledgement is failed, the AP will use the requested RX NSS and RX Channel width to the STA
  The STA can not change ROM because it doesn’t receive the acknowledgement successfully
  In this case, the STA couldn’t receive DL Data when the AP sends DL Data with new Rx values because new Rx values of AP is higher than old Rx values of STA
DATA
BA
AP
STA
STA does not receive
an ACK for ROM acceptance
STA requests new Rx values
(4 Rx NSS, 40MHz Rx BW)
TX
RX
ROM request
x
AP: new Rx values (4 Rx NSS, 40MHz Rx BW)
STA: old Rx values (2 Rx NSS, 20MHz Rx BW)
(2 Rx NSS, 20MHz Rx BW)
DL DATA
AP sends DL Data with new changed Rx values (Rx NSS=4, Rx BW=40MHz)
STA may not receive DL Data correctly
since the AP may send DL Data using larger NSS
and higher BW than STA’s Rx values

## Slide 20: Proposal for CASE 2
When the HE STA transmits a frame with ROMI field indicating larger Rx NSS and/or lower Rx BW than currently in use
  Step 1) HE STA sends a ROM change request to the AP to increase Rx values
  Step 2) When the AP receives the ROM request, , it takes the received RX BW or RX NSS into use, if they are smaller than the current ROMI values and the AP sends an ACK to the STA
  Step 3-1) If the STA doesn’t receive the ACK for the ROMI packet, it should change the ROM parameter after the ACK timeout
  Step 3-2) If the STA receives the ACK for the ROMI packet, it should change the ROM parameter immediately
ROMI packet
ACK
AP
STA
x
ACK timeout
Change to new ROM parameter
ROMI packet
ACK
AP
STA
Accept
Change to new ROM parameter
Step 3-1)
Step 3-2)

## Slide 21: Conclusion
In this presentation, Procedures for ROM signaling failure have been proposed
  when the HE STA changes a parameter from lower to higher, it should make the change for that parameter right after the ACK timeout or receiving the ACK for the ROMI packet
  when the HE STA changes a parameter from higher to lower, it should make the change for that parameter only after receiving the ACK for the ROMI packet

## Slide 22: References
[1] https://mentor.ieee.org/802.11/dcn/15/11-15-0132-16-00ax-spec-framework.docx

## Slide 23: Straw Poll
Do you agree to add the following text to the 11ax Specification Frame work document clause 6.3 Power save?
  For each of the ROMI parameters Rx NSS and Rx BW, the following rules are used:
  when the HE STA changes a parameter from lower to higher, it should make the change for that parameter right after the ACK timeout or receiving the ACK for the ROMI packet.
  when the HE STA changes a parameter from higher to lower, it should make the change for that parameter only after receiving the ACK for the ROMI packet.