## Slide 1: BSS Color Collision
Date: 2016-05-16
Authors:

## Slide 2: Introduction
In the previous meeting, we have discussed some technical issues on BSS Color collision [1]:
  The case that neighboring BSSs use the same BSS Color value is referred as “BSS Color collision” in this contribution.
Current 11ax draft spec [2] contains potential problems caused by BSS Color collision.
  There were multiple comments which mentioned the problems [3]. For example, CID 62, 193, 205, 626, 632, 640, 2661, etc.
This contribution points out the potential technical issues on the operation of spatial reuse, NAV setting, and intra-PPDU power save when BSS Color collision occurs.

## Slide 3: Possibility of BSS Color Collision
According to 11ax D0.1 [2],
  BSS_COLOR in TXVECTOR and RXVECTOR is “set to a value of the AP’s choosing within the range 0 to TBD” (Table 26-1)
  The number of bits for BSS Color Field in HE-SIG-A is 6. (Table 26-15, 26-16, and 26-17)
If each AP chooses BSS Color randomly, there is a probability that neighboring BSSs use the same BSS Color.
Even if we define BSS Color selection procedure (e.g. OBSS scanning), AP may not avoid BSS Color collision because of
  Limited BSS Color space
  Mobile hotspots, etc.

## Slide 4: Determination Rule of an Intra-BSS Frame
Determination rule of an intra-BSS frame in 11ax D0.1 [2]
  “The detected frame is intra-BSS frame if one of the following conditions is true:
    The BSS color in the detected PPDU is same as the BSS color announced by its associated AP
    The RA or TA of the detected frame is same as the BSSID or its bandwidth signaling variant of its associated AP
    Its associated AP is identified by TBD Multiple BSSID element and the RA or TA of the detected frame is same as one of the BSSID or its bandwidth signaling variant defined by TBD Multiple BSSID element”

## Slide 5: False Classification due to BSS Color collision
Following the rule in the previous slide, an inter-BSS frame may be determined as an intra-BSS frame when BSS Color collision has happened.
  Problem 1: When a STA decodes the MAC header,
    BSS Color is same but MAC address does not correspond to the BSSID.
    The determination rule in the current draft spec does not specify the operation for BSS Color collision.
    Based on the first condition of the rule, the frame can be classified as an “intra-BSS” frame.
  Problem 2: When a STA does not decode the MAC header,
    BSS Color is same.  Classified as an “intra-BSS” frame
The following slides describe undesirable results when an inter-BSS frame is determined as an intra-BSS frame.

## Slide 6: Spatial Reuse in BSS Color Collision
A. Spatial reuse
  In 25.9.2 Color code based CCA rules of 11ax D0.1 [2],
    “If the detected frame is an inter-BSS frame, under TBD condition, uses TBD OBSS PD level that is greater than the minimum receives sensitivity level.”
  With BSS Color collision, since an inter-BSS frame is determined as an intra-BSS frame, the color code based CCA with OBSS PD level can be less utilized.

## Slide 7: NAV Setting in BSS Color Collision (1)
B. NAV setting: An intra-BSS frame may set the intra-BSS NAV of an inter-BSS STA.
  In 25.5.2.4 UL MU CS mechanism of 11ax D0.1 [2],
    When a Trigger frame polls a STA for UL MU transmission, the STA does not consider its NAV set by an intra-BSS frame.
Intra-BSS Frame*
STA1
Intra-BSS NAV
STA3
Trigger Frame
AP
Trigger-based UL Frame
Intra-BSS Frame
STA2
TXOP (Intra-BSS)
Intra-BSS
Inter-BSS
with
same BSS Color
Intra-BSS frame sets
Intra-BSS NAV of Inter-BSS STA.
Interference to Intra-BSS!
* The frame is HE SU UL PPDU, HE trigger-based PPDU, or HE MU PPDU which does not carry STAID that addresses the STA.

## Slide 8: NAV Setting in BSS Color Collision (2)
B. NAV setting: An intra-BSS frame may set the intra-BSS NAV of an inter-BSS STA.
  In 10.22.2.9 Truncation of TXOP of 11ax D0.1 [2],
    A STA that receives a CF-End frame should not reset its NAV, if
      The CF-End frame is not an intra-BSS frame and the most recent NAV was set by an intra-BSS frame.
      The CF-End frame is an intra-BSS frame and the most recent NAV was not set by an intra-BSS frame.
Intra-BSS Frame*
STA1
Intra-BSS NAV
STA3
CF-End
Frame
STA4
Intra-BSS Frame
STA2
TXOP (Intra-BSS)
Intra-BSS
Inter-BSS
with
same BSS Color
Does not set
regular NAV of Inter-BSS STA
 Undesirable operation
Desirable regular NAV, but not be set
Cancelled
Resets Intra-BSS NAV of STA3
STA may
transmit PPDU
Interference to Intra-BSS!
TXOP (Inter-BSS)
* The frame is HE SU UL PPDU, HE trigger-based PPDU, or HE MU PPDU which does not carry STAID that addresses the STA.

## Slide 9: Power Save in BSS Color Collision
C. Intra-PPDU power save: A STA may enter the doze state during an inter-BSS PPDU.
  In 25.13.1 Intra-PPDU power save for HE non-AP STAs of 11ax D0.1 [2],
    To enter the doze state, STA checks whether the value of the RXVECTOR parameter BSS_COLOR is equal to the BSS Color of the BSS with which the STA is associated.
Awake
Doze
Inter-BSS STA
with same BSS Color
Inter-BSS Frame*
STA
AP
DL Data to STA
A STA detects an Inter-BSS frame and may enter the doze state for the same BSS Color.
The STA cannot receive the frame intended to it during the doze state.
Intra-BSS
* The frame is HE SU UL PPDU, HE trigger-based PPDU, or HE MU PPDU which does not carry STAID that addresses the STA.

## Slide 10: Proposed Solutions
Undesirable operations due to BSS Color collision should be considered in the determination rule of an “Intra-BSS Frame”.
  If BSS Color is the same and MAC address does not correspond to the BSSID:
    When RA and TA fields of the detected frame are identified, the determination should be made based on MAC address, not based on BSS Color field of the detected frame.
  If BSS Color is the same but a STA does not decode the MAC header:
    We need further discussions for the operation in case that BSS Color collision has been detected [1].

## Slide 11: Conclusions
Based on the BSS Color Information, 11ax defines several operations in spatial reuse, NAV setting, and power save. However, there are some potential issues when BSS Color collision occurs.
Since BSS Color collision may happen, the specification should further consider the determination rule for an intra-BSS frame (at least) when a STA decodes the MAC header.

## Slide 12: References
[1] 11-16/0396r0 Issues on BSS Color Bits Collision
[2] Draft P802.11ax D0.1
[3] 11-16/0535r4 Comments on TGax D0.1

## Slide 13: Straw Poll
  Do you agree to add the following text into 11ax SFD ?
  5.1 When a STA that receives HE PPDU identifies both RA and TA fields, the STA shall determine whether the frame is an inter-BSS or an intra-BSS frame by using the address fields.
  Y 7
  N 3
  A 16

## Slide 14: Straw Poll
  Do you agree to add the following text into 11ax SFD ?
  5.1 When a STA, that receives an HE PPDU with the same BSS Color as the BSS Color announced by its associated AP, identifies from RA and TA fields that the frame is an inter-BSS frame, the STA shall treat the frame as an inter-BSS frame after the FCS has been verified.
  Y
  N
  A