## Slide 1: Further consideration on channel access rule to facilitate MU transmission opportunity
Date: 2016-05-18
Authors:

## Slide 2: Background
As specified in 11ax, MU operation is crucial to improve the channel efficiency and BSS throughput
And, HE MU operations have been specified in 11ax draft 0.1[1]
  AP initiates MU DL/UL transmission
    AP transmits simultaneously to one or more non-AP STAs using MU DL transmission.
    AP initiates trigger frame to solicit immediate simultaneous response frames using HE trigger-based PPDU format from one or more non-AP STAs in MU UL transmission.

## Slide 3: Issue
However, in dense deployed scenario, such as SS3 (1 AP/ 30~40 STAs per BSS), AP has to compete with a large number of STAs to access channel and actually gets less chance accessing the channel to initiate MU DL/UL transmission.
  (802.11 base line operation) An AP/STA shall invoke backoff procedure with the same backoff parameter values following an idle DIFS/EIFS period.

## Slide 4: Proposal
We propose increase AP’s probability to access channel
For example,
  Reducing CWmin and CWmax to provide AP with small initial CW backoff window.
  AP sets trigger frame to access category AC_VO to further facilitate UL MU transmission.
  AP may be allowed to use a set of EDCA parameter with values smaller than it advertises to the STAs in its BSS to increase AP’s transmission opportunity.

## Slide 5: SP
Do you agree to add to the following to 11ax TG SFD:
  Do you agree to allow the AP choose any access category for contending to send the trigger frame?
  The chosen AC may give to the AP higher priority in accessing the channel compared to its associated STAs

## Slide 6: References
11-16/0024r1, Draft Specifications, March 2016
IEEE std 802.11, “IEEE Standard Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications” , 2012