## Slide 1: Consideration on backoff procedure for UL MU transmission
Date: 2016-05-18
Authors:

## Slide 2: Background
A non-AP STA possibly commences UL transmission using UL SU MPDU or UL MU MPDU after performing Carrier Sensing (CS) in 11ax specification.
  The non-AP STA commences UL transmission using UL SU MPDU in case of the medium is determined to be idle for the duration of (DIFS/EIFS + backoff).
  The non-AP STA commences UL transmission using UL MU MPDU when the STA receives Trigger Frame (TF) while performing CS during the (DIFS/EIFS + backoff) period.

## Slide 3: Issue
Backoff procedure is defined in baseline 802.11 specification
  “ …. After the DIFS or EIFS medium idle time, the STA shall then generate a random backoff period for an additional deferred time before transmitting, unless the backoff timer already contains a non zero value, …”
In case of UL MU transmission (sub- bullet #2 in previous page)
  A STA potentially gets more chance accessing the channel and commences SU UL transmission since the STA will use the remaining backoff time according to the baseline behavior (which is nonzero due to the UL transmission is triggered) instead of generates new backoff period

## Slide 4: Proposal
We propose
  Option 1: A non-AP STA should reset its backoff timer after transmitting an UL PPDU as the response to trigger frame.
  Option 2: A non-AP STA keeps the backoff counter unchanged after transmitting an UL PPDU as the response to trigger frame.

## Slide 5: SP
Which option do you support
  Option 1: the non-STA resets its backoff counter after transmitting an UL PPDU as the response to trigger frame.
  Option 2: the non-STA keeps the backoff counter unchanged after transmitting an UL PPDU as the response to trigger frame.

## Slide 6: References
11-16/0024r1, Draft Specifications, March 2016
11-15/0132r15, Specification Framework for TGax, Jan 2016