## Slide 1: Considerations on Long Range
Date: 2016-05-16
Authors:
Name | Affiliation | Address | Email
Ke Yao | ZTE |  | yao.ke5@zte.com.cn
Xuelin Zhang | ZTE |  | Zhang.x_l@zte.com.cn
Bo Sun | ZTE |  | sun.bo1@zte.com.cn
Nan Li | ZTE |  | li.nan25@zte.com.cn
Weimin Xing | ZTE |  | Xing.weimin@zte.com.cn
Kaiying Lv | ZTE |  | lv.kaiying@zte.com.cn

## Slide 2: Abstract
  LRLP key differentiator, long range operation approach and approach of coexistence for long range are expected to be the main topics for this meeting.
  We proposed some considerations regarding long range, including link budget, challenge and coexistence.
  We also proposed use cases of tunnel and underground mine.

## Slide 3: Basic Link Budget Assumption and Analysis
Next slide shows the link budget result based on the following assumptions:
  Path Loss Model and shadow fading [1]
    Note that shadow fading for 11n channel B and channel D is included in Path Loss model, but there is no shadow fading factor in Path Loss model for Umi NLOS/LOS.
  Using the values of required SINR in [2], we got very similar range results in meters.
Narrow band (2 MHz) can bring 10 dB path loss margin compared with 20MHz, that means about double range of coverage in meters, or 2 more walls, or less than 1 floor.

## Slide 4: Basic Link Budget (1)
BW | 20M | 2M | 78.125k | 20M | 2M | 78.125k | 20M | 2M | 78.125k | 20M | 2M | 78.125k
Transmitter |  |  |  |  |  |  |  |  |  |  |  | 
(1) Tx power (dBm) | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20
Receiver |  |  |  |  |  |  |  |  |  |  |  | 
(2) Thermal noise density (dBm/Hz) | -174 | -174 | -174 | -174 | -174 | -174 | -174 | -174 | -174 | -174 | -174 | -174
(3) Receiver noise figure (dB) | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7
(4) Interference margin (dB) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
(5) Occupied channel bandwidth (Hz) | 20000000 | 2000000 | 78125 | 20000000 | 2000000 | 78125 | 20000000 | 2000000 | 78125 | 20000000 | 2000000 | 78125
(6) Effective noise power | -93.99 | -103.99 | -118.07 | -93.99 | -103.99 | -118.07 | -93.99 | -103.99 | -118.07 | -93.99 | -103.99 | -118.07
= (2) + (3) + (4) + 10 log ((5)) (dBm) |  |  |  |  |  |  |  |  |  |  |  | 
(7) Required SINR (dB ) ---- MCS0 (no repetition) | 12.5 | 12.5 | 12.5 | 9 | 9 | 9 | 6.75 | 6.75 | 6.75 | 2.75 | 2.75 | 2.75
(8) Receiver sensitivity = (6) + (7) (dBm) | -81.49 | -91.49 | -105.57 | -84.99 | -94.99 | -109.07 | -87.24 | -97.24 | -111.32 | -91.24 | -101.24 | -115.32
(9) Rx processing gain | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Link Budget (in dB and in meter) |  |  |  |  |  |  |  |  |  |  |  | 
(10) MCL = (1) -(8) + (9) (dB) | 101.49 | 111.49 | 125.57 | 104.99 | 114.99 | 129.07 | 107.24 | 117.24 | 131.32 | 111.24 | 121.24 | 135.32
(11) link margin (including SF) | 5 | 5 | 5 | 5 | 5 | 5 | 0 | 0 | 0 | 0 | 0 | 0
path loss = (10)-(11) (dB) | 96.49 | 106.49 | 120.57 | 99.99 | 109.99 | 124.07 | 107.24 | 117.24 | 131.32 | 111.24 | 121.24 | 135.32
channel type | Channel B (d_BP = 5m) |  |  | channel D (d_BP = 10m ) |  |  | UMi NLOS |  |  | UMi LOS |  | 
range (meter) | 81.84 | 158.01 | 399.05 | 137.94 | 266.33 | 672.63 | 108.22 | 202.68 | 490.37 | 490.22 | 871.75 | 1960.89

## Slide 5: Up-Link Budget Assumption and Analysis
In the next slide we made some changes compared with basic link budget:
  For uplink direction, assume Max TX power <=15dBm.
  Required SINR for MCS0: refer to11ax PHY abstraction doc[3] which is under AWGN, nearly ideal performance.
So we get the max ranges in meters in reality
  For 2MHz, the largest range is less than 800 meters which is in UMi LOS environment, and less than 400 meters otherwise.
    Can hardly support some outdoor use cases which require about 1km.
    Smaller BW might be needed to achieve larger coverage.
    Or some techniques to improve the required SINR
      Coding gain enhancement (repetition)
      Reducing interference
    Directional antenna and beamforming can benefit transmitting efficiency
    Multi-hopping could be an candidate but the complexity and the cost should be further evaluated.

## Slide 6: Link Budget (2)
BW | 20M | 2M | 78.125k | 20M | 2M | 78.125k | 20M | 2M | 78.125k | 20M | 2M | 78.125k
Transmitter |  |  |  |  |  |  |  |  |  |  |  | 
(1) Tx power (dBm) | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15
Receiver |  |  |  |  |  |  |  |  |  |  |  | 
(2) Thermal noise density (dBm/Hz) | -174 | -174 | -174 | -174 | -174 | -174 | -174 | -174 | -174 | -174 | -174 | -174
(3) Receiver noise figure (dB) | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7
(4) Interference margin (dB) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
(5) Occupied channel bandwidth (Hz) | 20000000 | 2000000 | 78125 | 20000000 | 2000000 | 78125 | 20000000 | 2000000 | 78125 | 20000000 | 2000000 | 78125
(6) Effective noise power | -93.99 | -103.99 | -118.07 | -93.99 | -103.99 | -118.07 | -93.99 | -103.99 | -118.07 | -93.99 | -103.99 | -118.07
= (2) + (3) + (4) + 10 log ((5)) (dBm) |  |  |  |  |  |  |  |  |  |  |  | 
(7) Required SINR (dB ) ---- MCS0 (no repetition) | -0.7 | -0.7 | -0.7 | -0.7 | -0.7 | -0.7 | -0.7 | -0.7 | -0.7 | -0.7 | -0.7 | -0.7
(8) Receiver sensitivity = (6) + (7) (dBm) | -94.69 | -104.69 | -118.77 | -94.69 | -104.69 | -118.77 | -94.69 | -104.69 | -118.77 | -94.69 | -104.69 | -118.77
(9) Rx processing gain | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Link Budget (in dB and in meter) |  |  |  |  |  |  |  |  |  |  |  | 
(10) MCL = (1) -(8) + (9) (dB) | 109.69 | 119.69 | 133.77 | 109.69 | 119.69 | 133.77 | 109.69 | 119.69 | 133.77 | 109.69 | 119.69 | 133.77
(11) link margin (including SF) | 5 | 5 | 5 | 5 | 5 | 5 | 0 | 0 | 0 | 0 | 0 | 0
path loss = (10)-(11) (dB) | 104.69 | 114.69 | 128.77 | 104.69 | 114.69 | 128.77 | 109.69 | 119.69 | 133.77 | 109.69 | 119.69 | 133.77
channel type | Channel B (d_BP = 5m) |  |  | channel D (d_BP = 10m ) |  |  | UMi NLOS |  |  | UMi LOS |  | 
range (meter) | 140.36 | 271.00 | 684.41 | 187.93 | 362.83 | 916.35 | 126.21 | 236.35 | 571.84 | 448.38 | 797.34 | 1793.50

## Slide 7: Challenge
PA for supporting additional LRLP
  An AP supporting 11ac should have PA with linear range from 20MHz to 80MHz which is mandatory and to 160MHz which is optional.
  If LRLP is added to such AP, the PA is expected to extend the linear range to smaller BW, 2MHz or even smaller.
  It could be a challenge for zero extra cost of AP.
  Same challenge for full function LRLP STA.

## Slide 8: Efficiency consideration
Efficiency in coexistence environment (LRLP & WLAN)
  With or without protection, longer range would cause worse system efficiency
    When RTS/CTS-like schemes are useded to protect NB system transmission, the WB system should be muted in corresponding periods, which would downgrade the overall system performance.
    Without any protection, the quality of NB transmissions couldn’t be guaranteed at all, which causes a low efficiency LRLP.
Long range
  In coexistence environment, LRLP should focus on mid Long-distance which means longer than the legacy WLAN distance but not expect to be very long, e.g. several kilometers (LoRa, SigFox)
  In stand-alone environment, it is possible to enlarge the distance to more than 1km.

## Slide 9: Competitiveness Analysis
Why can WLAN series products be flourishing?
  Low complexity and low cost !!
  Can deploy without infrastructure
Prospect of LRLP
  IoT is not a totally new field, there have been some potential rivals which have long range and/or low power properties.
    Long range (> 1km)
      Ultra NB: 100Hz ~ 200kHz (LoRa, SigFox),
      NB: 3.75kHz ~ 2MHz (3GPP: NB-CIoT, NB-LTE), etc.
    Mid Long range (< 1km)
      802.11ah (Halow),
      802.11ax (extended range PPDU format), etc..
  Face challenge from 3GPP techs which are higher efficient due to scheduling and has existing infrastructure
  Face challenge from other techs which are professional for long range or low power without considering coexistence issues.
  The prospect of LRLP lies in integration with legacy WiFi device, therefore LRLP can enter the mature market of current WiFi as an attachment with assumption that it can be realized with very low extra cost.

## Slide 10: Use case for tunnel and underground mine
Tunnel /mine monitoring and management
  Environment monitoring
    Air condition for fire alarm or toxic air density (e.g. density of CO)
    Temperature and Humidity
    Extreme weather
      Wind direction and strength,
      accumulated water level on road
    Visibility
    Pressure of tunnel/mine wall
    Devices working condition normal/abnormal states report (ventilator and all kinds of lights, etc.)
  Traffic monitoring and traffic (only for traffic tunnel)
    Traffic flow
    Vehicle velocity
    Lane occupancy
  Devices auto control
    According to the reported info, send message to control devices states like signal lights display, lights on/off, the power level of ventilator, etc.

## Slide 11: Use case – cont.
Property
  Large amount of uplink report data
  Small amount of downlink control data
Requirements
  Data transmission rate
    Low data throughput typical of applications in sensor, e.g., 100kbps
  Transmission range
    500m
  Battery Life
    >1 year

## Slide 12: Conclusion
Analyze the link budget to see the max distance in meters
Discuss the challenge for PA and the relation between efficiency and long distance.
  In coexistence environment, longer range downgrades system efficiency.
  Real long range may be considered in stand-alone environment.
Propose a use case for tunnel and underground mine.

## Slide 13: References
[1] IEEE 802.11-14/882r4, IEEE 802.11ax channel model document
[2] 11-15-1308-00-lrlp-link-budget-analysis.
[3] 11-14-1176-01-00ax-phy-abstraction-tables-for-11ax-system-level-simulation
[4] 11-15-1446-12-lrlp-lrlp-output-report-draft

## Slide 14: Appendix
Path loss model for channel B and D
Path loss model for UMi LOS
Path loss model for UMi NLOS