## Slide 1: Channel Access Efficiency
Date: 2016-05-16
Authors:
Name | Affiliation | Address | Phone | Email
Evgeny Khorov | IITP |  |  | khorov@frtk.ru
Anton Kiryanov | IITP |  |  | ant456@ya.ru
Sigurd Schelstraete | Quantenna |  |  | sigurd@quantenna.com
Huizhao Wang | Quantenna |  |  | hwang@quantenna.com

## Slide 2: Background
Trigger frames can schedule UL RUs for both deterministic and random channel access.
To send a Trigger frame, an AP shall contend for the channel with associated STAs and STAs from other BSSs. When the AP wins the contention, it allocates RUs for the STAs. However, when STAs use DCF (or EDCA), collision probability increases.
What is the most efficient way to allocate channel resource: DCF (EDCA) or Trigger-based?

## Slide 3: Scenario Description
We consider 4 channel access methods
DCF without RTS/CTS
DCF with RTS/CTS
Trigger-based Random Access without RTS/CTS
Trigger-based Deterministic Access without RTS/CTS
In 3 and 4, the STAs can also try to send frames with DCF
All nodes are
in the RX range of each other
No hidden STAs
AP
N STAs

## Slide 4: Trigger-based Random Access without RTS/CTS
………………………………………..
………………………………………..
………………………………………..
………………………………………..
20 MHz
Collisions and empty RU are possible!
20 MHz
20 MHz
20 MHz
Trigger for
Random Access
M-STA
BlockACK
Data
26
SIFS
SIFS
DIFS+
backoff
Trigger for
Random Access
26
26
26
26
26
26
26
26
26
26
26
26
26
26
26
Collision
Success
Empty

## Slide 5: Trigger-based Deterministic Access without RTS/CTS
………………………………………..
………………………………………..
20 MHz
No collisions,
no empty RUs!
20 MHz
20 MHz
20 MHz
Trigger
M-STA
BlockACK
Data
SIFS
SIFS
DIFS+
7 slots
Trigger
N=37 STAs
………………………………………..
………………………………………..
26
26
26
26
26
26
26
26
26
26
26
26
26
26
26
26

## Slide 6: Scenario Parameters
Parameter | Value
Channel width | 80 MHz
Control frame MCS | MCS0
Data frame MCS | MCS5 (272 Mbps @80 MHz)
MSDU size | 1500 byte
Data frame | 1 MSDU 24 MSDUs
Traffic mode | Saturated

## Slide 7: Results (24 MSDUs)
Chart: Throughput
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100
DCF | 224.737 | 217.6683 | 209.9305 | 203.5224 | 198.3243 | 194.0419 | 190.4356 | 187.3383 | 184.6277 | 182.2153 | 180.0463 | 178.0776 | 176.2632 | 174.6027 | 173.0415 | 171.5877
DCF with RTS/CTS | 199.7921 | 202.7181 | 203.0972 | 202.96 | 202.6886 | 202.3877 | 202.0899 | 201.8053 | 201.5362 | 201.2816 | 201.0411 | 200.8134 | 200.5958 | 200.3902 | 200.1913 | 200.0012
Trigger Deterministic | 216.0922 | 231.1149 | 249.5379
Trigger Deterministic + DCF | 225.815 | 226.6552 | 222.7826
Trigger Deterministic + DCF with RTS/CTS | 204.1602 | 219.1509 | 226.4097
Trigger RA | 216.0922 | 115.5574 | 105.2738
Trigger RA + DCF | 225.815 | 169.9914 | 158.3845
Trigger RA + DCF RTS/CTS | 204.1602 | 164.3632 | 160.9632
Trigger RA #RU=4 | 54.023 | 93.5767 | 110.9057 | 105.2738 | 102.2107 | 100.2837 | 98.9591 | 97.9925 | 97.256 | 96.6761 | 96.2076 | 95.8213 | 95.4973 | 95.2216 | 94.9842 | 94.7776
* For Trigger Based Deterministic Access the throughput depends on the # RUs.
For long frames, Trigger-based Random access provides low performance,
while Trigger-based Deterministic access gives the highest throughput
#RUs = N *
#RUs = N = OCW
RU ~4.5ms

## Slide 8: Results (1 MSDU)
For short frames, DCF provides the lowest performance because of relatively long headers, etc.
Trigger-based Deterministic access shows the best performance.
Trigger based Deterministic Access suffers from STAs which use DCF
Chart: Throughput
Trigger Deterministic | 37.7289 | 65.0072 | 129.5966 | 147.8799 | 175.3134 | 204.5265
Trigger Deterministic + DCF | 46.7625 | 65.34 | 76.3467 | 82.5013 | 80.6142 | 72.9641
Trigger Deterministic + DCF with RTS/CTS | 30.6207 | 44.1206 | 52.2082 | 58.1678 | 58.3297 | 54.0255
Trigger RA | 37.7289 | 32.5036 | 54.6736 | 76.2742
Trigger RA + DCF | 46.7625 | 49.005 | 54.2777 | 50.0873
Trigger RA + DCF RTS/CTS | 30.6207 | 33.0904 | 37.1167 | 37.0866
RU ~2ms

## Slide 9: Remarks
Since the cumulative UL throughput degrades when STAs use DCF in addition to transmission in allocated RUs, it makes sense to improve efficiency of the channel access by using deterministic Trigger-based channel access instead of random access (DCF and/or Trigger-based Random Access).
This restriction should be applied for any frame transmission except for TBD cases (e.g. sending Buffer Status Report, delay sensitive frames, VO frames, management frames, etc).
Obviously, the AP should allocate some amount of channel time to the STAs which are limited in use of DCF and Trigger-based RA.

## Slide 10: Signaling Channel Access Method
802.11 defines Action frame formats for wireless network management (WNM)
  See 8.5.14 in 802.11-2012 or 8.6.14 in P802.11-REVmc/D5.3
  WNM Action frame serves a variety of Wireless Network Management purposes
  WNM Action field values 28-255 currently unused
Details:
  Category = WNM
  WNM Action = newly defined WNM Action field value
  Random Access Limits = TBD bitmap describing when random access is limited
Category
Random Access Limits
WNM Action

## Slide 11: Straw Poll #1
Do you agree to add the following text in SFD:
x.y.z Do you support adding a mechanism that allows the AP to individually configure associated STAs not to use random access (DCF, EDCA and Trigger-based RA) for the frames except for TBD cases?
  Y
  N
  A